## Slide 1: On operation beyond 10-bit
JVET-S0243
Advanced Technology Team
European Professional Engineering
Sony Europe BV
Adrian Browne
Sony Corp.

## Slide 2: Is a 12-bit profile practical?
If 12-bit profiles have a bit rate 20% higher than equivalent 10-bit profile:
  150Mbps for Main 12 4:4:4 60P (Level 4.1 high tier) (CrowdRun 60P RGB 444)
  90Mbps for Main 12 4:4:4 30P (Level 4.0, high tier) (Balloon 30P YUV 444 PQ)
Should achieve higher PSNR than 10-bit allows
Therefore 12-bit processing should approach or exceed 60dB
MSE | Bit depth |  | 
 | 8 | 10 | 12
1 | 48.1 | 60.2 | 72.2
2 | 45.1 | 57.2 | 69.2
4 | 42.1 | 54.2 | 66.2
8 | 39.1 | 51.2 | 63.2

## Slide 3: Is a 12-bit profile practical?
RGB 444 test sequences hard to compress
  At 150Mbps, less than 40dB implies no need for 12-bit processing
  Much higher bitrate required to justify 12-bit
VTM does outperform HM

## Slide 4: Is a 12-bit profile practical?
YUV 444 HDR test sequences seem easier to compress
  At 90Mbps, in excess of 55dB (RA)
  LSBs in decoded stream likely to preserve structure in 12-bit source
VTM outperforms HM over this range of PSNR

## Slide 5: Is a 12-bit profile practical?
Yes
  At least for some content
  As long as VVC performance outweighs complexity vs HEVC
Other applications:
  12-bit still picture profile
  12-bit lossless
Next steps?
  Identify suitable test sequences and establish CTC
  Identify which existing tools work well at higher PSNR

## Slide 6: Beyond 12-bit
As QPs become more negative:
  VTM bitrates start significantly exceeding those of HM
    Also affects 12-bit processing for RGB 444 content (outside suggested profile)
Bitrate increase identified as due to Golomb-Rice coding of coefficients

## Slide 7: Beyond 12-bit
VVC version 1 has very restricted Rice parameter range (0->3)
HEVC allows Rice parameter to increase as coefficient size increases
  Tried HEVC-based technique in VTM
Experiments are described in more detail in the contribution document

## Slide 8: Beyond 12-bit
Modified VTM and HM bitrates are similar for highest PSNRs
Gains can be made at intermediate PSNRs
  Where VTM performance currently starts weakening
Experiments are described in more detail in the contribution document

## Slide 9: Beyond 12-bit
Question:
  How can VVC/VTM be modified so that its complexity/coding trade off is seen to give an advantage of HEVC/HM?
    VTM requires fix to Golomb-Rice coding to outperform HM for high PSNR
    HM and patched VTM have very similar performance
    VTM encoder 20-25 times slower than HM
Possible solutions:
  Some tools show reduced/zero gain as QP decreases – could be excluded
  Others may need modification
Tool | Combined YUV gain at QP range |  |  | 
 | 22 → 37 | 2 → 17 | -18 → -3 | -38 → -23
SBT | 0.49% | 0.14% | 0.00% | 0.00%
GPM | 0.26% | 0.01% | 0.02% | 0.02%
JCCR | 0.16% | 0.60% | 0.00% | 0.00%
ALF+CCALF | 3.00% | 1.06% | 0.06% | 0.00%
Example of declining gains from tools as QPs decrease (CrowdRun + Balloon)

## Slide 10: Conclusions
A 12-bit profile seems reasonable for v2
  VTM offers gains over HM
  At least some 12-bit content will be within bit rate limit
A 12-bit still picture is another use case
Above 12 bit is a more difficult argument
  VTM in present form underperforms due to Golomb-Rice coding issues
  VTM/VVC needs to show real bitrate savings over HM/HEVC
For both 12-bit and above 12-bit it would be helpful to consider test conditions
Document describes methods to modify Golomb-Rice coding
  Improvements over HM at all operating points
    12-bit and above 12-bit