## Slide 1: Cross-RAP referencing
Slides for JVET-U0084

## Slide 2: The concept (1/3)
The application (e.g., adaptive streaming) determines the frequency of random access points (RAPs), e.g., RAP period 1s or 2s.
Conventionally RAPs are provided by coding of IRAP pictures.
  When random accessing from CRA6, the decoder receives and correctly decodes the following pictures:
CRA6
CRA7
CRA8
CRA9
…
IDR0
CRA3
CRA1
CRA2
CRA4
CRA5
CRA6
CRA7
CRA8
CRA9
…
Note that inter prediction references for the non-key pictures between RAP pictures are not shown, and from left to right is the output order.

## Slide 3: The concept (2/3)
The DRAP approach provides improved coding efficiency by allowing a DRAP picture (and subsequent pictures) to refer to the previous IRAP picture for inter prediction.
  When random accessing from DRAP6, the decoder receives and correctly decodes the following pictures:
IDR0
DRAP3
DRAP1
DRAP2
DRAP4
DRAP5
DRAP6
DRAP7
DRAP8
DRAP9
…
IDR0
DRAP6
DRAP7
DRAP8
DRAP9
…
Note that inter prediction for the non-key pictures between RAP pictures are not shown, and from left to right is the output order.

## Slide 4: The concept (3/3)
The CRR approach provides a bit more flexibility by allowing a CRR picture (and subsequent pictures) to refer to a few of the earlier RAP pictures (IRAP or CRR), e.g., as follows:
  When random accessing from CRR6, the decoder receives and correctly decodes the following pictures:
IDR0
CRR1
CRR2
CRR3
CRR4
CRR5
CRR6
CRR7
CRR8
CRR9
…
IDR0
CRR2
CRR6
CRR7
CRR8
CRR9
…
Note that inter prediction for the non-key pictures between RAP pictures are not shown, and from left to right is the output order.

## Slide 5: CRR in systems
Main stream track or representation
External stream track or representation
When random accessing from or switching to the segment starting at CRR6, the decoder receives and decodes the following segments:
none
…
IDR0
IDR0 & CRR2
IDR0 & CRR2
IDR0 & CRR2
IDR0 & CRR2
IDR0 & CRR2
IDR0 & CRR2
IDR0 & CRR2
IDR0
IDR0
CRR1
CRR2
CRR3
CRR4
CRR5
CRR6
CRR7
CRR8
CRR9
…
Main stream track or representation
External stream track or representation
IDR0 & CRR2
CRR6
CRR7
CRR8
CRR9
…