## Slide 1
AHG8: Encoder improvements to palette coding for high bit depth (JVET-V0066)
T. Tsukuba, M. Ikeda, T. Suzuki

## Slide 2: Summary
Issues on palette coding at high bit depth
  #1: Memory usage for bit calculation using pre-defined LUTs becomes quite high at high bit depth.
    Up to 8.6GB in 16-bit case.
  #2: Coding performance drops at high bit depth due to the unadjusted QP for the threshold “errorLimit”
Proposal
  #1: Use bit calculation functions on the fly instead of pre-defined LUTs (for issue#1)
    No impact on coding performance, but can save the max memory size by roughly 8 GB for 16-bit case
  #2: Adjust QP based on internal bit depth for retrieving the errorLimit from LUTs (for issue#2)
    BD-rate gain: ~8.5% for AI, ~6.0% for RA at normal QPs
 |  | Over VTM-12.0 IBD=12 at normal QPs (QP=22,27,32,37) |  |  |  |  |  |  |  |  | 
 |  | YUV 4:4:4 |  |  |  |  | RGB 4:4:4 |  |  |  | 
 |  | Y | U | V | EncT | DecT | G | B | R | EncT | DecT
Proposal#1 | AI | 0.00% | 0.00% | 0.00% | 101% | 100% | 0.00% | 0.00% | 0.00% | 99% | 100%
 | RA | 0.00% | 0.00% | 0.00% | 100% | 100% | 0.00% | 0.00% | 0.00% | 100% | 100%
Proposal#2 | AI | -8.70% | -10.86% | -11.66% | 101% | 95% | -8.51% | -8.65% | -8.32% | 100% | 95%
 | RA | -6.09% | -8.43% | -9.16% | 98% | 99% | -5.64% | -5.86% | -5.73% | 99% | 99%

## Slide 3: Issue#1: Memory usage at encoder side
Following LUTs are used to estimate bit amounts for palette coding.
  m_truncBinBits[][] : 16-bit (1<<BitDepth)x(1<<BitDepth) array
  m_escapeNumBins[]: 16-bit 1x(1<<BitDepth) array
The array sizes depend on the BitDepth, which incurs huge memory consumption at high bit depth.
  16-bit case: ~8.6 GB (= 2bytes * ( (1<<16)**2 + (1<<16)) / 10**6)
Measured max memory size (RSS; resident set size) for IBD=16 reaches up to 14 GB for AI.
Chart: Maximum Resident set size [GB]
| RGB_ArenaOfValor | RGB_GlassHalf | RGB_Robot | YUV_ArenaOfValor | YUV_GlassHalf | YUV_Robot | RGB_BasketballScreen | RGB_MissionControlClip2 | RGB_MissionControlClip3 | YUV_BasketballScreen | YUV_MissionControlClip2 | YUV_MissionControlClip3 | RGB_ChineseEditing | RGB_Console | RGB_Desktop | RGB_FlyingGraphics | YUV_ChineseEditing | YUV_Console | YUV_Desktop | YUV_FlyingGraphics | RGB_Map | RGB_Programming | RGB_SlideShow | RGB_WebBrowsing | YUV_Map | YUV_Programming | YUV_SlideShow | YUV_WebBrowsing | ClassSC_A | ClassSC_M | ClassSC_TGM1 | ClassSC_TGM2
IBD=12 | 4094460 | 5255176 | 2771204 | 2834872 | 4157832 | 2685260 | 4377564 | 3739584 | 3955120 | 4168908 | 3222972 | 2890636 | 2561424 | 4021632 | 4002856 | 2928452 | 1982420 | 3970804 | 3001432 | 3494800 | 3642612 | 2360780 | 3126180 | 3082540 | 2945540 | 1968516 | 2421396 | 2729216
IBD=14 | 4657004 | 5801268 | 4316672 | 2695224 | 5589988 | 3150020 | 4839924 | 4910972 | 4400140 | 4430884 | 4496912 | 3906080 | 4589696 | 4568848 | 4541900 | 4559192 | 3579308 | 3881600 | 4395548 | 4044712 | 4337372 | 3512940 | 4284748 | 4265264 | 3420148 | 4181876 | 3121052 | 3233952
IBD=16 | 12918952 | 14382492 | 12504996 | 11549112 | 14392620 | 11454252 | 13242972 | 13317008 | 12841876 | 12528660 | 13205656 | 11450536 | 12843260 | 12690772 | 12741264 | 12753540 | 12291296 | 10089160 | 9525396 | 9555416 | 12516248 | 12428984 | 12433048 | 12472400 | 11301064 | 11487876 | 10807700 | 9909752
Max memory size per sequence for AI among QP=22,27,32,37 with frameNum=16, measured by using “time” command

## Slide 4: Proposal#1
To save memory size at high bit depth, it is proposed to use bit calculation functions, which are already implemented in VTM.
  getTruncBinBits: on the fly instead of the LUT m_truncBinBits[][]
  getEpExGolombNumBins: on the fly instead of the LUT m_escapeNumBins[]
Apply this fix only when the macro for high bit depth coding is enabled, i.e., JVET_R0351_HIGH_BIT_DEPTH_ENABLED is set to 1.
Can save memory usage by roughly 8 GB for 16-bit case.

## Slide 5: Issue#2: Coding Performance of Palette coding at high bit depth
Compared to 10-bit results, coding performance of 12-bit drops by roughly 12% for AI and 9% for RA.
The root cause is due to the unadjusted QP used for retrieving the threshold “errorLimit” from LUTs.
Tool-off tests on palette coding at normal QPs (QP=22,27,32,37) using Non-420 SCC sequence in JVET-T2013
 |  | YUV 4:4:4 |  |  |  |  | RGB 4:4:4 |  |  |  | 
 |  | Y | U | V | EncT | DecT | G | B | R | EncT | DecT
IBD=10 | AI | 13.58% | 16.71% | 18.20% | 98% | 108% | 15.43% | 15.39% | 14.67% | 98% | 109%
 | RA | 9.71% | 13.12% | 14.73% | 100% | 101% | 11.11% | 11.29% | 10.85% | 100% | 101%
IBD=12 | AI | 1.91% | 2.13% | 2.29% | 99% | 101% | 3.25% | 3.24% | 3.12% | 98% | 102%
 | RA | 1.49% | 1.75% | 1.95% | 98% | 101% | 2.85% | 2.86% | 2.71% | 99% | 101%

## Slide 6: Issue#2: Coding Performance of Palette coding at high bit depth
At encoder, a threshold “errorLimit” is used to associate each sample with one of palette table entries based on 8-bit domain SAD for lossy coding.
To retrieve “errorLimit” from LUT, QP needs to be adjusted to 8-bit domain QP by an offset based on BitDepth.
However, in VTM, the offset always takes a fixed value “-12” and fails to obtain appropriate “errorLimit” for high bit depth.
// at IntraSearch.cpp
void IntraSearch::derivePLTLossy(CodingStructure& cs, …)
{
…
TransformUnit &tu = *cs.getTU(partitioner.chType);
QpParam cQP(tu, compBegin);
int qp = cQP.Qp(true) - 12;
qp = (qp < 0) ? 0 : ((qp > 56) ? 56 : qp);
int errorLimit = g_paletteQuant[qp];
…
}

## Slide 7: Proposal#2
To retrieve appropriate errorLimit, it is proposed to adjust QP based on BitDepth, i.e., considering BdOffset:
// at IntraSearch.cpp
void IntraSearch::derivePLTLossy(CodingStructure& cs, …)
{
… TransformUnit &tu = *cs.getTU(partitioner.chType);
QpParam cQP(tu, compBegin);
int qp = cQP.Qp(true) - 12;
int qp = cQP.Qp(true) – 6 *(bitDepth – 8);
qp = (qp < 0) ? 0 : ((qp > 56) ? 56 : qp);
int errorLimit = g_paletteQuant[qp];
…
}

## Slide 8: Simulation
Following tests were conducted for AI and RA under non-420 common test condition (JVET-T2013) with InternalBitDepth set to 12:
  Test#1: VTM-12.0 vs VTM-12.0 with memory reduction (Proposal#1)
    Normal QP (QP=22, 27, 32, 37)
  Test#2: VTM-12.0 vs Proposal#1 + adjust QP based on BitDepth for errorLimit (proposal#2)
    Normal QP (QP=22, 27, 32, 37)
    Low QP (QP=-13, -8, -3, 2, 7, 12)
      hbd.cfg is additionally applied
      The number of frames is 100 for AI and 97 for RA
      Gop size is set to 32 for RA

## Slide 9: Test#1: VTM-12.0 vs VTM-12.0 + Memory size reduction (Proposal#1)
No impact to coding performance with negligible runtime changes
Saving max memory size by 8 GB for 16-bit case
Chart: Maximum resident set size [GB]
| RGB_ArenaOfValor | RGB_GlassHalf | RGB_Robot | YUV444_ArenaOfValor | YUV444_Robot | YUV444_GlassHalf | RGB_BasketballScreen | RGB_MissionControlClip2 | RGB_MissionControlClip3 | YUV444_BasketballScreen | YUV444_MissionControlClip2 | YUV444_MissionControlClip3 | RGB_ChineseEditing | RGB_Console | RGB_Desktop | RGB_FlyingGraphics | YUV444_FlyingGraphics | YUV444_Desktop | YUV444_Console | YUV444_ChineseEditing | RGB_Map | RGB_Programming | RGB_SlideShow | RGB_WebBrowsing | YUV444_WebBrowsing | YUV444_Map | YUV444_Programming | YUV444_SlideShow | ClassSC_A | ClassSC_M | ClassSC_TGM1 | ClassSC_TGM2
IBD=12 | 2550136 | 5044556 | 3122860 | 3646540 | 3745212 | 3271440 | 4127680 | 3189140 | 2884300 | 4231952 | 4410700 | 3441348 | 2302268 | 2859680 | 2824880 | 3967516 | 3070420 | 2567152 | 3948044 | 1572956 | 3784276 | 2641636 | 3472844 | 3684432 | 3219128 | 3744932 | 3708628 | 3283900
IBD=14 | 4108320 | 4885012 | 2758096 | 4131112 | 3216336 | 5130920 | 3809708 | 4340700 | 3570536 | 3822476 | 4463632 | 3948064 | 3606896 | 3978268 | 3808800 | 3936236 | 2602312 | 3383240 | 3777832 | 4040820 | 3820196 | 3764516 | 3761348 | 3736156 | 3261680 | 3308112 | 2724908 | 3580080
IBD=16 | 4169468 | 5621360 | 3837820 | 4159716 | 3806332 | 5149396 | 4535716 | 4483532 | 4146844 | 3977484 | 4382292 | 3548820 | 4110796 | 4041212 | 4084972 | 4084972 | 4039124 | 3846728 | 3589724 | 3924620 | 3894384 | 3764872 | 3777540 | 3776656 | 3690668 | 3365012 | 3758392 | 3648124
Max memory size per sequence for AI among QP=22,27,32,37 with frameNum=16, measured by using “time” command
 | All Intra |  |  |  |  |  |  |  |  | 
 | YUV 4:4:4 |  |  |  |  | RGB 4:4:4 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
TGM 1080p | 0.00% | 0.00% | 0.00% | 101% | 99% | 0.00% | 0.00% | 0.00% | 99% | 100%
TGM 720p | 0.00% | 0.00% | 0.00% | 101% | 100% | 0.00% | 0.00% | 0.00% | 99% | 100%
Animation | 0.00% | 0.00% | 0.00% | 100% | 100% | 0.00% | 0.00% | 0.00% | 97% | 101%
Mixed content | 0.00% | 0.00% | 0.00% | 101% | 101% | 0.00% | 0.00% | 0.00% | 100% | 100%
Overall | 0.00% | 0.00% | 0.00% | 101% | 100% | 0.00% | 0.00% | 0.00% | 99% | 100%
 | Random access |  |  |  |  |  |  |  |  | 
 | YUV 4:4:4 |  |  |  |  | RGB 4:4:4 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
TGM 1080p | 0.00% | 0.00% | 0.00% | 101% | 100% | 0.00% | 0.00% | 0.00% | 101% | 100%
TGM 720p | 0.00% | 0.00% | 0.00% | 100% | 100% | 0.00% | 0.00% | 0.00% | 100% | 100%
Animation | 0.00% | 0.00% | 0.00% | 99% | 100% | 0.00% | 0.00% | 0.00% | 100% | 100%
Mixed content | 0.00% | 0.00% | 0.00% | 98% | 100% | 0.00% | 0.00% | 0.00% | 100% | 100%
Overall | 0.00% | 0.00% | 0.00% | 100% | 100% | 0.00% | 0.00% | 0.00% | 100% | 100%
Normal QPs (QP=22,27,32,37)

## Slide 10: Test#2: VTM-12.0 vs Proposal#1 + adjust QP based on BitDepth for errorLimit (Proposal#2)
BD-rate reduction
  ~8.50% for AI and ~ 5.6% for RA at normal QPs
  ~1.8% for AI and ~1.2% for RA at low QPs
 | All Intra |  |  |  |  |  |  |  |  | 
 | YUV 4:4:4 |  |  |  |  | RGB 4:4:4 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
TGM 1080p | -16.37% | -18.13% | -17.86% | 102% | 89% | -12.64% | -12.80% | -12.47% | 103% | 91%
TGM 720p | -8.90% | -10.50% | -12.64% | 101% | 95% | -10.96% | -10.82% | -10.48% | 100% | 95%
Animation | -2.27% | -4.13% | -4.50% | 100% | 99% | -4.95% | -4.97% | -4.57% | 97% | 98%
Mixed content | -4.63% | -8.39% | -9.26% | 100% | 97% | -3.28% | -3.90% | -3.68% | 100% | 98%
Overall | -8.70% | -10.86% | -11.66% | 101% | 95% | -8.51% | -8.65% | -8.32% | 100% | 95%
 | Random access |  |  |  |  |  |  |  |  | 
 | YUV 4:4:4 |  |  |  |  | RGB 4:4:4 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
TGM 1080p | -10.63% | -12.93% | -12.61% | 97% | 97% | -7.62% | -8.06% | -7.86% | 99% | 98%
TGM 720p | -8.26% | -10.66% | -13.06% | 98% | 100% | -8.84% | -9.13% | -9.15% | 99% | 99%
Animation | -0.29% | -1.48% | -1.66% | 98% | 100% | -3.05% | -2.60% | -2.40% | 99% | 99%
Mixed content | -2.96% | -6.42% | -6.83% | 98% | 99% | -1.34% | -1.85% | -1.65% | 101% | 100%
Overall | -6.09% | -8.43% | -9.16% | 98% | 99% | -5.64% | -5.86% | -5.73% | 99% | 99%
 | All Intra |  |  |  |  |  |  |  |  | 
 | YUV 4:4:4 |  |  |  |  | RGB 4:4:4 |  |  |  | 
 | Y | U | V | EncT | DecT | G | B | R | EncT | DecT
TGM 1080p | -2.72% | -2.87% | -2.87% | 98% | 97% | -1.87% | -1.94% | -1.92% | 101% | 97%
TGM 720p | -2.61% | -2.25% | -2.49% | 100% | 96% | -4.73% | -4.85% | -4.90% | 97% | 94%
Animation | -1.34% | -2.69% | -2.55% | 95% | 97% | -0.29% | -0.33% | -0.36% | 103% | 99%
Mixed content | -0.55% | -0.51% | -0.45% | 97% | 99% | -0.60% | -0.60% | -0.65% | 101% | 99%
Overall | -1.80% | -2.08% | -2.09% | 97% | 97% | -1.87% | -1.93% | -1.96% | 100% | 98%
 | Random access |  |  |  |  |  |  |  |  | 
 | YUV 4:4:4 |  |  |  |  | RGB 4:4:4 |  |  |  | 
 | Y | U | V | EncT | DecT | G | B | R | EncT | DecT
TGM 1080p | -2.34% | -2.48% | -2.47% | 98% | 99% | -1.51% | -1.52% | -1.52% | 98% | 99%
TGM 720p | -1.44% | -0.71% | -1.04% | 98% | 99% | -2.69% | -3.32% | -3.01% | 99% | 99%
Animation | -1.44% | -1.81% | -1.66% | 100% | 99% | -0.29% | -0.30% | -0.31% | 101% | 99%
Mixed content | -0.15% | -0.08% | -0.07% | 100% | 100% | -0.28% | -0.19% | -0.25% | 100% | 100%
Overall | -1.34% | -1.27% | -1.31% | 99% | 99% | -1.19% | -1.33% | -1.27% | 100% | 99%
Normal QPs (QP=22,27,32,37)
Low QPs (QP=-13,-8,-3,2,7,12)

## Slide 11: Conclusion
Proposal#1: use bit calculation functions on the fly instead of LUTs (for issue#1)
  No impact to coding performance, saving memory usage up to 8 GB for 16-bit case
Proposal#2: adjust QP based on internal bit depth used for errorLimit (for issue#2)
  BD-rate gain: ~8.5% for AI and ~6.0% for RA at normal QPs, ~1.8% for AI and ~1.2% for RA at low QPs
Recommend to adopt to the next VTM
Thanks to Kwai for cross-check
 |  | Over VTM-12.0 IBD=12 at normal QPs (QP=22,27,32,37) |  |  |  |  |  |  |  |  | 
 |  | YUV 4:4:4 |  |  |  |  | RGB 4:4:4 |  |  |  | 
 |  | Y | U | V | EncT | DecT | G | B | R | EncT | DecT
Proposal#1 | AI | 0.00% | 0.00% | 0.00% | 101% | 100% | 0.00% | 0.00% | 0.00% | 99% | 100%
 | RA | 0.00% | 0.00% | 0.00% | 100% | 100% | 0.00% | 0.00% | 0.00% | 100% | 100%
Proposal#2 | AI | -8.70% | -10.86% | -11.66% | 101% | 95% | -8.51% | -8.65% | -8.32% | 100% | 95%
 | RA | -6.09% | -8.43% | -9.16% | 98% | 99% | -5.64% | -5.86% | -5.73% | 99% | 99%
 |  | Over VTM-12.0 IBD=12 at low QPs (QP=-13,-8,-3,2,7,12) |  |  |  |  |  |  |  |  | 
 |  | YUV 4:4:4 |  |  |  |  | RGB 4:4:4 |  |  |  | 
 |  | Y | U | V | EncT | DecT | G | B | R | EncT | DecT
Proposal#2 | AI | -1.80% | -2.08% | -2.09% | 97% | 97% | -1.87% | -1.93% | -1.96% | 100% | 98%
 | RA | -1.34% | -1.27% | -1.31% | 99% | 99% | -1.19% | -1.33% | -1.27% | 100% | 99%

## Slide 13: Tool-off tests on Palette coding at normal QPs (QP=22,27,32,37)
Compared to 10-bit case, BD-rate reduction is degraded by:
  12% for AI
  9% for RA
 | All Intra |  |  |  |  |  |  |  |  | 
 | YUV 4:4:4 |  |  |  |  | RGB 4:4:4 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
TGM 1080p | 28.52% | 31.87% | 31.75% | 102% | 119% | 27.55% | 27.74% | 26.51% | 100% | 120%
TGM 720p | 12.49% | 14.15% | 18.05% | 98% | 105% | 17.75% | 16.85% | 16.36% | 97% | 107%
Animation | 2.89% | 5.94% | 6.63% | 97% | 101% | 6.64% | 6.66% | 6.02% | 99% | 103%
Mixed content | 5.81% | 10.69% | 11.92% | 97% | 103% | 4.97% | 5.71% | 5.29% | 97% | 105%
Overall | 13.58% | 16.71% | 18.20% | 98% | 108% | 15.43% | 15.39% | 14.67% | 98% | 109%
 | Random access |  |  |  |  |  |  |  |  | 
 | YUV 4:4:4 |  |  |  |  | RGB 4:4:4 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
TGM 1080p | 18.68% | 22.91% | 22.53% | 103% | 103% | 18.34% | 19.23% | 18.43% | 103% | 102%
TGM 720p | 12.33% | 14.93% | 20.09% | 100% | 100% | 16.09% | 15.66% | 15.63% | 100% | 100%
Animation | 0.35% | 1.81% | 2.51% | 98% | 100% | 3.68% | 3.13% | 2.73% | 100% | 101%
Mixed content | 3.62% | 8.95% | 9.41% | 97% | 100% | 2.28% | 3.04% | 2.47% | 96% | 100%
Overall | 9.71% | 13.12% | 14.73% | 100% | 101% | 11.11% | 11.29% | 10.85% | 100% | 101%
 | All Intra |  |  |  |  |  |  |  |  | 
 | YUV 4:4:4 |  |  |  |  | RGB 4:4:4 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
TGM 1080p | 5.30% | 5.89% | 5.95% | 103% | 104% | 8.11% | 8.48% | 8.02% | 101% | 106%
TGM 720p | 0.95% | 0.87% | 1.15% | 101% | 100% | 2.30% | 1.90% | 2.03% | 96% | 102%
Animation | 0.17% | 0.36% | 0.52% | 95% | 100% | 0.49% | 0.46% | 0.44% | 95% | 100%
Mixed content | 0.42% | 0.55% | 0.70% | 95% | 101% | 0.78% | 0.82% | 0.71% | 98% | 101%
Overall | 1.91% | 2.13% | 2.29% | 99% | 101% | 3.25% | 3.24% | 3.12% | 98% | 102%
 | Random access |  |  |  |  |  |  |  |  | 
 | YUV 4:4:4 |  |  |  |  | RGB 4:4:4 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
TGM 1080p | 4.02% | 4.61% | 4.55% | 100% | 104% | 6.85% | 7.08% | 6.77% | 102% | 104%
TGM 720p | 1.06% | 0.92% | 1.51% | 97% | 101% | 2.61% | 2.37% | 2.42% | 99% | 102%
Animation | -0.13% | -0.04% | 0.21% | 96% | 100% | 0.21% | 0.21% | 0.10% | 98% | 100%
Mixed content | 0.29% | 0.84% | 0.82% | 96% | 98% | 0.49% | 0.57% | 0.28% | 97% | 99%
Overall | 1.49% | 1.75% | 1.95% | 98% | 101% | 2.85% | 2.86% | 2.71% | 99% | 101%
IBD=10
IBD=12