## Slide 1
JVET-V0068
A constraint of max CTU size for high bit depth and high bit rate coding
Kenji Kondo, Masaru Ikeda (Sony)

## Slide 2: Outline
Introduce an issue
  When WPP is used, a large CTU may decrease a CABAC throughput.
Proposed solution
  For high bit rate coding, restrict max CTU size to 64.
Experiment
  CTU size: 64
Conclusion
  No impact BD-rate for low QP
  Propose the constraint

## Slide 3: The issue of parallel parsing with WPP
For VVC, max CTU size was extended from HEVC.
One entropy slice becomes bigger because of large CTU size.
  It’s illustrated below.
The time for parsing becomes longer.
  It would make a real time playback difficult.
CTU rows
…
Many bits may be concentrated into a specific CTU row.
…
CTU size: 64
CTU size: 128

## Slide 4: Proposed solution
Propose a constraint
  Give a constraint to max CTU size 64, the same as HEVC.
  For high bit rate (low QP range), it’s expected that large CTU is not so efficient.
Experiment
  Anchor
    CTC for HBD and high bit rate coding
  Test
    CTU size : 64
Cross check
  JVET-V0160
  Thank Sharp for the cross checking.

## Slide 5: Experimental results for low QP
HDR PQ |  |  | AI |  |  |  |  | 
 |  |  | Over VTM12.0 |  |  |  |  | 
 | wPsnrY | wPsnrU | wPsnrV | psnrY | psnrU | psnrV | EncT | DecT
PQ444 | 0.00% | -0.11% | -0.12% | 0.01% | -0.10% | -0.12% | 99% | 100%
PQ422 | 0.01% | -0.08% | -0.15% | 0.02% | -0.06% | -0.13% | 99% | 101%
Overall | 0.01% | -0.10% | -0.14% | 0.01% | -0.08% | -0.12% | 99% | 100%
 |  |  | LDB |  |  |  |  | 
 |  |  | Over VTM12.0 |  |  |  |  | 
 | wPsnrY | wPsnrU | wPsnrV | psnrY | psnrU | psnrV | EncT | DecT
PQ444 | -0.10% | -0.23% | -0.29% | -0.08% | -0.21% | -0.25% | 96% | 100%
PQ422 | -0.11% | -0.30% | -0.40% | -0.09% | -0.26% | -0.35% | 99% | 98%
Overall | -0.11% | -0.26% | -0.34% | -0.08% | -0.24% | -0.30% | 98% | 99%
 |  |  | RA |  |  |  |  | 
 |  |  | Over VTM12.0 |  |  |  |  | 
 | wPsnrY | wPsnrU | wPsnrV | psnrY | psnrU | psnrV | EncT | DecT
PQ444 | -0.05% | -0.22% | -0.27% | -0.04% | -0.20% | -0.24% | 98% | 98%
PQ422 | -0.05% | -0.24% | -0.34% | -0.03% | -0.21% | -0.30% | 99% | 99%
Overall | -0.05% | -0.23% | -0.31% | -0.03% | -0.20% | -0.27% | 98% | 99%
Overall PQ | -0.05% | -0.20% | -0.26% | -0.04% | -0.17% | -0.23% | 98% | 99%
HDR HLG |  |  | AI |  | 
 |  |  | Over VTM12.0 |  | 
 | psnrY | psnrU | psnrV | EncT | DecT
HLG444 | 0.02% | 0.01% | 0.00% | 100% | 99%
HLG422 | 0.03% | 0.00% | 0.00% | 100% | 100%
Overall | 0.02% | 0.00% | 0.00% | 100% | 100%
 |  |  | LDB |  | 
 |  |  | Over VTM12.0 |  | 
 | psnrY | psnrU | psnrV | EncT | DecT
HLG444 | -0.02% | -0.10% | -0.18% | 96% | 98%
HLG422 | 0.00% | -0.12% | -0.22% | 98% | 98%
Overall | -0.01% | -0.11% | -0.20% | 97% | 98%
 |  |  | RA |  | 
 |  |  | Over VTM12.0 |  | 
 | psnrY | psnrU | psnrV | EncT | DecT
HLG444 | 0.02% | -0.09% | -0.16% | 100% | 99%
HLG422 | 0.02% | -0.11% | -0.23% | 101% | 98%
Overall | 0.02% | -0.10% | -0.19% | 101% | 98%
Overall HLG | 0.01% | -0.07% | -0.13% | 99% | 99%

## Slide 6: Experimental results for low QP
SVT RGB |  |  | AI |  | 
 |  |  | Over VTM12.0 |  | 
 | psnrG | psnrB | psnrR | EncT | DecT
SVT16 | 0.00% | 0.01% | 0.01% | 99% | 100%
SVT12 | 0.00% | 0.00% | 0.00% | 98% | 100%
Overall | 0.00% | 0.00% | 0.00% | 98% | 100%
 |  |  | LDB |  | 
 |  |  | Over VTM12.0 |  | 
 | psnrG | psnrB | psnrR | EncT | DecT
SVT16 | 0.05% | 0.00% | 0.00% | 102% | 99%
SVT12 | 0.02% | 0.00% | -0.01% | 101% | 99%
Overall | 0.03% | 0.00% | 0.00% | 102% | 99%
 |  |  | RA |  | 
 |  |  | Over VTM12.0 |  | 
 | psnrG | psnrB | psnrR | EncT | DecT
SVT16 | 0.03% | -0.01% | -0.01% | 102% | 99%
SVT12 | 0.02% | -0.02% | -0.02% | 101% | 100%
Overall | 0.02% | -0.01% | -0.01% | 102% | 100%
Overall RGB | 0.02% | 0.00% | 0.00% | 101% | 100%

## Slide 7: Experimental results for normal QP
 | Random Access |  |  |  |  |  |  |  |  | 
 | Over VTM-12.0 |  |  |  |  |  |  |  |  | 
 |  |  | wPSNR |  |  | PSNR |  |  |  | 
 | DE100 | PSNR-L100 | Y | U | V | Y | U | V | EncT | DecT
Class H1 | 3.99% | 1.99% | 1.58% | 4.86% | 5.60% | 1.50% | 4.38% | 4.22% | 88% | 100%
Class H2 |  |  |  |  |  | 1.97% | 4.69% | 4.36% | 82% | 103%
Overall | 3.99% | 1.99% | 1.58% | 4.86% | 5.60% | 1.74% | 4.53% | 4.29% | 85% | 101%
 | All Intra |  |  |  |  |  |  |  |  | 
 | Over VTM-12.0 |  |  |  |  |  |  |  |  | 
 |  |  | wPSNR |  |  | PSNR |  |  |  | 
 | DE100 | PSNR-L100 | Y | U | V | Y | U | V | EncT | DecT
Class H1 | 0.84% | 0.49% | 0.39% | 1.46% | -0.46% | 0.38% | 1.38% | -0.45% | 105% | 102%
Class H2 |  |  |  |  |  | 0.33% | 1.60% | 1.37% | 103% | 100%
Overall | 0.84% | 0.49% | 0.39% | 1.46% | -0.46% | 0.35% | 1.49% | 0.46% | 104% | 101%

## Slide 8: Conclusion
Introduced an issue of this contribution
  The CABAC throughput may decrease when large CTU and WPP are used.
Proposed a constraint for high bit depth and high bit rate coding
  Max CTU size 64
Showed experimental results
  Tested “CTUsize : 64”
  Negligible loss for low QP
  Loss was confirmed for normal QP
 |  |  | Over VTM12.0 |  | 
 | psnrY | psnrU | psnrV | EncT | DecT
Overall HLG | 0.01% | -0.07% | -0.13% | 99% | 99%
 |  |  | Over VTM12.0 |  |  |  |  | 
 | wPsnrY | wPsnrU | wPsnrV | psnrY | psnrU | psnrV | EncT | DecT
Overall PQ | -0.05% | -0.20% | -0.26% | -0.04% | -0.17% | -0.23% | 98% | 99%
Overall RGB | 0.02% | 0.00% | 0.00% | 101% | 100%