## Slide 1: Enhanced Intra MTS and LFNST for compression beyond VVC (JVET-V0116)
Bappaditya Ray, Louis Kerofsky, Muhammed Coban, Marta Karczewicz, Hilmi Egilmez, Vadim Seregin (Qualcomm)

## Slide 2: Mode dependent intra-MTS
VVC uses DCT8/DST7 transform pairs (i.e., 4 choices) for all intra modes.
Proposal:
Additional primary transforms: DCT5, DST4, DST1 and Identity Transform (IDTR).
Choices of transform pairs (i.e., 4 choices) dependent on intra mode and block shape.
16 different classes for block shapes; 5 different classes for intra mode.
Symmetry considering both block shape and intra mode ( e.g. WxH (mode 50) = HxW (mode 18)).
IDTR is used for small blocks (W & H <=16) and mode is closer to Ver/Hor.
4 MTS candidates signaled with 2 bit fixed-length coding (as opposed to truncated unary).
VTM shortcuts related to intra MTS are removed (Encoder only).
4x4 | 4x8 | 4x16 | 4xM
8x4 | 8x8 | 8x16 | 8xM
16x4 | 16x8 | 16x16 | 16xM
Mx4 | Mx8 | Mx16 | MxM
0 | 0 <= mode <=1
1 | 2 <= mode <=12
2 | 13 <= mode <=23
3 | 24 <= mode <=34
4 | MIP

## Slide 3: LFNST improvement
On top of Extended-LFNST (U0100).
2 methods are proposed – based on TU shape.
The other parameters are the same as Extended-LFNST.
Method 2 splits the 16x16 LFNST kernels into 7 classes: {4 x min(32,M), min(32,N) x 4}
TU Class | LFNST Kernels
{NxM ¦ min(N,M) = 4} | 16x16
{NxM ¦ min(N,M) > 4} | 64x64
LFNST Design | 16x16 | 64x64 | Sets | Candidates
U0100 | 1 | 1 | 35 | 3
Method 1 | 1 | 3 | 35 | 3
Method 2 | 7 | 3 | 35 | 3
LFNST Kernels:
TU class and LFNST kernel size
TU Class | LFNST Kernels
{NxM ¦ min(N,M) = 4} | 16x16
{NxM ¦ min(N,M) > 4} | 64x64
TU class and LFNST kernel size
Notes: 4x4,4x8,4x16,4x32,8x4,16x4,32x4 = 7 sets.

## Slide 4: Results: intra-MTS
Tool On
U0100

## Slide 5: Results: intra-MTS speedup
MTS can be speedup for a better tradeoff.
MTS
MTS with speedup

## Slide 6: Results: LFNST
Tool On(*) (Method 1)
(*) Tool on results show combined gain of Extended - LFNST and LFNST improvement
(**) Runtime not reliable, should be similar to Extended - LFNST.
Tool On(*)(**) (Method 2)

## Slide 7: Conclusion
Intra-MTS provides gain with encoder runtime increase.
  Preliminary results demonstrate encoder speedup is possible for a better tradeoff.
LFNST improvement provides gain on top of Extended-LFNST
It is requested to consider both MTS and LFNST improvement aspects to be studied in EE2.