## Slide 1: EE2: Tests of compression efficiency methods beyond VVC
JVET-V0120
Yao-Jen Chang, Chun-Chi Chen, Jie Dong, Nan Hu, Han Huang, Marta Karczewicz, Bappaditya Ray, Vadim Seregin, Yan Zhang, Zhi Zhang

## Slide 2: Summary of the modifications
Intra
  Multi-model LM
  Gradient PDPC
  Secondary MPM
  Reference sample interpolation
  Decoder side intra
Inter
  Local illumination compensation
  Extended merge list with non-adjacent candidates
  Template matching
  Multi-pass decoder side MV refinement
  OBMC
  Sample-based BDOF
  12-tap interpolation
  Multi-hypothesis prediction
  Affine MMVD
  CIIP with PDPC blending
Base modifications
  Non-normative
    lossy encoder speedups for affine, AMVR, and merge.
    Use original samples for SAO and ALF (reported in JVET-V0095)
    More SIMD
  Normative
    Increase CTU and TU sizes to 256
    Remove MTS zero out, VPDU, constraints on small intra (SCIPU), inter, and CIIP blocks; CCLM latency restriction, use LMS linear model for CCLM, affine and BDOF constraints.
    Adjust deblocking parameters based on temporal ID.
Transform and coefficient coding
  CTU and max transform is 256
  Extended LFNST
  Sign prediction
  8-state dependent quantization
ALF
  9x9 filter shape
  Multiple fixed filters
Entropy coding
  Extended precision
  Slice type based CABAC window size

## Slide 3: Intra prediction
Multi-model LM (JVET-D0110)
  Neighboring samples are classified into 2 classes
  Linear model is derived per class
  Linear least square method is used
Gradient PDPC (JVET-Q0391)
  Gradient PDPC method of horizontal/vertical modes is extended to other modes
Secondary MPM (JVET-D0114)
  Primary MPM consists of 5 entries
  Secondary MPM list of 16 entries is introduced, derived from the primary MPMs by adding ±1, ±2, ±3, …
  Shape dependent order of neighboring blocks to construct the list
Reference sample interpolation (JVET-D0119)
  4-tap cubic interpolation is replaced by 6-tap filter
  6-tap Gaussian filter is used for larger blocks
  4-tap filtering is used instead of the nearest neighbor to derive extended reference
Decoder side intra mode derivation (JVET-O0449)
  Intra prediction is derived as a weighted average between Planar and two derived directions
  The first DIMD mode is stored with a block and is included into the primary MPM list of the neighboring blocks

## Slide 4: Multi-Model LM Mode
Multiple linear models between the luma samples and chroma samples in a block.
Neighboring luma samples and neighboring chroma samples of the current block are classified into 2 groups by threshold calculated as a mean luma value.
A specific linear model (a and b ) is derived for each group.

## Slide 5: Gradient PDPC and reference interpolation
Gradient based PDPC is extended from ver/hor PDPC modes for unavailable secondary reference samples
p(x,y) = ((64 – wL(x)) * p(x,y) +
wL(x) * (r(-1, y) - r(-1+d,-1)) + 32) >> 6)
gradient term
6 tap interpolation for intra prediction.
4 tap filter to extend reference line (generating P from X0, X1, X2, X3).
6 tap Gaussian filter for bigger blocks (width >= 32 and height >=32).
d is the horizontal displacement depending on the angular direction,
which is already derived in the intra prediction process

## Slide 6: Decoder Side Intra Mode Derivation
Intra prediction direction is estimated without intra mode signaling
Step 1. Estimate gradient per sample (for orange samples)
Step 2: Map gradient values to closest prediction direction within [2, 66]
Gx
Gy
N
N+1
map to closest direction
  angTable[N] < Gy/Gx < angTable[N+1]
Step 3: Select 2 prediction directions
For each prediction direction, sum up all absolute gradients Gx and Gy of neighboring pixels with that direction. Top 2 directions are selected.
Step 4: Weighted Intra prediction with the selected directions
M1
M2

## Slide 7: Local illumination compensation
Linear model compensating local illumination variation is derived between current block and its prediction block.
It is based on CE test JVET-O0066 with the following changes:
  LIC is disabled for blocks with less than 32 luma samples;
  For both non-subblock and affine modes, LIC parameter derivation is performed based on the template block samples corresponding to the current CU, instead of partial template block samples corresponding to first top-left 16x16 unit;
  Intra neighbor samples can be used in LIC parameter derivation;
  Samples of the reference block template are generated by using MC with the block MV without rounding it to integer-pel precision.
For sub-block modes (affine), LIC model is derived based on the boundary sub-blocks and the derived single model is applied to the entire block

## Slide 8: Extended merge list with non-adjacent candidates
Max number of merge candidates is set to 10
Add non-adjacent candidates to the merge list
Merge list construction:
Spatial candidates 2134
Spatial candidate block 5 if previous number less than 4
TMVP candidate
Non-adjacent spatial candidates (blocks 6 to 23)
HMVP
Pair-wise
Zero candidates
Spatial candidates' positions

## Slide 9: Template matching
Decode side MV refinement based on template matching (JVET-J0021)
Search range is [-8, +8] around the initial MV using iterative search process
Initial MV comes from the merge mode or AMVP
In AMVP mode, MVP is refined by this process
Search pattern | AMVR mode |  |  |  | Merge mode |  | 
 | 4-pel | F-pel | H-pel | Q-pel | BM off AltIF=0 | BM off AltIF=1 | BM on
4-pel diamond | v |  |  |  |  |  | 
4-pel cross | v |  |  |  |  |  | 
Full-pel diamond |  | v | v | v | v | v | v
Full-pel cross |  | v | v | v | v | v | v
Half-pel cross |  |  | v | v | v | v | v
Quarter-pel cross |  |  |  | v | v |  | 
1/8-pel cross |  |  |  |  | v |  | 
Model-based |  |  |  |  |  |  | v

## Slide 10: Multi-pass decoder-side motion vector refinement (1)
Bilateral merge is applied to bi-prediction only, and both MVs are simultaneously refined in a symmetrical manner
Multi-pass DMVR derives refined motion vector in a hieratical process
First pass
  Bilateral template matching is applied to the whole block to get the updated MV
  3x3 square integer search is used within up to [-8, +8]
Second pass
  Bilateral template matching is applied to 16x16 subblocks to update the first pass MV
  Full integer search is performed within up to [-8, +8]
Third pass
  BDOF refinement is applied to 8x8 subblocks to update the second pass MV
  MV offsets Vx and Vy are rounded to 1/16 and clipped between -32 and 32
PU
Third pass
8x8
Second pass
16x16
First pass

## Slide 11: Multi-pass decoder-side motion vector refinement (2)
First pass 3x3 square search
Integer search is terminated if the cost in the center of 3x3 square reaches the minimum
Second pass subblocks full search
SATD cost is multiplied by the cost factor depending on the search region
Each region is processed in the raster scan order
Integer search is terminated if the minimum cost in the search region is less than a threshold

## Slide 12: Overlapped block motion compensation (OBMC)
OBMC is always enabled for merge mode and OBMC flag is signaled otherwise
  Disabled when LIC is enabled
CU-boundary OBMC
  Top and left CU boundaries are refined using neighbor block motion
  4(luma)/1(chroma) lines processed for blending
Subblock-OBMC
  Top, left, bottom, and right subblock boundaries are refined using neighbor subblock motion
  Applied to subblock-coded CUs, e.g. affine modes, SbTMVP, and subblock-based bilateral matching
  3(luma)/1(chroma) lines processed for blending

## Slide 13: Other inter modifications
Sample-based BDOF
  Instead of the block basis, BDOF refinement is derived per sample
  5x5 window around each sample is used to derive Vx and Vy refinement
  On 8x8 subblock basis, whether to apply BDOF or not is determined by checking the SAD between the two reference subblocks against a threshold
Multi-hypothesis prediction (JVET-M0425)
  Applied to bi-prediction in AMVP mode (for non equal BCW weights), affine AMVP (IMV 0), regular merge mode, MMVD, Affine MMVD
  Additional hypothesis can be MERGE or AMVP mode
  Up to 2 additional predictors are signalled or inherited for merge mode
12-tap interpolation for luma
Affine MMVD (JVET-N0378)
  3 sets of distance offsets are used, offset is added to CPMV
CIIP with PDPC blending (JVET-O0537)
  Regular merge predictor is refined using the above (Rx, -1) and left (R-1, y) reconstructed samples
  The refinement uses PDPC scheme

## Slide 14: Transform and coefficient coding
CTU and max transform size is extended to 256
The number of LFNST sets is extended to 35 with 3 candidates
Full 64x64 LFNST matrix is used (no zeroing out)
8-state DQ is utilized (JVET-Q0243)

## Slide 15: Transform Coefficients Sign Prediction
Sign prediction is applied for up to 8 transform coefficients (JVET-D0031, JVET-J0021)
A context coded bin is signaled to indicate whether a coefficient sign is equal to the sign which minimizes the cost function.
  E.g., if two signs are predicted, for all possible combination of sign values, (+, +), (+, –), (–, +), (–, –), the cost function is calculated and the combination with the minimum cost is selected.
  Context is derived whether a coefficient is DC or not, contexts are separated for intra and inter blocks, for luma and chroma components.
Cost function
  Calculate reconstructed residual for both negative and positive sign combinations.
    The reconstructed residual is derived based on the prestored elemental residuals multiplied by coefficient magnitude and accumulated for all coefficients for which sign is predicted.
  Cost function is defined as discontinuity measure across block boundary.

## Slide 16: Entropy coding
The precisions for two probability states are both increased to 15 bits, in comparison to 10 bits and 14 bits in VVC
LPS range update process is modified as follows
CABAC context window is defined for each slice type (I-, B-, and P-slices)
if q >= 214
q = 215 – 1 – q
RLPS = ( ( range × (q>>6) ) >>9 ) + 1
range: width of the current interval, 9-bit
q: probability state of the current context model, 15-bit
RLPS: updated range for LPS, 8-bit

## Slide 17: Adaptive loop filter
Luma and chroma filter shapes are extended to 9x9
Classification is performed on 2x2 basis
Luma filtering is applied using 1 signaled F2 9x9 filter and 2 fixed F0, F1 13x13 filters
Weighting coefficients for F0 and F1 fixed filters are signalled
Different 2x2 based classifiers are used for F0, F1, and F2 filters
  Directionality is derived by comparing the ratio of horizontal, vertical, and diagonal gradients with a set of thresholds, which supports more edge strengths
 | 0 | 1 | 2 | 3 | 4 | 5 | 6
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 1 | 2 | 0 | 0 | 0 | 0 | 0
2 | 3 | 4 | 5 | 0 | 0 | 0 | 0
3 | 6 | 7 | 8 | 9 | 0 | 0 | 0
4 | 10 | 11 | 12 | 13 | 14 | 0 | 0
5 | 15 | 16 | 17 | 18 | 19 | 20 | 0
6 | 21 | 22 | 23 | 24 | 25 | 26 | 27
 | 0 | 1 | 2 | 3 | 4 | 5 | 6
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 1 | 2 | 0 | 0 | 0 | 0 | 0
2 | 3 | 4 | 5 | 0 | 0 | 0 | 0
3 | 6 | 7 | 8 | 9 | 0 | 0 | 0
4 | 10 | 11 | 12 | 13 | 14 | 0 | 0
5 | 15 | 16 | 17 | 18 | 19 | 20 | 0
6 | 21 | 22 | 23 | 24 | 25 | 26 | 27
 | 0 | 1 | 2 | 3 | 4 | 5 | 6
0 | 28 | 0 | 0 | 0 | 0 | 0 | 0
1 | 29 | 30 | 0 | 0 | 0 | 0 | 0
2 | 31 | 32 | 33 | 0 | 0 | 0 | 0
3 | 34 | 35 | 36 | 37 | 0 | 0 | 0
4 | 38 | 39 | 40 | 41 | 42 | 0 | 0
5 | 43 | 44 | 45 | 46 | 47 | 48 | 0
6 | 49 | 50 | 51 | 52 | 53 | 54 | 55
 | 0 | 1 | 2 | 3 | 4 | 5 | 6
0 | 28 | 0 | 0 | 0 | 0 | 0 | 0
1 | 29 | 30 | 0 | 0 | 0 | 0 | 0
2 | 31 | 32 | 33 | 0 | 0 | 0 | 0
3 | 34 | 35 | 36 | 37 | 0 | 0 | 0
4 | 38 | 39 | 40 | 41 | 42 | 0 | 0
5 | 43 | 44 | 45 | 46 | 47 | 48 | 0
6 | 49 | 50 | 51 | 52 | 53 | 54 | 55

## Slide 18: Results
All Intra Main10 |  |  |  |  | 
Over VTM-11.0 |  |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -5.37% | -9.93% | -10.84% | 208% | 211%
Class A2 | -5.02% | -8.10% | -6.15% | 201% | 193%
Class B | -4.60% | -7.49% | -7.97% | 225% | 191%
Class C | -5.41% | -7.68% | -8.02% | 224% | 180%
Class E | -5.64% | -8.17% | -6.86% | 230% | 213%
Overall | -5.15% | -8.15% | -7.97% | 218% | 196%
Class D | -4.31% | -5.95% | -5.72% | 237% | 188%
Class F | -8.17% | -10.63% | -11.09% | 177% | 182%
Random access Main10 |  |  |  |  | 
Over VTM-11.0 |  |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -11.82% | -13.54% | -16.14% | 275% | 445%
Class A2 | -13.10% | -14.71% | -14.45% | 260% | 533%
Class B | -11.13% | -12.38% | -11.82% | 258% | 444%
Class C | -12.91% | -13.25% | -13.36% | 270% | 438%
Class E |  |  |  |  | 
Overall | -12.14% | -13.31% | -13.62% | 265% | 459%
Class D | -14.02% | -13.65% | -13.47% | 286% | 464%
Class F | -10.77% | -12.74% | -12.90% | 231% | 319%
Low delay B Main10 |  |  |  |  | 
Over VTM-11.0 |  |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -9.30% | -10.48% | -10.21% | 230% | 279%
Class C | -10.86% | -10.71% | -11.98% | 248% | 268%
Class E | -9.05% | -10.57% | -8.34% | 203% | 244%
Overall | -9.76% | -10.58% | -10.37% | 229% | 266%
Class D | -12.53% | -12.18% | -13.05% | 264% | 314%
Class F | -11.29% | -11.53% | -11.38% | 216% | 223%
EE2 U0100 software, all macros enabled