## Slide 1: CE-related: On prefix code length of remaining level coding for high bit depth and high bit rate coding JVET-V0123
Yue Yu, Zhihuang Xie, Fan Wang, Haoping Yu, Dong Wang
JVET-V0123

## Slide 2: Remaining Level Coding in VVC version 1
After context coded bins, remaining level coded with Golomb-Rice/exponential-Golomb ;
The maximum length of binarization for remaining level is 32;
There are three parameters, prefix length, Rice parameter and coefficient range (Log2TransformRange) to decide how to binarize a level;
Prefix length = 6, Log2TransformRange = 15, Rice = 1 for TSRC; Rice = 0 to 3 for RRC;
If extended precision is on, Log2TransformRange = max(15, bitDepth + 6), 22 for 16 bit-depth input.

## Slide 3: One example
Left (PrefixLength = 1): level above 4092 will use 32 bins if prefix length is 1;
Right (PrefixLength = 4) : Level above 2300 will use 32 bins if prefix length is 4;

## Slide 4: Proposed Method
A simple change: using a smaller prefix length for high bit depth, high bit rate coding;
Change prefix length to a smaller fixed number equal to 1 for both RRC and TSRC on the VTM12;
cMax = 1 << cRiceParam (1526)
cMax = 1 << cRiceParam (1529)
Change prefix length to a smaller fixed number equal to 4 for both RRC and TSRC on the top of CE base.
cMax = 4 << cRiceParam (1526)
cMax = 4 << cRiceParam (1529)

## Slide 5: Simulation Results
Simulation conditions follow the CTC for high bit-depth coding;
Over VTM12, low QP, lossy (PrefixLength = 1).

## Slide 6
Over VTM 12, normal QP, lossy (PrefixLength = 1)

## Slide 7
Over CEBase, low QP, lossy (PrefixLength = 4)

## Slide 8
Over CEBase, normal QP, lossy (PrefixLength = 4)

## Slide 9: Conclusion
There are many large remaining level for high bit depth, high bit rate coding;
A smaller prefix length is suitable for high bit depth, high bit rate coding;
Suggest to conduct smaller prefix length tests in relevant CE.
Thank Kwai for crosschecking!