## Slide 1: AHG8: Weighted Prediction for VVC High Bit Depth Extension JVET-V0124
Yue Yu, Haoping Yu, Zhihuang Xie, Fan Wang, Dong Wang
JVET-V0124

## Slide 2: Weighted Prediction in VVC version 1
Weighted prediction is very useful for coding fades;
>>log2Wd+O0)
where O0 is an additive offset, w0 is weighted factor, Wd is the log denominator rounding factor.
Luma component
O0 = luma_offset_l0 << ( bitDepth − 8 )
where luma_offset_l0 is an 8-bit syntax element (-128 to 127).
For high bit depth input, eg. 16-bit depth, if we use the same method,
O0 = luma_offset_l0 << 8
The actual precision is still 8-bit, may not good enough for such high bit depth video coding.

## Slide 3: Weighted Prediction in HEVC Range Extension
Offset is bit-depth-dependent precision equal to bit-depth of input video.
O0 = luma_offset_l0
where luma_offset_l0 is a bit-depth-dependent syntax element;
For 16-bit depth input video, the range of luma_offset_l0 is from to).

## Slide 4: Proposed Method
Design Goal:
  good performance for input video bit-depth >10 : weighted prediction offset with full precision;
  consistent design between profiles for 8 or 10-bit input video: same solution as in VVC version 1
If bit depth of input video is 8 or 10, keep current VVC’s way unchanged.
O0 = luma_offset_l0 << ( bitDepth − 8 )
where luma_offset_l0 is an 8-bit syntax element (-128 to 127);
If bit depth of input video is above 10, the dynamic range of luma_offset_l0 is the same with that specified by the input bit-depth.
O0 = luma_offset_l0
where luma_offset_l0 is a bit-depth-dependent syntax element.

## Slide 5: Proposed Syntax and Semantics Changes
sps_high_precision_offsets_enabled_flag, ph_high_precision_offsets_enabled_flag on/off the proposed method at SPS and picture levels;
luma_offset_l0[ i ] is the additive offset applied to the luma prediction value for list 0 prediction using RefPicList[ 0 ][ i ]. The value of luma_offset_l0[ i ] shall be in the range of -WpOffsetHalfRangeY to WpOffsetHalfRangeY, inclusive. When luma_weight_l0_flag[ i ] is equal to 0, luma_offset_l0[ i ] is inferred to be equal to 0.
WpOffsetBdShiftY = ph_high_precision_offsets_enabled_flag ? ( BitDepthY ==10 ? (BitDepthY − 8) : 0 ) : ( BitDepthY − 8 ) (1)
WpOffsetHalfRangeY = 1 << ( ph_high_precision_offsets_enabled_flag ? (BitDepthY ==10 ? 7 : ( BitDepthY − 1 )) : 7 ) (2)
o0 = luma_offset_l0[ refIdxL0 ] << WpOffsetBdShiftY (3)

## Slide 6: Conclusions
Proposes a weighted prediction method for VVC high bit depth coding;
If the input video is 8 or 10 bit-depth, offset syntax element is 8-bit precision;
If the input video is above 10 bit-depth, offset syntax element is the same precision with bit-depth of input video.