## Slide 1
JVET-V0153
AHG12: Cross-component Sample Adaptive Offset
Che-Wei Kuo, Xiaoyu Xiu, Yi-Wen Chen, Hong-Jheng Jhu, Wei Chen, and Xianglin Wang

## Slide 2: Introduction
SAO EO: removes ringing artifacts near sharp transitions
SAO BO: alleviates the DC distortion caused by the coding process
  Reconstructed samples are classified into multiple bands
  At encoder, one offset is derived and signaled for each band
  Only uses one single luma/chroma sample as input to enhance itself
There exists strong correlation between different components

## Slide 3: Introduction
Cross-component Sample Adaptive Offset (CCSAO) is proposed for further compression efficiency exploration beyond VVC
Highlights
  Over VTM-12.0
  Low complexity & hardware friendly
AI |  |  | RA |  |  | LDB |  | 
Y | U | V | Y | U | V | Y | U | V
0.13% | -2.43% | -2.39% | 0.04% | -3.62% | -3.61% | -0.15% | -8.45% | -8.64%

## Slide 4: CCSAO
Utilizes all three components to classify the current sample
At encoder, one offset is derived and explicitly signaled for each class
Output samples from the de-blocking filter are used for classification
  Parallel processing between SAO and CCSAO

## Slide 5: Classification
, ,
, ,
BD
,
collocated three component samples used to classify the current sample
numbers of equally divided bands applied to {, , } full range
internal coding bit-depth
reconstruction samples before/after CCSAO
i-th BO category CCSAO offset
E.g., current sample is a choma U sample located at , three component samples are used to classify it
4
4
4
4

## Slide 6: CTB-level Classifier Switch
Parameters for each classifier are signaled in frame level
  Position of which can be chosen from 9 candidates
  Maximum of {, , } is set to {16, 4, 4}
  Offsets are constrained to be within the range [-15, 15]
Which classifier to be used is explicitly signaled and switched in CTB level
Maximum classifiers per frame is constrained to be 4

## Slide 7: Simulation Results
 | All Intra Main10 |  |  |  | 
 | Over VTM-12.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.13% | -1.93% | -2.63% | 113% | 101%
Class A2 | 0.14% | -3.60% | -0.61% | 118% | 101%
Class B | 0.15% | -3.12% | -3.90% | 106% | 101%
Class C | 0.12% | -1.59% | -1.45% | 102% | 102%
Class E | 0.13% | -1.77% | -2.67% | 103% | 102%
Overall | 0.13% | -2.43% | -2.39% | 108% | 102%
Class D | 0.06% | -1.35% | -0.82% | 100% | 102%
Class F | -0.21% | -2.67% | -2.14% | 104% | 102%
Class TGM | -0.94% | -1.55% | -1.57% | 110% | 103%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-12.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.31% | -2.96% | -5.04% | 106% | 103%
Class A2 | 0.14% | -3.45% | -1.57% | 107% | 102%
Class B | 0.13% | -5.18% | -5.41% | 106% | 103%
Class C | 0.12% | -2.30% | -1.81% | 103% | 102%
Class E |  |  |  |  | 
Overall | 0.04% | -3.62% | -3.61% | 105% | 102%
Class D | 0.19% | -2.38% | -1.58% | 102% | 103%
Class F | -0.31% | -3.20% | -2.87% | 107% | 102%
Class TGM | -1.14% | -3.15% | -3.51% | 116% | 103%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-12.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.30% | -13.09% | -12.86% | 107% | 103%
Class C | 0.06% | -5.93% | -4.78% | 102% | 101%
Class E | -0.16% | -4.06% | -6.75% | 103% | 102%
Overall | -0.15% | -8.45% | -8.64% | 104% | 102%
Class D | 0.21% | -5.97% | -5.12% | 101% | 102%
Class F | -0.87% | -8.15% | -7.15% | 110% | 103%
Class TGM | -2.14% | -7.42% | -7.38% | 121% | 104%
Over VTM-12.0 with encoder fix in [1]
Without SIMD
[1] N. Hu, V. Seregin, M. Karczewicz, “ AHG10: Using original samples for SAO and ALF optimization”, JVET-V0095, Apr. 2021, Teleconference.

## Slide 8: Conclusion
Cross-component Sample Adaptive Offset (CCSAO) is proposed for further compression efficiency exploration beyond VVC
Coding gains with marginal cost
  Classification-based sample operation
  Low encoding/decoding complexity (can be further optimized)
Suggest to study in EE