## Slide 1
JVET-W0052
CE-related: CABAC skip mode
K. Abe, T. Toma, V. Drugeon
Panasonic Corporation

## Slide 2
2
Introduction
Overview
・Proposal to completely skip CABAC for all slice data syntax.
・It was originally proposed in JVET-M0089, JVET-N0207 and JVET-O0308.
・There are no technical changes compared to the previous proposals, only a report of HBD
CTC results.
Related CE items
・CE3.1 (JVET-W0044)
Performing CABAC bypass alignment after CCB threshold is reached.
・CE3.2 (JVET-W0045)
Setting CCB threshold to 0 and performing CABAC bypass alignment at the start of residual.
All proposals aim to solve CABAC throughput issues by skipping CABAC engine processing.

## Slide 3
3
Proposal
・Output binarized bins directly as a bitstream.
・CCB threshold is set equal to 0 (all residual is bypass coded in both RRC and TSRC).
Binarization
CABAC
Trans/Quant
＋
－
Intra Pred
Inter Pred
Input
image
Output
stream
Inv Quant/Trans
Bin stream
buffer
Bit stream
buffer
Avoids all CABAC throughput issues without any additional building blocks.
It can be switched at stream level.
CCB threshold is always set equal to 0.

## Slide 4
Simulation results (HBD Low QP CTC)
Anchor : VTM13.0
Test : CABAC skip mode
HDR PQ | AI |  |  |  |  |  |  |  |  | HDR HLG | AI |  |  |  |  |  | SVT RGB | AI |  |  |  | 
 | Over VTM13.0 |  |  |  |  |  |  |  |  |  | Over VTM13.0 |  |  |  |  |  |  | Over VTM13.0 |  |  |  | 
 | wPsnrY | wPsnrU | wPsnrV | psnrY | psnrU | psnrV | EncT | DecT |  |  | psnrY | psnrU | psnrV | EncT | DecT |  |  | psnrG | psnrB | psnrR | EncT | DecT
PQ444 | 13.04% | 15.22% | 15.57% | 12.82% | 14.92% | 15.39% | 85% | 82% |  | HLG444 | 7.81% | 8.45% | 9.18% | 93% | 70% |  | SVT16 | 2.13% | 1.84% | 1.79% | 80% | 59%
PQ422 | 11.06% | 12.39% | 12.35% | 10.85% | 12.18% | 12.26% | 90% | 81% |  | HLG422 | 7.41% | 7.89% | 8.47% | 86% | 70% |  | SVT12 | 3.40% | 2.94% | 2.92% | 82% | 63%
Overall | 12.05% | 13.80% | 13.96% | 11.83% | 13.55% | 13.83% | 87% | 82% |  | Overall | 7.61% | 8.17% | 8.82% | 89% | 70% |  | Overall | 2.77% | 2.39% | 2.36% | 81% | 61%
 | LDB |  |  |  |  |  |  |  |  |  | LDB |  |  |  |  |  |  | LDB |  |  |  | 
 | Over VTM13.0 |  |  |  |  |  |  |  |  |  | Over VTM13.0 |  |  |  |  |  |  | Over VTM13.0 |  |  |  | 
 | wPsnrY | wPsnrU | wPsnrV | psnrY | psnrU | psnrV | EncT | DecT |  |  | psnrY | psnrU | psnrV | EncT | DecT |  |  | psnrG | psnrB | psnrR | EncT | DecT
PQ444 | 17.98% | 22.18% | 21.48% | 17.29% | 21.52% | 21.26% | 86% | 87% |  | HLG444 | 14.15% | 16.22% | 17.13% | 77% | 80% |  | SVT16 | 1.68% | 1.82% | 1.82% | 72% | 70%
PQ422 | 16.97% | 18.15% | 17.54% | 16.30% | 17.67% | 17.45% | 83% | 86% |  | HLG422 | 15.01% | 16.29% | 16.28% | 78% | 79% |  | SVT12 | 3.79% | 4.00% | 3.99% | 70% | 74%
Overall | 17.47% | 20.17% | 19.51% | 16.79% | 19.60% | 19.35% | 84% | 87% |  | Overall | 14.58% | 16.26% | 16.70% | 77% | 80% |  | Overall | 2.74% | 2.91% | 2.90% | 71% | 72%
 | RA |  |  |  |  |  |  |  |  |  | RA |  |  |  |  |  |  | RA |  |  |  | 
 | Over VTM13.0 |  |  |  |  |  |  |  |  |  | Over VTM13.0 |  |  |  |  |  |  | Over VTM13.0 |  |  |  | 
 | wPsnrY | wPsnrU | wPsnrV | psnrY | psnrU | psnrV | EncT | DecT |  |  | psnrY | psnrU | psnrV | EncT | DecT |  |  | psnrG | psnrB | psnrR | EncT | DecT
PQ444 | 17.80% | 21.53% | 21.62% | 17.16% | 20.99% | 21.45% | 86% | 88% |  | HLG444 | 14.47% | 16.46% | 17.06% | 78% | 81% |  | SVT16 | 1.75% | 1.77% | 1.77% | 70% | 70%
PQ422 | 16.61% | 17.96% | 17.43% | 16.02% | 17.56% | 17.39% | 85% | 86% |  | HLG422 | 15.26% | 16.13% | 16.21% | 75% | 80% |  | SVT12 | 4.07% | 4.14% | 4.13% | 69% | 75%
Overall | 17.21% | 19.75% | 19.52% | 16.59% | 19.28% | 19.42% | 86% | 87% |  | Overall | 14.87% | 16.29% | 16.64% | 77% | 80% |  | Overall | 2.91% | 2.96% | 2.95% | 70% | 72%
Overall PQ | 15.58% | 17.90% | 17.66% | 15.07% | 17.48% | 17.53% | 86% | 85% |  | Overall HLG | 12.35% | 13.57% | 14.06% | 81% | 77% |  | Overall RGB | 2.80% | 2.75% | 2.74% | 74% | 68%

## Slide 5
Simulation results (HBD Low QP CTC)
HDR PQ | AI |  |  |  |  |  |  |  |  | HDR HLG | AI |  |  |  |  |  | SVT RGB | AI |  |  |  | 
 | Over HM16.23 |  |  |  |  |  |  |  |  |  | Over HM16.23 |  |  |  |  |  |  | Over HM16.23 |  |  |  | 
 | wPsnrY | wPsnrU | wPsnrV | psnrY | psnrU | psnrV | EncT | DecT |  |  | psnrY | psnrU | psnrV | EncT | DecT |  |  | psnrG | psnrB | psnrR | EncT | DecT
PQ444 |  |  |  | 6.25% | 7.30% | 6.75% |  |  |  | HLG444 | 3.04% | 1.93% | 2.26% |  |  |  | SVT16 | -0.30% | 0.24% | 0.18% |  | 
PQ422 |  |  |  | 0.80% | -2.51% | -3.33% |  |  |  | HLG422 | 1.87% | -0.10% | 0.35% |  |  |  | SVT12 | -0.78% | -0.08% | -0.18% |  | 
Overall |  |  |  | 3.52% | 2.39% | 1.71% |  |  |  | Overall | 2.45% | 0.91% | 1.31% |  |  |  | Overall | -0.54% | 0.08% | 0.00% |  | 
 | LDB |  |  |  |  |  |  |  |  |  | LDB |  |  |  |  |  |  | LDB |  |  |  | 
 | Over HM16.23 |  |  |  |  |  |  |  |  |  | Over HM16.23 |  |  |  |  |  |  | Over HM16.23 |  |  |  | 
 | wPsnrY | wPsnrU | wPsnrV | psnrY | psnrU | psnrV | EncT | DecT |  |  | psnrY | psnrU | psnrV | EncT | DecT |  |  | psnrG | psnrB | psnrR | EncT | DecT
PQ444 |  |  |  | 10.01% | 16.04% | 13.51% |  |  |  | HLG444 | 7.60% | 6.93% | 8.48% |  |  |  | SVT16 | -0.67% | 1.00% | 1.00% |  | 
PQ422 |  |  |  | 7.46% | 3.94% | 2.72% |  |  |  | HLG422 | 8.86% | 5.18% | 7.08% |  |  |  | SVT12 | -0.59% | 2.19% | 2.17% |  | 
Overall |  |  |  | 8.73% | 9.99% | 8.12% |  |  |  | Overall | 8.23% | 6.06% | 7.78% |  |  |  | Overall | -0.63% | 1.59% | 1.59% |  | 
 | RA |  |  |  |  |  |  |  |  |  | RA |  |  |  |  |  |  | RA |  |  |  | 
 | Over HM16.23 |  |  |  |  |  |  |  |  |  | Over HM16.23 |  |  |  |  |  |  | Over HM16.23 |  |  |  | 
 | wPsnrY | wPsnrU | wPsnrV | psnrY | psnrU | psnrV | EncT | DecT |  |  | psnrY | psnrU | psnrV | EncT | DecT |  |  | psnrG | psnrB | psnrR | EncT | DecT
PQ444 |  |  |  | 9.67% | 15.31% | 13.89% |  |  |  | HLG444 | 7.26% | 6.41% | 7.85% |  |  |  | SVT16 | -0.72% | 0.77% | 0.78% |  | 
PQ422 |  |  |  | 6.84% | 3.33% | 2.68% |  |  |  | HLG422 | 8.43% | 4.69% | 6.78% |  |  |  | SVT12 | -0.61% | 2.12% | 2.10% |  | 
Overall |  |  |  | 8.26% | 9.32% | 8.29% |  |  |  | Overall | 7.85% | 5.55% | 7.31% |  |  |  | Overall | -0.67% | 1.44% | 1.44% |  | 
Overall PQ |  |  |  | 6.84% | 7.23% | 6.04% |  |  |  | Overall HLG | 6.18% | 4.17% | 5.47% |  |  |  | Overall RGB | -0.61% | 1.04% | 1.01% |  | 
Anchor : HM16.23 RExt (AHG8 report)
Test : CABAC skip mode

## Slide 6
Simulation results (HBD Normal QP CTC)
Anchor : VTM13.0
Test : CABAC skip mode
 | AI |  |  |  |  |  |  |  |  | 
 | Over VTM13.0 |  |  |  |  |  |  |  |  | 
 |  |  | wPSNR |  |  | PSNR |  |  |  | 
 | DE100 | PSNR-L100 | Y | U | V | Y | U | V | EncT | DecT
Class H1 | 13.47% | 13.91% | 14.38% | 16.37% | 17.40% | 14.21% | 16.31% | 17.49% | 97% | 95%
Class H2 |  |  |  |  |  | 19.35% | 13.58% | 11.28% | 94% | 97%
Overall | 13.47% | 13.91% | 14.38% | 16.37% | 17.40% | 16.78% | 14.94% | 14.39% | 95% | 96%
 | RA |  |  |  |  |  |  |  |  | 
 | Over VTM13.0 |  |  |  |  |  |  |  |  | 
 |  |  | wPSNR |  |  | PSNR |  |  |  | 
 | DE100 | PSNR-L100 | Y | U | V | Y | U | V | EncT | DecT
Class H1 | 15.86% | 18.50% | 18.51% | 15.80% | 16.99% | 18.39% | 15.76% | 16.75% | 100% | 100%
Class H2 |  |  |  |  |  | 22.12% | 12.68% | 10.32% | 96% | 102%
Overall | 15.86% | 18.50% | 18.51% | 15.80% | 16.99% | 20.25% | 14.22% | 13.54% | 98% | 101%

## Slide 7
Additional Study
 |  | QP | VTM13.0 |  |  |  |  | CABAC skip mode (proposal) |  |  |  | 
 |  |  | bit rata (kbps) | Bin rate (kbps) |  |  | symbol rate (ksps) | bit rata (kbps) | Bin rate (kbps) (for reference) |  |  | symbol rate (ksps)
 |  |  |  | context | bypass | total |  |  | context | bypass | total | 
PQ 4:2:2 AI | Market3 (1920x1080, 50fps) (CTC results x 8) | -8 | 802,127 | 425,872 | 527,980 | 953,852 | 649,766 | 839,641 | 48,883 | 790,730 | 839,613 | 382,101
 |  | 2 | 475,046 | 309,651 | 273,461 | 583,111 | 444,795 | 502,473 | 50,406 | 452,039 | 502,445 | 269,834
 |  | 12 | 226,963 | 192,207 | 103,562 | 295,769 | 249,183 | 236,666 | 43,362 | 193,197 | 236,559 | 146,371
PQ 4:2:2 LDB | BalloonFestival (1920x1080, 24fps) | -8 | 119,269 | 80,316 | 65,124 | 145,440 | 113,859 | 128,073 | 15,128 | 112,933 | 128,061 | 69,995
 |  | 2 | 59,292 | 50,048 | 28,008 | 78,056 | 67,019 | 65,252 | 11,947 | 53,294 | 65,241 | 42,783
 |  | 12 | 18,347 | 20,237 | 6,803 | 27,040 | 24,599 | 19,520 | 7,113 | 12,384 | 19,497 | 14,790
HLG 4:4:4 AI | DayStreet (1920x1080, 60fps) (CTC results x 8) | -8 | 1,499,140 | 790,975 | 985,097 | 1,776,072 | 1,232,849 | 1,565,525 | 78,878 | 1,486,613 | 1,565,492 | 741,574
 |  | 2 | 902,948 | 672,860 | 475,685 | 1,148,546 | 940,954 | 973,407 | 83,915 | 889,415 | 973,329 | 570,582
 |  | 12 | 361,399 | 333,921 | 158,738 | 492,660 | 424,219 | 375,834 | 93,263 | 282,446 | 375,708 | 249,901
HLG 4:4:4 LDB | PeopleInSC (1920x1080, 60fps) | -8 | 1,116,201 | 734,117 | 622,479 | 1,356,596 | 1,113,043 | 1,198,699 | 58,183 | 1,140,504 | 1,198,687 | 697,707
 |  | 2 | 514,356 | 526,618 | 218,940 | 745,558 | 696,482 | 583,375 | 59,188 | 524,147 | 583,336 | 422,159
 |  | 12 | 63,748 | 80,229 | 20,831 | 101,059 | 92,360 | 53,733 | 25,763 | 27,905 | 53,668 | 42,416
SVT16 AI | OldTownCross (1920x1080, 50fps) (CTC results x 8) | -28 | 3,234,310 | 676,504 | 3,024,816 | 3,701,320 | 1,233,276 | 3,260,258 | 48,924 | 3,211,307 | 3,260,232 | 655,271
 |  | -18 | 2,698,290 | 653,014 | 2,485,122 | 3,138,136 | 1,221,334 | 2,712,089 | 31,174 | 2,680,888 | 2,712,062 | 644,926
 |  | -8 | 2,180,421 | 652,839 | 1,906,011 | 2,558,850 | 1,201,749 | 2,194,466 | 28,113 | 2,166,327 | 2,194,440 | 641,201
SVT16 LDB | CrowdRun (1920x1080, 50fps) | -28 | 2,879,097 | 622,467 | 2,690,645 | 3,313,112 | 1,210,289 | 2,924,017 | 43,697 | 2,880,312 | 2,924,009 | 652,833
 |  | -18 | 2,351,691 | 617,823 | 2,119,732 | 2,737,555 | 1,195,943 | 2,396,929 | 36,915 | 2,360,006 | 2,396,921 | 647,284
 |  | -8 | 1,829,671 | 626,694 | 1,502,962 | 2,129,656 | 1,162,861 | 1,875,851 | 38,634 | 1,837,209 | 1,875,843 | 642,999
Comparison of bit rate, Bin rate, and symbol rate in HBD Low QP condition
In CABAC skip mode, the symbol rate will be the bottleneck of the throughput instead of Bin rate.
The numbers of context Bin and symbol drastically decrease compared to VTM13 since CCB threshold is always set equal to 0.
The symbol rate is still huge, however, it would be possible to implement as multiple symbols in one cycle in the binarization stage.

## Slide 8
8
Conclusions
CABAC skip mode can avoid all CABAC throughput issues without any additional building blocks.
It would be helpful for high bit rate and super low delay use cases.
15%, 12%, 3% bitrate increase for PQ, HLG, SVT for HBD Low QP CTC .
The coding performance is similar to HEVC RExt (having CABAC) in AI conditions.
Thanks Sharp for cross-checking.
We propose to consider CABAC skip mode as a high throughput tool together with CE3 items.