## Slide 1
AHG8: A Study on bin-to-bit ratio of VTM-13.0 for high bit depth coding (JVET-W0115)
T. Tsukuba, S. Keating, M. Ikeda, T. Suzuki

## Slide 2: Motivation
One of the mandates in AHG8: HBD, HBR and HFR coding is
  Study VVC entropy decoding throughput in the cases of high bit depth, high bit rate, and high frame rate coding
Investigated BD-binrate, bin-to-bit ratio and other metrics of VTM-13.0 compared to HM-16.23 like JVET-N0049 and JVET-V0150.
  HBD CTC/Low QPs (QP=-13,…,12 for 12bit, QP=-33,…,-8 for 16bit)
  HBD CTC/Normal QPs (QP=22, 27, 32, 37) with GOP size set to 16

## Slide 3: Collected data and measurements
Data collected from the decoder
  The peak context coded bin rate, bypass bin rate and bitrate of a coded sequence
  The average context coded bin rate, bypass bin rate and bitrate over a coded sequence.
  The average context coded bin rate, bypass bin rate and bitrate for the transform coefficients coding over a coded sequence.
Measurements for the peak case, the average case and the transform coefficient coding part
  Weighted BD-binrate
  Weighted bin to bit ratio, unweighted bin to bit ratio
  Weighted delta binrate, which is measured using Bjøntegaard Delta-rate on bitrate vs bin rate.
Note: In the weighted measurements, a bypass bin is counted at 0.25 context coded bins (1:4); in the unweight measurements, a bypass bin is counted at 1 context coded bin (1:1).

## Slide 4: Results for Normal QPs (Anchor=HM-16.23, Tested=VTM-13.0)
Weighted BD-binrate (average): -2.43% for AI, -18.01% for RA
Unweighted Peak Bin-to-Bit ratio: AI:14.89%, RA:13.14%, Weighted Peak Bin-to-Bit ratio: AI:21.16%, RA:19.95%
Weighted Delta binrate: AI:17.94%, RA:12.87%; For the same bitrate, VTM’s binrate is higher than HM’s.
 | Random Access |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Over HM-16.23 GOP16 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | BD-bitrate |  |  | BD-binrate (average, weighted) |  |  | Delta Binrate (average) | Bin2Bit (peak, unweighted) |  |  | Bin2Bit (peak, weighted) |  |  | Runtime | 
 | Y | U | V | PsnrY | PsnrU | PsnrV | weighted | Reference | Tested | Diff (%) | Reference | Tested | Diff (%) | EncT | DecT
Class H1 | -21.38% | -65.31% | -76.35% | -12.90% | -59.01% | -71.46% | 10.72% | 1.19 | 1.33 | 12.31% | 0.87 | 1.05 | 20.24% | 376% | 166%
Class H2 | -31.05% | -54.17% | -53.43% | -23.12% | -48.09% | -47.16% | 15.03% | 1.18 | 1.35 | 13.97% | 0.89 | 1.07 | 19.65% | 374% | 143%
Overall | -26.21% | -59.74% | -64.89% | -18.01% | -53.55% | -59.31% | 12.87% | 1.19 | 1.34 | 13.14% | 0.88 | 1.06 | 19.95% | 375% | 154%
 | All Intra |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Over HM-16.23 GOP16 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | BD-bitrate |  |  | BD-binrate (average, weighted) |  |  | Delta Binrate (average) | Bin2Bit (peak, unweighted) |  |  | Bin2Bit (peak, weighted) |  |  | Runtime | 
 | Y | U | V | PsnrY | PsnrU | PsnrV | weighted | Reference | Tested | Diff (%) | Reference | Tested | Diff (%) | EncT | DecT
Class H1 | -11.88% | -67.94% | -54.94% | 3.18% | -59.75% | -49.11% | 17.36% | 1.21 | 1.37 | 13.24% | 0.92 | 1.10 | 20.30% | 2863% | 178%
Class H2 | -22.45% | -49.20% | -49.99% | -8.05% | -39.58% | -40.39% | 18.52% | 1.21 | 1.41 | 16.53% | 0.94 | 1.15 | 22.00% | 3356% | 158%
Overall | -17.17% | -58.57% | -52.47% | -2.43% | -49.67% | -44.75% | 17.94% | 1.21 | 1.39 | 14.89% | 0.93 | 1.13 | 21.16% | 3100% | 168%

## Slide 5: Results for Low QPs (Anchor=HM-16.23, Tested=VTM-13.0)
Compared to the normal QPs,
  BD-bitrate and BD-bin rate are significantly degraded.
  Weighted bin-to-bit ratio (or Delta Binrate) of VVC is higher than HEVC’s for PQ and HLG except ultra high bitrate like SVT12 and SVT16.
 |  |  | AI |  |  |  |  |  |  |  |  |  |  |  | 
 | BD-bitrate |  |  | BD-binrate (average, weighted) |  |  | Delta Binrate (average) | Bin2Bit (peak, unweighted) |  |  | Bin2Bit (peak, weighted) |  |  | Runtime | 
 | psnrY/G | psnrU/B | psnrV/R | PsnrY/G | PsnrU/B | PsnrV/R | weighted | Reference | Tested | Diff (%) | Reference | Tested | Diff (%) | EncT | DecT
PQ | -8.61% | -11.28% | -11.96% | 7.71% | 5.00% | 4.23% | 15.21% | 1.19 | 1.27 | 6.35% | 0.75 | 0.88 | 17.77% | 3150% | 163%
HLG | -4.95% | -7.32% | -7.49% | 3.75% | 1.79% | 1.48% | 7.30% | 1.20 | 1.24 | 2.72% | 0.71 | 0.78 | 10.75% | 3792% | 165%
SVT12 | -4.26% | -3.69% | -3.79% | -3.67% | -3.28% | -3.35% | -1.10% | 1.22 | 1.17 | -4.44% | 0.57 | 0.58 | 1.04% | 5911% | 144%
SVT16 | -2.36% | -1.56% | -1.58% | 0.14% | 0.64% | 0.63% | 1.61% | 1.19 | 1.16 | -2.84% | 0.46 | 0.47 | 2.47% | 6249% | 154%
 |  |  | LDB |  |  |  |  |  |  |  |  |  |  |  | 
 | BD-bitrate |  |  | BD-binrate (average, weighted) |  |  | Delta Binrate (average) | Bin2Bit (peak, unweighted) |  |  | Bin2Bit (peak, weighted) |  |  | Runtime | 
 | psnrY/G | psnrU/B | psnrV/R | PsnrY/G | PsnrU/B | PsnrV/R | weighted | Reference | Tested | Diff (%) | Reference | Tested | Diff (%) | EncT | DecT
PQ | -7.34% | -8.38% | -9.52% | 6.41% | 5.31% | 4.27% | 13.04% | 1.18 | 1.25 | 5.36% | 0.73 | 0.86 | 18.30% | 416% | 178%
HLG | -5.74% | -8.91% | -7.84% | 3.32% | 0.25% | 1.04% | 7.57% | 1.20 | 1.24 | 3.60% | 0.71 | 0.80 | 12.34% | 497% | 151%
SVT12 | -4.46% | -2.12% | -2.10% | -4.27% | -2.88% | -2.87% | -1.77% | 1.22 | 1.17 | -4.48% | 0.56 | 0.57 | 1.10% | 675% | 126%
SVT16 | -2.29% | -0.78% | -0.77% | -0.52% | 0.35% | 0.36% | 0.81% | 1.19 | 1.16 | -2.61% | 0.45 | 0.47 | 2.84% | 721% | 137%
 |  |  | RA |  |  |  |  |  |  |  |  |  |  |  | 
 | BD-bitrate |  |  | BD-binrate (average, weighted) |  |  | Delta Binrate (average) | Bin2Bit (peak, unweighted) |  |  | Bin2Bit (peak, weighted) |  |  | Runtime | 
 | psnrY/G | psnrU/B | psnrV/R | PsnrY/G | PsnrU/B | PsnrV/R | weighted | Reference | Tested | Diff (%) | Reference | Tested | Diff (%) | EncT | DecT
PQ | -7.54% | -8.66% | -9.46% | 6.51% | 5.30% | 4.52% | 13.53% | 1.19 | 1.23 | 3.66% | 0.70 | 0.82 | 17.40% | 508% | 176%
HLG | -6.24% | -9.32% | -8.09% | 3.03% | -0.05% | 0.92% | 7.91% | 1.20 | 1.23 | 2.42% | 0.69 | 0.77 | 11.74% | 594% | 151%
SVT12 | -4.72% | -2.32% | -2.30% | -3.86% | -2.41% | -2.41% | -1.19% | 1.23 | 1.17 | -4.88% | 0.55 | 0.56 | 0.58% | 879% | 137%
SVT16 | -2.40% | -0.95% | -0.94% | -0.28% | 0.56% | 0.56% | 1.11% | 1.18 | 1.15 | -2.68% | 0.45 | 0.46 | 2.34% | 914% | 132%

## Slide 6: Summary
This contribution gave you an information of study on VVC bin to bit ratio.
Lower coding performance at low QPs
  Need to further improve coding performance of VVC for high bit depth coding ?
Weighted peak bin to bit ratio for low QPs
  A higher bin to bit ratio generally requires a higher throughput CABAC engine for real time decoding
  VVC’s is generally higher than HEVC’s for PQ and HLG cases except ultra high bitrate like SVT12 & SVT16.
  Need to improve CABAC throughput ?
Lower weighted BD-binrate for low QPs
  For the same PSNR values, VVC generally consumes more bins than HEVC for PQ & HLG cases except ultra high bit rate like SVT12 & SVT16.
  Need to improve coding performance of VVC or reduce its bin rate ?
It is recommended to study VVC CABAC throughput for high bit depth coding.