## Slide 1: AHG8: On significance, GT1, and GT2 flag coding for high bit depths
JVET-X0136
Sony Europe BV.
Adrian Browne, Steve Keating, Karl Sharman
Sony Group Corp.

## Slide 2: Introduction
JVET-W0093 “AHG8: On significance, GT1, and GT2 flag coding for high bit depths”
  Introduced technique which modified RRC
  Reported gains for SVT-16 and lossless coding
Further work requested
  Limited normative change over JVET-W0093
  Improved non-normative algorithms including DepQuant
  Updated and extended study vs VTM 14.0

## Slide 3: Motivation for JVET-W0093
JVET-V0122 reported results for disabling the context coding of coefficient values using significance (Sig), GT1, GT2, parity flags
  Losses for PQ and HLG in low QP range
    Expected result
  Gains for SVT-16 in low QP range, and all HBD content for lossless coding
    Unexpected result
Gains for JVET-V0122 indicate
  For lossless and SVT-16 context coding offers no benefit
    More efficient to code coefficients using only Golomb-Rice
  Context coding is no longer working at these operating points
    Why?
    Can this be fixed?

## Slide 4: Analysis of VTM 14.0
SVT-12 OldTownCross
AI (TransformSkip=0)
SVT-16 OldTownCross
AI (TransformSkip=0)
As QPs drop coefficients increase in magnitude
  Percentage of Sig, GT1 and GT2 flags set to 1 increases
    Over 90% for all three flags below QP -8
  Flags will be efficiently coded
  Flags provide little information on coefficient value
Percentage of Sig, GT1 and GT2 flags set to 1

## Slide 5: Analysis of VTM 14.0
Number of coefficients coded with context-coded flags
Below QP 22, number of coefficients coded with content-coded bins decreases
  Limit of context-coded bins reached so must share between Sig, GT1, GT2, parity
  Number of coefficients requiring Golomb-Rice coding increases
    Very few coefficients coded with just context-coded bins at very low QPs
SVT-12 OldTownCross
AI (TransformSkip=0)
SVT-16 OldTownCross
AI (TransformSkip=0)

## Slide 6: Analysis of VTM 14.0
SVT-12 OldTownCross
AI (TransformSkip=0)
SVT-16 OldTownCross
AI (TransformSkip=0)
Number of coded bins
Below QP 22, number of context-coded bins is near / at limit
At low QPs (below about QP 12)
  Number of escape coded (Golomb-Rice) bins increases almost linearly
  Number of other EP bins is almost constant
  Golomb-Rice coded bins dominate bin usage

## Slide 7: Aims of modification
Reduce percentage of significance, GT1 and GT2 flags set to 1
  Increase number of coefficients coded using context-coded bins
    Less GT1, GT2 and parity flags required
  Reduce number of coefficients requiring Golomb-Rice coding
Make bin usage more consistent for a range of operating points
  Currently different demands at different QPs
    At low QPs Golomb-Rice coding dominates
    At higher QPs (10 bit range) context-coded bin coding dominates
No need to reduce quantity of context-coded bins for coefficients
  No significant increase below QP 22
    Reaches limit

## Slide 8: Modification
Separate coding of MSBs and LSBs
Sig, GT1, GT2 and parity used for sub-block coding of MSBs
  No change from VVC
LSBs coded at end of block
Value reconstructed by shifting left MSBs and adding LSBs
  LSBs require signs if MSBs are zero
Number of LSBs determined by encoder-side algorithm
  Signalled in slice header
  If number of LSBs is zero, coding is unchanged from VVC
Code MSBs using Sig, GT1, GT2, parity
and/or Golomb-Rice
Code LSBs as EP-bins

## Slide 9: Effect of modification - flags
Percentage of Sig, GT1 and GT2 flags set to 1
SVT-12
SVT-16

## Slide 10: Effect of modification - coefficients
SVT-12
SVT-16
Number of coefficients coded with context-coded flags

## Slide 11: Effect of modification - bins
SVT-12
SVT-16
Number of coded bins

## Slide 12: Effect of modification - summary
Percentage of Sig, GT1 and GT2 flags set to 1 reduced
  Similar percentages for all simulations where technique used (QP < 12)
    Number of context-coded bins of each type similar at all QPs below this point
    More consistent numbers may aid CABAC engine
Number of coefficients coded with flags increased
  Number of coefficients requiring Golomb-Rice coding reduced
    Quantity of Golomb-Rice coding no longer increases with QP
Total number of EP-bins reduced
  Number of Golomb-Rice (escape) coded bins reduced
    Similar number at all QPs when technique used
  Suggest new LSB coded bins impose less workload than escape coding
Number of context-coded bins little changed

## Slide 13: Results – Lossless vs VTM
PQ | All Intra |  |  | Low delay B |  |  | Random Access |  | 
 | ratio |  | bit-rate savings | ratio |  | bit-rate savings | ratio |  | bit-rate savings
 | VTM14.0 | SigGt1Gt2Shift |  | VTM14.0 | SigGt1Gt2Shift |  | VTM14.0 | SigGt1Gt2Shift | 
PQ444 | 2.6 | 2.6 | -0.17% | 3.1 | 3.1 | -0.21% | 3.1 | 3.1 | -0.20%
PQ422 | 2.4 | 2.4 | -0.23% | 2.9 | 2.9 | -0.26% | 2.9 | 2.9 | -0.28%
Overall | 2.5 | 2.5 | -0.20% | 3.0 | 3.0 | -0.24% | 3.0 | 3.0 | -0.24%
Enc Time[%] | 96% |  |  | 98% |  |  | 101% |  | 
Dec Time[%] | 97% |  |  | 98% |  |  | 101% |  | 
HLG | All Intra |  |  | Low delay B |  |  | Random Access |  | 
 | ratio |  | bit-rate savings | ratio |  | bit-rate savings | ratio |  | bit-rate savings
 | VTM14.0 | SigGt1Gt2Shift |  | VTM14.0 | SigGt1Gt2Shift |  | VTM14.0 | SigGt1Gt2Shift | 
HLG444 | 1.8 | 1.8 | -0.80% | 2.0 | 2.0 | -0.86% | 2.0 | 2.0 | -0.86%
HLG422 | 1.7 | 1.7 | -0.85% | 1.9 | 2.0 | -0.99% | 1.9 | 2.0 | -0.98%
Overall | 1.7 | 1.8 | -0.83% | 2.0 | 2.0 | -0.92% | 2.0 | 2.0 | -0.92%
Enc Time[%] | 101% |  |  | 102% |  |  | 100% |  | 
Dec Time[%] | 99% |  |  | 101% |  |  | 99% |  | 
SVT | All Intra |  |  | Low delay B |  |  | Random Access |  | 
 | ratio |  | bit-rate savings | ratio |  | bit-rate savings | ratio |  | bit-rate savings
 | VTM14.0 | SigGt1Gt2Shift |  | VTM14.0 | SigGt1Gt2Shift |  | VTM14.0 | SigGt1Gt2Shift | 
SVT16 | 1.2 | 1.2 | -1.17% | 1.2 | 1.2 | -1.35% | 1.2 | 1.2 | -1.37%
SVT12 | 1.3 | 1.3 | -1.18% | 1.3 | 1.3 | -1.51% | 1.3 | 1.3 | -1.53%
Overall | 1.2 | 1.3 | -1.17% | 1.3 | 1.3 | -1.43% | 1.3 | 1.3 | -1.45%
Enc Time[%] | 102% |  |  | 99% |  |  | 101% |  | 
Dec Time[%] | 97% |  |  | 98% |  |  | 100% |  | 

## Slide 14: Results – VTM vs HM (for comparison)
PQ | All Intra |  |  | Low delay B |  |  | Random Access |  | 
 | ratio |  | bit-rate savings | ratio |  | bit-rate savings | ratio |  | bit-rate savings
 | HM16.23 | VTM14.0 |  | HM16.23 | VTM14.0 |  | HM16.23 | VTM14.0 | 
PQ444 | 2.5 | 2.6 | -1.58% | 3.1 | 3.1 | 1.18% | 3.1 | 3.1 | 0.96%
PQ422 | 2.3 | 2.4 | -2.72% | 2.9 | 2.9 | -0.21% | 2.9 | 2.9 | -0.36%
Overall | 2.4 | 2.5 | -2.15% | 3.0 | 3.0 | 0.49% | 3.0 | 3.0 | 0.30%
Enc Time[%] | 7610% |  |  | 1063% |  |  | 1100% |  | 
Dec Time[%] | 171% |  |  | 160% |  |  | 159% |  | 
HLG | All Intra |  |  | Low delay B |  |  | Random Access |  | 
 | ratio |  | bit-rate savings | ratio |  | bit-rate savings | ratio |  | bit-rate savings
 | HM16.23 | VTM14.0 |  | HM16.23 | VTM14.0 |  | HM16.23 | VTM14.0 | 
HLG444 | 1.8 | 1.8 | -0.95% | 1.9 | 2.0 | -0.76% | 2.0 | 2.0 | -0.83%
HLG422 | 1.7 | 1.7 | -1.40% | 1.9 | 1.9 | -1.11% | 1.9 | 1.9 | -1.18%
Overall | 1.7 | 1.7 | -1.17% | 1.9 | 2.0 | -0.94% | 1.9 | 2.0 | -1.00%
Enc Time[%] | 8084% |  |  | 1119% |  |  | 1118% |  | 
Dec Time[%] | 164% |  |  | 148% |  |  | 150% |  | 
SVT | All Intra |  |  | Low delay B |  |  | Random Access |  | 
 | ratio |  | bit-rate savings | ratio |  | bit-rate savings | ratio |  | bit-rate savings
 | HM16.23 | VTM14.0 |  | HM16.23 | VTM14.0 |  | HM16.23 | VTM14.0 | 
SVT16 | 1.2 | 1.2 | -0.43% | 1.2 | 1.2 | -0.01% | 1.2 | 1.2 | -0.06%
SVT12 | 1.3 | 1.3 | -0.75% | 1.3 | 1.3 | -0.21% | 1.3 | 1.3 | -0.27%
Overall | 1.2 | 1.2 | -0.59% | 1.3 | 1.3 | -0.11% | 1.3 | 1.3 | -0.16%
Enc Time[%] | 8781% |  |  | 1158% |  |  | 1139% |  | 
Dec Time[%] | 142% |  |  | 149% |  |  | 150% |  | 

## Slide 15: Results – SVT (Low QP)
SVT RGB |  |  | AI |  | 
 |  |  | Over VTM14.0 |  | 
 | psnrG | psnrB | psnrR | EncT | DecT
SVT16 | -0.75% | -0.77% | -0.78% | 100% | 101%
SVT12 | -0.20% | -0.19% | -0.21% | 107% | 102%
Overall | -0.47% | -0.48% | -0.50% | 104% | 101%
 |  |  | LDB |  | 
 |  |  | Over VTM14.0 |  | 
 | psnrG | psnrB | psnrR | EncT | DecT
SVT16 | -0.76% | -0.73% | -0.73% | 103% | 106%
SVT12 | -0.05% | -0.05% | -0.05% | 105% | 103%
Overall | -0.41% | -0.39% | -0.39% | 104% | 105%
 |  |  | RA |  | 
 |  |  | Over VTM14.0 |  | 
 | psnrG | psnrB | psnrR | EncT | DecT
SVT16 | -0.71% | -0.67% | -0.67% | 104% | 106%
SVT12 | -0.04% | -0.02% | -0.02% | 107% | 104%
Overall | -0.38% | -0.34% | -0.34% | 105% | 105%
Overall RGB | -0.42% | -0.41% | -0.41% | 104% | 104%

## Slide 16: Results – PQ (Low QP)
HDR PQ |  |  | AI |  |  |  |  | 
 |  |  | Over VTM14.0 |  |  |  |  | 
 | wPsnrY | wPsnrU | wPsnrV | psnrY | psnrU | psnrV | EncT | DecT
PQ444 | -0.01% | 0.02% | 0.01% | -0.01% | 0.02% | 0.01% | 104% | 99%
PQ422 | 0.00% | 0.02% | 0.02% | -0.01% | 0.02% | 0.02% | 105% | 101%
Overall | -0.01% | 0.02% | 0.02% | -0.01% | 0.02% | 0.02% | 105% | 100%
 |  |  | LDB |  |  |  |  | 
 |  |  | Over VTM14.0 |  |  |  |  | 
 | wPsnrY | wPsnrU | wPsnrV | psnrY | psnrU | psnrV | EncT | DecT
PQ444 | 0.00% | 0.00% | 0.01% | 0.00% | 0.00% | 0.01% | 103% | 100%
PQ422 | 0.03% | 0.03% | 0.04% | 0.03% | 0.03% | 0.05% | 103% | 98%
Overall | 0.02% | 0.01% | 0.03% | 0.01% | 0.01% | 0.03% | 103% | 99%
 |  |  | RA |  |  |  |  | 
 |  |  | Over VTM14.0 |  |  |  |  | 
 | wPsnrY | wPsnrU | wPsnrV | psnrY | psnrU | psnrV | EncT | DecT
PQ444 | 0.02% | 0.01% | 0.02% | 0.01% | 0.01% | 0.03% | 103% | 99%
PQ422 | 0.02% | 0.03% | 0.03% | 0.02% | 0.03% | 0.03% | 103% | 100%
Overall | 0.02% | 0.02% | 0.03% | 0.02% | 0.02% | 0.03% | 103% | 100%
Overall PQ | 0.01% | 0.02% | 0.02% | 0.01% | 0.02% | 0.02% | 104% | 100%

## Slide 17: Results – HLG (Low QP)
HDR HLG |  |  | AI |  | 
 |  |  | Over VTM14.0 |  | 
 | psnrY | psnrU | psnrV | EncT | DecT
HLG444 | -0.05% | -0.07% | -0.07% | 105% | 100%
HLG422 | -0.08% | -0.10% | -0.10% | 106% | 100%
Overall | -0.07% | -0.08% | -0.08% | 105% | 100%
 |  |  | LDB |  | 
 |  |  | Over VTM14.0 |  | 
 | psnrY | psnrU | psnrV | EncT | DecT
HLG444 | 0.01% | 0.02% | 0.02% | 104% | 101%
HLG422 | 0.02% | 0.03% | 0.01% | 103% | 99%
Overall | 0.02% | 0.02% | 0.02% | 103% | 100%
 |  |  | RA |  | 
 |  |  | Over VTM14.0 |  | 
 | psnrY | psnrU | psnrV | EncT | DecT
HLG444 | 0.02% | 0.03% | 0.03% | 104% | 100%
HLG422 | 0.02% | 0.04% | 0.04% | 103% | 100%
Overall | 0.02% | 0.03% | 0.04% | 104% | 100%
Overall HLG | -0.01% | -0.01% | -0.01% | 104% | 100%

## Slide 18: Conclusions
Described a modification to regular residual coding in VVC
  Code LSBs and MSBs separately
    MSBs coded in sub-blocks using same technique as VVC
    LSBs coded at end of block and combined with MSBs
  Results in more consistent and efficient coefficient coding
    Number of flags coded, and percentage each is set to 1
    Amount of Golomb-Rice coding
  Gains for SVT-16 and lossless coding of SVT, PQ and HLG content
Proposal may be too late for adoption VVC v2
However if VVC or a “beyond VVC” codec is to outperform HEVC for high end
  Need mechanism to allow longer-term HBD/HBR studies
    VVC v2 fixed problems rather than developing HBD specific tools
      Adopted tools similar to those in HEVC
Thanks to OPPO for cross-check (JVET-X0173)