## Slide 1: AHG12:removal of floating operations in DIMD and TIMD
Xiaoyu Xiu, Hong-Jheng Jhu, Wei Chen, Che-Wei Kuo, Ning Yan, Yi-Wen Chen, Xianglin Wang

## Slide 2: Problem statement
Floating-point operations in the DIMD and TIMD
  The derivation of gradient orientations in the DIMD
  The prediction sample blending in the DIMD
  The prediction sample blending in the TIMD

## Slide 3: Proposal
Integerization scheme for the DIMD and TIMD
  The integerization used by the CCLM is extended to replace the floating-point operations in the DMD and TIMD
    Approximating one denominator by one exponent bit and 4 following significands
    The same LUT used by the CCLM is reused, 16 elements and each element is in 3-bit precision
……
exponent
4-bit significands
DivSigTable[16] = { 0, 7, 6, 5 ,5, 4, 4, 3, 3, 2, 2, 1, 1, 1, 1, 0 }

## Slide 4: Performance evaluation

## Slide 5: Summary
  Proposal
    Extending the existing CCLM integerization to replace all the floating-point operations in the DIMD and TIMD.
    No new LUT is introduced.
    Negligible coding performance and Enc/Dec impacts.
  It is suggested to adopt the proposed scheme to ECM-3.0
  Thanks to Bytedance for the crosschecking!
 | Y | U | V | Enc | Dec
AI | 0.00% | -0.03% | -0.03% | 100% | 101%
RA | -0.01% | 0.04% | -0.04% | 100% | 101%