## Slide 1: JVET-Y0043
Baseline Low Latency, Controlled Complexity CTCs
Interdigital, Bytedance, Ektacom, Huawei, Qualcomm, Nokia, Tencent, Vitec.

## Slide 2: Proposals
Two new proposed baseline Low Latency Controlled Complexity (LLCC) CTCs
Corresponding to 5 identified scenarios and their characteristics
  cloud gaming, game casting, video surveillance, remote control of systems, video conferencing
Refine the LLCC baseline CTCs over time
  Based on a proposed process

## Slide 3
 | Cloud gaming | Game casting | Video conf. Individual stream | Video surveillance | Remote control of systems
Resolution | 720 to 4K 8K in the near future | 720 to 1080p | 720 to 1080p | 4M ~ 8M pixel, full HD the norm. 4K | Common: 1080p, 8b-12b, 4:2:0, 4:2:2, 4:4:4 YUV, 4:4:4 RGB From: 360p25 to UHD
Framerate | 30 to 120fps 60fps common | 25fps (720p) 60fps (1080p) | 30fps | 25 or 30fps | 60 fps
bitrate | 10-30Mbps on PC. Peak at 50 Mpbs. 2 to 8 on mobile CBR | 3 to 6 Mbps CBR | Up to 6Mbps | 2Mbps ~ 6Mbps for FHD, and 6Mbps ~ 12Mbps for 4K | 300kb/s (360p) to 6Mb/s Flat QP or Rate control
Known coding features | P frames simple RDO & partitionning Super resolution « Area of Interest » « GDR » Use of AU enough. | P or B frames. Nb of Ref. Frame restricted to 2. Random access every 2sec: possibly « GDR » | P or B frames. Nb of Ref. Frame restricted to 2. RPR - Resolution change. « GDR » may not be used | P or B frames (forward looking only) « Area of interest » Random access at every 2s ~ 4s: via GDR. Use of AU enough. | P frames. GDR and DU for latency RPR to deal with network capacity variation HDR
Latency/ complexity requirements | “Subframe” latency Small buffer size 50-80ms end to end latency for average gamer 20ms latency is perceived by a professional gamer Low decoder complexity (browser/hardware) |  | Low latency required: Impact of transcoding and stream aggregation No multipass encoding tools. | Low latency Low complexity for low-cost hardware design | between 40 and 300ms with a human in the loop. Between sub picture frame duration and up to 100ms with a machine in the loop. Reduced complexity for embedded video coding, including hardware assisted software coding
References | GeforceNow [1] [2] , Unity-Parsec [3], Amazon Luna [4], Vortex [5], Tencent [6], Stadia [7] Steam [8] | Twitch [9], Nvenc [2] | Webex [10] zoom [11] Nvenc [2] | Axis[12]; WesternDigital [13] | [14]

## Slide 4: LLCC CTCs
Current CTCs:
  address well offline encoding / real-time decoding mode
  “Anchor for real-time” encoding/scenarios often not the reference software
  Implementations are looking at a minimum coding efficiency of 30% BD-rate gain over “real-time anchor” with no more than doubled complexity.
  To meet complexity and latency requirements, implementations turn tools off, or partially used them, performance and visual quality suffers.
Objectives :
  A reasonable anchor and configuration for real-time / LLCC framework, scenarios and their requirements
  Allows to test tools in a variety of situations
  Enables the development of new tools to improve compression and visual quality when low latency and reduce complexity is needed.
  Particularly when “low latency” tools are used (GDR, DU, AU, limited reference frames etc)
  Not a profile, no tools are removed from the ref software/spec

## Slide 5: Baseline LLCC-1 configuration
Examplary Scenario: cloud gaming, remote control of systems, video surveillance
LLCC-1 (LD-P) | VTM | ECM
IPPP | Yes | Yes
Flat QP | Yes | Yes
QP values | Add QP 42 BD-rate calculations performed on QP22-37 and on QP 27-42. | Add QP 42 BD-rate calculations performed on QP22-37 and on QP 27-42.
“recovery/refresh” | GDR enabled every 1~2 second GdrInterval (between GDR picture to associated recovery point picture) is set to 1 second GdrPeriod (between two consecutive GDR pictures) = GdrInterval + 4 regular P pictures Disable LMCS chroma scaling during the GDR period* | IDR every 1 second  to be replace by GDR when fully implemented for the LLCC-1 toolset. Disable LMCS chroma scaling
Per class tools | Screen content tools RPR HDR | Screen content tools RPR HDR
*Chroma residual scaling depends on the average value of top and/or left reconstructed neighbouring luma samples of the current VPDU. With GDR, there are some cases where the current CU is in the clean area but the current VPDU cross the boundary between clean and dirty region, As chroma residual scaling cannot be deactivated on a per CU basis, it needs to be deactivated if GDR is enabled
It would be desirable for Tools (new or modified) that are impacted by GDR, to be provided with a GDR implementation in the LLCC1 configuration.

## Slide 6: Baseline LLCC-2 configuration
Examplary Scenario: Game casting, video conferencing
LLCC-2 (LD-B) | VTM | ECM
IBP | Yes | Yes
QP values | Add QP 42 BD-rate calculations on QP22-37 and on QP 27-42. | Add QP 42 BD-rate calculations on QP22-37 and on QP 27-42.
Number of Reference frame | Max 2 | Max 2
“recovery/refresh” | No GDR | No GDR
Per class tools | RPR for class E. one per clip | RPR for class E, one per clip

## Slide 7: Process to refine the baseline LLCC CTCs
Limit inclusion or disable tools that:
  Are inherently iterative, multi-pass or providing delays (cross-component delays, line of delays etc.)
  Have a sub-optimal implementation for LLCC conditions, e.g. increasing latency (ALF current implementation is multi-pass. )
  Have a sub-optimal gain/complexity trade-off in current LD CTCs; for instance below a threshold.
  Are known to not be used in LLCC scenario or deemed too “complex” (e.g. full search).
Proposed tools to be disabled:
  None in the baseline CTCs (except LMCS chroma scaling due to GDR, see previous slide)
  To be done over time

## Slide 8: Proposed ET/RT ratio to refine the CTCs
Define a ratio between a non-optimised single threaded reference software Encoding Time (ET) and Real time (RT)
  ET/RT provides an absolute value rather than a relative increase over previous anchor
  Not a metric for individual tools, rather for an overall configuration
Some ET/RT ratio:
Sequence(s) | HM LD-P | HM LD-B | VTM LD-P | VTM LD-B | ECM LD-P | ECM LD-B
Class E (720p): | 876/1 | 1086/1 | 2730/1 | 3774/1 | NA* | 9024/1
Class F | 756/1 | 870/1 | 3324/1 | 4224/1 | NA* | 7812/1
Class TGM (1080p) | NA | NA | 2601/1 | NA | NA | 29256/1
3GPP SA4 Gaming HD | NA | 4098/1 | NA | 14454/1 | NA | NA
3GPP SA4 Gaming HD no QP 22 | NA | 3630/1 | NA | 11592/1 | NA | NA
3GPP SA4 Gaming UHD | NA | 26760/1 | NA | 70754/1 | NA | NA
3GPP SA4 Gaming UHD no QP22. | NA | 23370/1 | NA | 56978/1 | NA | NA

## Slide 9: Proposed value for the ET/RT ratio
ET/RT value of 1000
Vvenc data:
[18] results for single threaded VVenC encoder in LD-B
Ektacom remote driving sequence at 720p25fps in LD-P
The medium preset of x265 corresponds to real-time encoding on Intel Core i9 9900K and where the VVenC version is V0.3

## Slide 10: Use of the ET/RT ratio
Using the ET/RT ratio of 1000/1
  As a starting point to refine the baseline CTCs
  Established for VVC, for 1080p, averaged over a few QPs
Proposed combination of tools to be disabled:
  None in the baseline CTCs
  To be done over time
  The “1000” value can be change, different thresholds can be used.

## Slide 11: LLCC1 -results
VTM
ECM
 | LLCC-1 (LDP) (QP22,27,32,37) |  |  |  |  |  |  | LLCC-1 (LDP) (QP27,32,37,42) |  |  |  | 
 | BD-rate Over VTM15 flat QP-IDP |  |  |  |  |  |  | BD-rate Over flat QP IDR |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | EncT | DecT |  |  | Y-PSNR | U-PSNR | V-PSNR | EncT | DecT
Class B | 2,87% | 9,52% | 13,75% | 96% | 97% |  | Class B | 5,13% | 12,52% | 15,92% | 98% | 100%
Class C | 3,70% | 9,82% | 10,83% | 96% | 105% |  | Class C | 5,17% | 14,08% | 15,40% | 96% | 101%
Class E | 11,65% | 22,99% | 23,28% | 101% | 102% |  | Class E | 17,45% | 28,80% | 29,11% | 102% | 104%
Overall | 5,34% | 12,99% | 15,16% | 97% | 101% |  | Overall | 8,22% | 17,11% | 19,04% | 98% | 101%
Class D | 4,57% | 12,28% | 12,25% | 98% | 103% |  | Class D | 6,83% | 19,27% | 17,82% | 101% | 104%
Class F | 12,52% | 18,57% | 19,48% | 107% | 104% |  | Class F | 14,39% | 21,60% | 23,16% | 108% | 104%
Class TGM | 8,71% | 9,39% | 9,40% | 112% | 104% |  | Class TGM | 9,45% | 10,35% | 10,29% | 113% | 104%
 | LLCC-1 (QP22,27,32,37) |  |  |  |  |  |  | LLCC-1 (QP27,32,37,42) |  |  |  | 
 | BD-rate Over ECM 3.1 LD-P |  |  |  |  |  |  | BD-rate Over ECM 3.1 LD-P |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | EncT | DecT |  |  | Y-PSNR | U-PSNR | V-PSNR | EncT | DecT
Class B | 9,00% | 3,43% | 2,08% | 99% | 103% |  | Class B | 11,76% | 7,31% | 6,01% | 98% | 105%
Class C | 9,49% | 3,74% | 3,29% | 96% | 99% |  | Class C | 12,09% | 5,91% | 6,66% | 94% | 99%
Class E | 28,63% | 27,27% | 25,11% | 98% | 106% |  | Class E | 36,35% | 36,30% | 34,27% | 98% | 105%
Overall | 14,07% | 9,49% | 8,24% | 98% | 102% |  | Overall | 18,02% | 14,09% | 13,29% | 97% | 103%
Class D | 9,94% | 2,23% | 3,16% | 98% | 93% |  | Class D | 13,65% | 7,14% | 8,49% | 97% | 94%
Class F | 64,87% | 65,44% | 59,43% | 110% | 113% |  | Class F | 68,47% | 69,84% | 62,28% | 109% | 110%
Class TGM | 32,16% | 31,34% | 29,21% | 121% | 113% |  | Class TGM | 33,34% | 32,54% | 30,25% | 118% | 110%

## Slide 12: LLCC-2 results
VTM
ECM
 | LLCC-2 (QP22,27,32,37) |  |  |  |  |  |  | LLCC-2 (QP27,32,37,42) |  |  |  | 
 | BD-rate Over VTM15 LD-B |  |  |  |  |  |  | BD-rate Over VTM15 LD-B |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | EncT | DecT |  |  | Y-PSNR | U-PSNR | V-PSNR | EncT | DecT
Class B | 6,13% | 8,17% | 7,91% | 84% | 99% |  | Class B | 5,00% | 6,53% | 5,70% | 82% | 97%
Class C | 8,81% | 11,80% | 11,77% | 86% | 94% |  | Class C | 8,89% | 12,12% | 12,65% | 85% | 97%
Class E | 5,71% | 4,68% | 5,98% | 86% | 101% |  | Class E | 3,84% | 2,94% | 4,05% | 87% | 105%
Overall | 6,92% | 8,51% | 8,72% | 85% | 98% |  | Overall | 6,01% | 9,02% | 8,79% | 84% | 99%
Class D | 7,11% | 9,49% | 10,98% | 90% | 108% |  | Class D | 6,62% | 8,09% | 9,71% | 88% | 109%
Class F | 8,15% | 10,43% | 10,28% | 94% | 108% |  | Class F | 7,78% | 10,27% | 10,50% | 93% | 109%
Class TGM | 10,64% | 9,87% | 9,60% | 98% | 107% |  | Class TGM | 10,43% | 9,15% | 9,10% | 97% | 109%
 | LLCC-2 (QP22,27,32,37) |  |  |  |  |  |  | LLCC-2 (QP27,32,37,42) |  |  |  | 
 | BD-rate Over ECM 3.1 LD-B |  |  |  |  |  |  | BD-rate Over ECM 3.1 LD-B |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | EncT | DecT |  |  | Y-PSNR | U-PSNR | V-PSNR | EncT | DecT
Class B | 5,12% | 6,57% | 6,73% | 78% | 100% |  | Class B | 4,39% | 5,31% | 4,85% | 79% | 102%
Class C | 9,86% | 13,39% | 13,01% | 87% | 105% |  | Class C | 9,64% | 14,53% | 13,37% | 86% | 105%
Class E | 4,57% | 4,21% | 4,21% | 76% | 108% |  | Class E | 3,55% | 2,83% | 3,42% | 78% | 105%
Overall | 6,56% | 8,25% | 8,19% | 81% | 104% |  | Overall | 5,93% | 9,41% | 8,64% | 81% | 104%
Class D | 6,69% | 8,07% | 6,92% | 85% | 102% |  | Class D | 5,65% | 6,24% | 5,41% | 83% | 100%
Class F | 9,56% | 11,14% | 11,46% | 87% | 112% |  | Class F | 8,64% | 10,44% | 10,73% | 87% | 109%
Class TGM | 9,86% | 9,83% | 9,74% | 96% | 111% |  | Class TGM | 9,70% | 9,31% | 9,41% | 95% | 109%