## Slide 1
JVET-Y0103
AHG9: Down-sample phase indication (SEI message)
Philippe Bordes, Philippe de Lagrange, Edouard François

## Slide 2
Signaling down-sampling phase
  Rationale:
  Down-sampling commonly used for adapting bit-streams to available bandwidth (MPEG-DASH, VVC RPR…).
  One should ensure that the receivers appropriately display (up-sample) the decoded video, seamlessly across different down-sampling ratio
  => need to know the phases that have been used when creating the down-sampled video
  Problems raised with previous proposals (JVET-X0092):
  - The luma and chroma can have a phase shift in down-sampling, and they may be different.
  - The chroma location type would also have an impact on the correct down-sampling filter phase to be used for chroma.
  => signal chroma H/V collocated flag, both in original and down-scaled pictures
  Higher precision in specifying the phase value (the syntax “co-sited/centered” which is well adapted to 2:1 down-sampling ratio doesn’t handle cases with other phases such as ¼ phase, useful for other down-sampling ratios typically). Allow different positions for horizontal and vertical direction.
  => signal H/V phase shift at grid resolution of 8 phase positions

## Slide 3
Signaling down-sampling phase
  Problems raised with previous proposals (continue):
  The syntax should indicate (or allow to derive) the down-sampling ratio so that the decoder can inversely up-sample with the right ratio.
  => signal original picture size
  the grid phase (1/8) is defined in the original picture size, the phase shift corresponds to the top-left sample,
  in VVC, SPS max picture size may be the default original picture size

## Slide 4
Signaling down-sampling phase
  Problems raised with previous proposals (continue):
  - The syntax should be applicable to AVC, HEVC and VVC. In the case of VVC, several PPS may be present in bit-stream, with potentially different picture sizes and down-sampling phases.
  => signal phase shift and down-sampled chroma collocated flags for all PPS
  in case of AVC, HEVC only one instance is sufficient

## Slide 5
Signaling down-sampling phase