## Slide 1: JVET-Y0104 Transparency information SEI for transparent screens
E.Thomas, P.Andrivon, F.Le Léannec, M.-L. Champel

## Slide 2: Outline
What transparent screen technologies are
Use cases for a high-quality viewing experience
SEI signaling for on-device content adaptation
Simulation results

## Slide 3: 1. What transparent screen technologies are
Sources: Discover - Mi Global Home #MiTVLUX Transparent Edition - YouTube
Mi TV LUX Transparent Edition (2020)
The viewer sees a floating image
Other mass market models: Panasonic TP-55ZT100, LG 55EW5G-V

## Slide 4: 1. What transparent screen technologies are
A transparent screen is roughly made of
  a regular screen
  “punched” with many holes to let the light goes through it
  Optional back panel to block the light
Perceived transparency
  For OLED, transparent is black (no emitted light)
  For LCD, transparent is white (no back light blocked)
  Also depends on ambient lighting
White pixels
Black pixels
Source: Planar® LookThru™ Transparent OLED Display Content Developer’s Guide

## Slide 5: 2. Enabling a high-quality viewing experience
The three main objectives are:
Prevent important parts of the image to be lost (e.g. logos, …)
Enable consistent display across different screen types
Allow display adaptation based on ambient lighting conditions

## Slide 6: 2. Enabling a high-quality viewing experience
For the use cases of:
Video communication
Video content (TV, sport, movies, etc…)
User interfaces

## Slide 7: 2. Enabling a high-quality viewing experience
How does this relate to alpha channel and related SEI?
  It looks similar but concepts are different.
    Alpha blending : f(B, F, A) -> D
    Transparency adjustment: f(I, A) -> D
  Both concepts can be combined e.g.:
    A logo and a picture are blended.
    The picture is adjusted for transparency keeping the logo visible.
  Alpha blending composition is pre-determined while transparency adjustment also depends on ambient lighting.
Alpha channel concept isn’t suited for transparent screen.

## Slide 8: 3. SEI for on-device content adaptation
Proposal: New SEI message for VSEI specification.
Metadata to identify the area in the decoded pictures meant to be transparent and opaque on a transparent screen.
Metadata expressed as a mask.
Enable post-decoding adaption on the device to match expected transparency signalled in the mask.

## Slide 9: 3. SEI for on-device content adaptation
Benefits of using SEI messages
  Lightweight design (CPU for mask handling, hardware for video decoding)
  Not specific to one codec (could be used with xVC)
  No need to transcode legacy content
  Metadata present as close as possible from the video data for the post-decoding operation
Measures to mitigate bitrate increase
  Persistence of the signalled mask for several consecutive coded pictures
  Mask with smaller resolution than the coded video sequence
  Optional run-length encoding for encoding the mask values

## Slide 10: 3. SEI for on-device content adaptation
Mask size if different from luma resolution
Compressed signalling with run-length encoding
Uncompressed signalling of mask values

## Slide 11: 3. SEI for on-device content adaptation

## Slide 12: 3. SEI for on-device content adaptation
Post-processing operation
  Does it need to be normative? Probably not.
  Different models may have different approaches to translate the transparency effect (back panel, light sensor available, brightness adaptation, etc… )
  Implementor may decided to apply it in RGB or YCbCr domain.
Example process (for luma samples)

## Slide 13: 4. Simulation results
Goal
  Estimate the order of magnitude of bitrate increase for such a SEI.
Steps
  Selection a test sequence.
  Manual extraction of a 8-bit mask based on the first picture.
  Creation of mask with half resolution.
  Count of the number of bits using RLE as proposed in the SEI for both masks.
  Assuming one mask per picture, calculate number of bits for the compressed mask times framerate.

## Slide 14: 4. Simulation results
Sequence | Resolution | Frame rate | Mask resolution | Mask uncompressed size (bits) | Mask compressed size (bits) | Ratio | Simulated mask bitrate (kbits/s)
Johnny | 1280x720 | 60 | 1280x720 | 7 372 800 | 287 177 | 96,1% | 17 231
Johnny | 1280x720 | 60 | 640x360 | 1 843 200 | 92 310 | 95,0% | 5 599
First picture
Mask
Possible adjusted picture

## Slide 15: 4. Simulation results
Sequence | Resolution | Frame rate | Mask resolution | Mask uncompressed size (bits) | Mask compressed size (bits) | Ratio | Simulated mask bitrate (kbits/s)
Desktop | 1920x1080 | 60 | 1920x1080 | 16 588 800 | 55 597 | 99,7% | 3 336
Desktop | 1920x1080 | 60 | 960x540 | 4 147 200 | 47 743 | 98,8% | 2 865
First picture
Mask
Possible adjusted picture

## Slide 16: 4. Simulation results
Sequence | Resolution | Frame rate | Mask resolution | Mask uncompressed size (bits) | Mask compressed size (bits) | Ratio | Simulated mask bitrate (kbits/s)
BasketballDrive | 1920x1080 | 50 | 1920x1080 | 16 588 800 | 301 124 | 98% | 15 056
BasketballDrive | 1920x1080 | 50 | 960x540 | 4 147 200 | 106 807 | 97,4% | 5 340
First picture
Mask
Possible adjusted picture

## Slide 17: 4. Simulation results
Sequence | Resolution | Frame rate | Mask resolution | Mask uncompressed size (bits) | Mask compressed size (bits) | Ratio | Simulated mask bitrate (kbits/s)
Johnny | 1280x720 | 60 | 1280x720 | 7 372 800 | 287 177 | 96,1% | 17 231
Johnny | 1280x720 | 60 | 640x360 | 1 843 200 | 92 310 | 95,0% | 5 599
Desktop | 1920x1080 | 60 | 1920x1080 | 16 588 800 | 55 597 | 99,7% | 3 336
Desktop | 1920x1080 | 60 | 960x540 | 4 147 200 | 47 743 | 98,8% | 2 865
BasketballDrive | 1920x1080 | 50 | 1920x1080 | 16 588 800 | 301 124 | 98% | 15 056
BasketballDrive | 1920x1080 | 50 | 960x540 | 4 147 200 | 106 807 | 97,4% | 5 340
With 1 picture = 1 mask, higher frame rate means high bitrate
½ resolution gives about 3x gain for Johnny and BasketballDrive
Spatial downsampling and message persistence bring reasonable bitrates

## Slide 18: 4. Conclusion
Transparent displays mature technologies on mass market.
Conventional video content displayed on a transparent display can result in a degraded experience for the viewer.
Additional metadata needed to enable high-quality viewing experience.
SEI signalling offers lightweight design with on-device adaptation.
Proposed as new SEI message for VSEI.