## Slide 1: JVET-Z0063 Fix for parsing of MHP information in ECM
Ruoyang Yu

## Slide 2: Problem statement
Parsing issue present in ECM-4.0
  Bitstreams are not decodable if using “BcwFast = 0”
…
mh_pred_data ()
…
mvd_coding ()
…
affine_amvr_mode()
…
if (PresenceOfMhpData == 0)
mvsd_data() (i.e., mvsd_idx: the templated-based mvd sign derivation Y0067 )
mh_pred_data () {
…
if ( !pu.mergeFlag && pu.cu->affine&& pu.cu->imv ) { return;}
…
MultiHypothesisFlag() (where MHP data is further parsed, and PresenceOfMhpData is determined)
}
affine_amvr_mode() {
…
if (NonZeroMvdPresent)
amvr_flag (also amvr_precision_idx, where the pu.cu->imv is parsed and set)
}
mvd_coding() {
…
mvd_magnitude_info() (abs_mvd_greater0_flag[0/1] etc.)
if ( PresenceOfMhpData == 1 )
mvd_sign_info() (mvd_sign_flag[ 0/1 ])
}

## Slide 3: Proposal
Proposes to adjust parsing of related syntax elements
…
mvd_coding ()
…
affine_amvr_mode()
…
mh_pred_data ()
…
if (PresenceOfMhpData == 0)
mvsd_data() (i.e., mvsd_idx: the templated-based mvd sign derivation Y0067 )
else if ( PresenceOfMhpData == 1 )
mvd_sign_info() (mvd_sign_flag[ 0/1 ])
mh_pred_data () {
…
if ( !pu.mergeFlag && pu.cu->affine&& pu.cu->imv ) { return;}
…
MultiHypothesisFlag() (where MHP data is further parsed, and PresenceOfMhpData is determined)
}
affine_amvr_mode() {
…
if (NonZeroMvdPresent)
amvr_flag (also amvr_precision_idx, where the pu.cu->imv is parsed and set)
}
mvd_coding() {
…
mvd_magnitude_info() (abs_mvd_greater0_flag[0/1] etc.)
}

## Slide 4: Results
The proposed fix was tested under ECM RA and LDB CTC
It is confirmed that with the fix, the bitstreams are now decodable if they are encoded using “BcwFast = 0”
 | Random Access Main 10 |  |  |  | 
 | Over ECM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | 0.03% | 0.03% | 104% | 104%
Class A2 | 0.01% | -0.04% | -0.04% | 101% | 103%
Class B | 0.00% | 0.00% | 0.04% | 102% | 98%
Class C | 0.00% | 0.07% | -0.06% | 107% | 100%
Class E |  |  |  |  | 
Overall | 0.00% | 0.01% | 0.00% | 104% | 101%
Class D | 0.00% | 0.01% | -0.02% | 112% | 104%
 | Low delay B Main10 |  |  |  | 
 | Over ECM-4.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.06% | 0.24% | -0.11% | 104% | 101%
Class C | -0.04% | 0.25% | -0.08% | 100% | 106%
Class E | -0.06% | 0.17% | -0.46% | 100% | 105%
Overall | -0.01% | 0.22% | -0.19% | 102% | 104%
Class D | -0.02% | 0.25% | 0.40% | 96% | 98%

## Slide 5: Conclusion
It is noted that there exists a parsing issue related to MHP in ECM
  The issue can be triggered using CTC configuration but with “BcwFast = 0”
A fix to the parsing issue is proposed
  The fix adjusts the parsing order of related syntax elements
    Existing tool dependencies are kept
    It is asserted that careful study is needed to identify whether to remove a certain tool dependency
  It is suggested to include the fix into next version of ECM
Thanks to Qualcomm for cross-checking