## Slide 1: EE1-related: Reduced complexity NN loop filter and ablation study JVET-Z0106
Jacob Ström, Du Liu, Mitra Damghanian, Kenneth Andersson, Yun Li, Per Wennersten and Ruoyang Yu,
Ericsson
Jacob Ström
Ericsson
2022-04-20

## Slide 2: Ablation study of NN loopfilter
We wanted to investigate questions such as
  How much does training time affect BD-rate results?
  What happens when we remove input X from NN loop filter?

## Slide 3: Based on JVET-Y0143 (EE1-1.6)
We based our experiments on JVET-Y0143. This has four models:
  Intra-luma model
  Intra-chroma model
  Inter-luma model
  Inter-chroma model
Used for I-slices
Used for B-slices

## Slide 4: Based on JVET-Y0143 (EE1-1.6)
We based our experiments on JVET-Y0143. This has four models:
  Intra-luma model <-- retrained
  Intra-chroma model <- untouched
  Inter-luma model <- untouched
  Inter-chroma model <- untouched
The untouched models are just copied from the directory of JVET-Y0143 (EE1-1.2 Y-meeting)
We concentrated on the BDR performance for the AI configuration
Used for I-slices
Used for B-slices

## Slide 5: Test from Section 2.1: Retraining
We wanted to see if we could reproduce the AI results from JVET-Y0143 of -7.39% (BDR-Y)
After 155 epochs we reached -7.38%
  This took 60 hours
  JVET-Y0143 also took 60 hours, however results are probably not comparable:
    Not same GPU (we used faster A100, not V100)
    We used one GPU, not two
    We used different training scripts
    We used different training data extraction (qps 20, 25, 30, 35, 40 instead of 17, 22, 27, 32, 37, 42)
    Different number of epochs (155 rather than 90)
    Our timing of 60 h is estimated “best case” if we were alone on the GPU (often shared)

## Slide 6: Test from Section 2.2: Longer Retraining (reference network)
We wanted to see if BDR-Y would improve if training longer
Trained for 378 epochs instead of 155 epochs
  BDR-Y improved from -7.38% to -7.57% (delta -0.19%)
This took 146 hours instead of 60 hours.

## Slide 7: Structure of network in JVET-Y0143
head
input

## Slide 8: Structure of network in JVET-Y0143
head
Residual block 0
input

## Slide 9: Structure of network in JVET-Y0143
head
Residual block 0
Residual block 1
…
Residual block 7
input

## Slide 10: Structure of network in JVET-Y0143
head
Residual block 0
Residual block 1
…
Residual block 7
tail
input

## Slide 11: Structure of network in JVET-Y0143
head
Residual block 0
Residual block 1
…
Residual block 7
tail
mix with rec.
input
to ALF

## Slide 12: Structure of network in JVET-Y0143
head
Residual block 0
Residual block 1
…
Residual block 7
tail
mix with rec.
input
to ALF

## Slide 13: Structure of network in JVET-Y0143
head
Residual block 0
Residual block 1
…
Residual block 7
tail
mix with rec.
input
to ALF
What happens when we:
  Remove partitioning input

## Slide 14: Structure of network in JVET-Y0143
head
Residual block 0
Residual block 1
…
Residual block 7
tail
mix with rec.
input
to ALF
What happens when we:
  Remove partitioning input
  Remove boundary strength input

## Slide 15: Structure of network in JVET-Y0143
head
Residual block 0
Residual block 1
…
Residual block 7
tail
mix with rec.
input
to ALF
What happens when we:
  Remove partitioning input
  Remove boundary strength input
  Remove both partitioning and boundary strength

## Slide 16: Structure of network in JVET-Y0143
head
Residual block 0
Residual block 1
…
Residual block 7
tail
mix with rec.
input
to ALF
What happens when we:
  Remove partitioning input
  Remove boundary strength input
  Remove both partitioning and boundary strength
  Remove prediction

## Slide 17: Structure of network in JVET-Y0143
head
Residual block 0
Residual block 1
…
Residual block 7
tail
mix with rec.
input
to ALF
What happens when we:
  Remove partitioning input
  Remove boundary strength input
  Remove both partitioning and boundary strength
  Remove prediction
  Remove attention from every residual block but the last

## Slide 18: Structure of network in JVET-Y0143
head
Residual block 0
Residual block 1
…
Residual block 7
tail
mix with rec.
input
to ALF
What happens when we:
  Remove partitioning input
  Remove boundary strength input
  Remove both partitioning and boundary strength
  Remove prediction
  Remove attention from every residual block but the last
  Remove attention completely

## Slide 19: Structure of network in JVET-Y0143
head
Residual block 0
Residual block 1
…
Residual block 7
tail
mix with rec.
input
to ALF
What happens when we:
  Remove partitioning input
  Remove boundary strength input
  Remove both partitioning and boundary strength
  Remove prediction
  Remove attention from every residual block but the last
  Remove attention completely

## Slide 20: Structure of network in JVET-Y0143
head
Residual block 0
Residual block 1
…
Residual block 7
tail
mix with rec.
input
to ALF
What happens when we:
  Remove partitioning input
  Remove boundary strength input
  Remove both partitioning and boundary strength
  Remove prediction
  Remove attention from every residual block but the last
  Remove attention completely
  Have fewer residual blocks
4 instead of 8

## Slide 21: Structure of network in JVET-Y0143
head
Residual block 0
Residual block 1
…
Residual block 7
tail
mix with rec.
input
to ALF
What happens when we:
  Remove partitioning input
  Remove boundary strength input
  Remove both partitioning and boundary strength
  Remove prediction
  Remove attention from every residual block but the last
  Remove attention completely
  Have fewer residual blocks
  Have more residual blocks
16 instead of 8

## Slide 22: Test from Section 2.3.1: No partitioning
We wanted to see if BDR-Y would deteriorate if removing the partitioning input
Trained for 378 epochs
  BDR-Y at -7.57%. Same as the reference of -7.57%
  This took 138 hours instead of 146 hours.
Complexity for intra luma model only:
  418 kMACs/sample instead of 429 kMACs/sample
Compleity for intra luma+chroma:
  638 kMACs/sample instead of 649 kMACs/sample
Memory requirements for all four models (intra-luma, intra-chroma, inter-luma, inter-chroma)
  24.89 106 bytes instead of 24.94 106 bytes

## Slide 23: Test from Section 2.3.2: No boundary strength input
We wanted to see if BDR-Y would deteriorate if removing the boundary strength input
Trained for 378 epochs
  BDR-Y at -7.56%. Close to the reference of -7.57%
  This took 138 hours instead of 146 hours.
Complexity for intra luma model only:
  418 kMACs/sample instead of 429 kMACs/sample
Compleity for intra luma+chroma:
  638 kMACs/sample instead of 649 kMACs/sample
Memory requirements for all four models (intra-luma, intra-chroma, inter-luma, inter-chroma)
  24.89 106 bytes instead of 24.94 106 bytes

## Slide 24: Test from Section 2.3.3: Neither partitioning nor boundary strength input
We wanted to see if BDR-Y would deteriorate if removing both the partitioning input and the boundary strength input
Trained for 378 epochs
  BDR-Y at -7.42%. Reference at -7.57%
  This took 131 hours instead of 146 hours.
Complexity for intra luma model only:
  407 kMACs/sample instead of 429 kMACs/sample
Compleity for intra luma+chroma:
  628 kMACs/sample instead of 649 kMACs/sample
Memory requirements for all four models (intra-luma, intra-chroma, inter-luma, inter-chroma)
  24.84 106 bytes instead of 24.94 106 bytes

## Slide 25: Test from Section 2.3.4: No prediction input
We wanted to see if BDR-Y would deteriorate if removing the prediction input
Trained for 378 epochs
  BDR-Y at -7.35%. Reference at -7.57%
  This took 138 hours instead of 146 hours.
Complexity for intra luma model only:
  418 kMACs/sample instead of 429 kMACs/sample
Compleity for intra luma+chroma:
  638 kMACs/sample instead of 649 kMACs/sample
Memory requirements for all four models (intra-luma, intra-chroma, inter-luma, inter-chroma)
  24.89 106 bytes instead of 24.94 106 bytes

## Slide 26: Test from Section 2.4: Making the network shallower
We wanted to see if BDR-Y would deteriorate if removing half of the residual blocks
Trained for 378 epochs
  BDR-Y at -6.67%. Reference at -7.57%
  This took 131 hours instead of 146 hours.
Complexity for intra luma model only:
  261 kMACs/sample instead of 429 kMACs/sample
Compleity for intra luma+chroma:
  481 kMACs/sample instead of 649 kMACs/sample
Memory requirements for all four models (intra-luma, intra-chroma, inter-luma, inter-chroma)
  22.26 106 bytes instead of 24.94 106 bytes

## Slide 27: Test from Section 2.5: Making the network deeper
We wanted to see if BDR-Y would deteriorate if removing half of the residual blocks
Trained for 378 epochs
  BDR-Y at -8.28%. Reference at -7.57%
  This took 235 hours instead of 146 hours.
Complexity for intra luma model only:
  765 kMACs/sample instead of 429 kMACs/sample
Compleity for intra luma+chroma:
  985 kMACs/sample instead of 649 kMACs/sample
Memory requirements for all four models (intra-luma, intra-chroma, inter-luma, inter-chroma)
  30.31 106 bytes instead of 24.94 106 bytes

## Slide 28: Test from Section 2.6: Removing the attention from all but the last residual block
We wanted to see if BDR-Y would deteriorate if removing most of the attention
Trained for 378 epochs
  BDR-Y at -7.56%. Reference at -7.57%
  This took 132 hours instead of 146 hours.
Complexity for intra luma model only:
  426 kMACs/sample instead of 429 kMACs/sample
Compleity for intra luma+chroma:
  646 kMACs/sample instead of 649 kMACs/sample
Memory requirements for all four models (intra-luma, intra-chroma, inter-luma, inter-chroma)
  24.89 106 bytes instead of 24.94 106 bytes

## Slide 29: Test from Section 2.7: Removing attention from all residual blocks
We wanted to see if BDR-Y would deteriorate if removing most of the attention
Trained for 378 epochs
  BDR-Y at -7.58%. Reference at -7.57%
  This took 132 hours instead of 146 hours.
Complexity for intra luma model only:
  426 kMACs/sample instead of 429 kMACs/sample
Compleity for intra luma+chroma:
  646 kMACs/sample instead of 649 kMACs/sample
Memory requirements for all four models (intra-luma, intra-chroma, inter-luma, inter-chroma)
  24.89 106 bytes instead of 24.94 106 bytes

## Slide 30: Summary of all experiments
Section in contr. | Test | BDR-Y (AI) | Inputs used | kMACs per sample (Y) | kMACs per pixel (YUV) | Epochs trained | Training time (h)
 | JVET-Y0143 | -7.39% | rec, pred, part, BS, QP | 429 | 649 | 90 | 60
2.1 | Retrain 60 h | -7.38% | rec, pred, part, BS, QP | 429 | 649 | 155 | 60
2.2 | Retrain 143 h | -7.57% | rec, pred, part, BS, QP | 429 | 649 | 378 | 146
2.3.1 | Without part | -7.57% | rec, pred, BS, QP | 418 | 638 | 378 | 138
2.3.2 | Without BS | -7.56% | rec, pred, part, QP | 418 | 638 | 378 | 138
2.3.3 | Without part and BS | -7.42% | rec, pred, QP | 407 | 628 | 378 | 131
2.3.4 | Without pred | -7.35% | rec, part, BS, QP | 418 | 638 | 378 | 138
2.4 | 4 res. blocks | -6.67% | rec, pred, part, BS, QP | 261 | 481 | 378 | 131
2.5 | 16 res. blocks | -8.28% | rec, pred, part, BS, QP | 765 | 985 | 378 | 234
2.6 | Attention only at last res. block | -7.56% | rec, pred, part, BS, QP | 426 | 646 | 378 | 132
2.7 | No Attention | -7.58% | rec, pred, part, BS, QP | 426 | 646 | 378 | 132

## Slide 31: Possible Interpretation
Neural network training is stochastic in its nature.
  If we retrain from scratch 10 times, what is the spread? We don’t know.
  Thus it is hard to know what is a statistically significant result.
  This study says nothing about the inter model or about chroma
However, the result still suggest that
  Partitioning or BS can potentially be removed without hurting AI-BDR-Y much
  Removing both is potentially harmful
  Attention can potentially be removed without hurting AI-BDR-Y much

## Slide 33: Structure of network in JVET-Y0143
head
Residual block 0
Residual block 1
…
Residual block 7
tail
mix with rec.
input
to ALF