## Slide 1
Woong Lim
JVET-AA0053
AHG12: Using block vector derived from IntraTMP for IBC

## Slide 2: Summary
Motivation
  In ECM-5.0, IntraTMP block vector (BV) can be simply stored, but it is not exploited in the IBC mode despite IntraTMP BV can be added to IBC BV candidate list to improve coding efficiency.
Proposed Method
  To use BVs from IntraTMP as spatial candidates for IBC mode.
Experimental Results
  AI: -0.13% for class F, -0.17% for TGM
  RA: -0.06% for class F, -0.04% for TGM

## Slide 3: Proposed method
IntraTMP BVs are stored in IBC BV buffer and added to IBC BV candidate list.
  In IntraTMP mode, BVs are simply stored.
  In IBC mode, IntraTMP BVs are added to IBC BV candidate list as spatial candidates.
Cur
block
Template
intraTMP BV
Ref
block
Best matching
Template
Reconstructed area
BVIBC | BVIBC | BVIBC | …
IBC BV candidate list
BVIBC | BVintraTMP | BVIBC | …
IBC BV candidate list
Figure 1. Derivation of IntraTMP BV
Figure 2. Examples of IBC BV candidate list existing (a) only IBC BVs and (b) both IBC and IntraTMP BVs
(a)
(b)

## Slide 4: Experimental results
Anchor: ECM-5.0 under CTC
 | All Intra Main 10 |  |  |  | 
 | Over ECM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | -0.13% | -0.13% | -0.13% | 100% | 99%
Class TGM | -0.17% | -0.13% | -0.14% | 100% | 97%
 | Random Access Main 10 |  |  |  | 
 | Over ECM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | -0.06% | -0.08% | 0.09% | 100% | 100%
Class TGM | -0.04% | -0.01% | -0.02% | 100% | 100%
 |  | BD-rate |  | 
 |  | Y | U | V
Class F | BasketballDrillText | -0.02% | 0.12% | 0.05%
 | ArenaOfValor | -0.05% | -0.17% | -0.09%
 | SlideEditing | -0.29% | 0.00% | -0.31%
 | SlideShow | -0.15% | -0.47% | -0.15%
Class TGM | FlyingGraphic | -0.26% | -0.21% | -0.18%
 | Desktop | -0.16% | -0.15% | -0.09%
 | Console | -0.14% | -0.04% | -0.14%
 | ChineseEditing | -0.13% | -0.11% | -0.15%
Per-sequence coding performance of All intra test

## Slide 5: Conclusions
Proposed to store and use IntraTMP BV for IBC.
Negligible complexity impact and no additional memory for storing BVs.
Suggested to include this proposal into the next version of ECM.
Thanks to Xiaomi for cross-check (JVET-AA0155).