## Slide 1: JVET-AA0090 EE1-related: One luma model with IPB and skip for filtering intra and inter luma slices
Du Liu, Jacob Ström, Mitra Damghanian, Per Wennersten, Yun Li

## Slide 2: Overview
Propose to use one luma model with block type information and block skip information for NN-filtering
  Block type information: I, P, B
  Block skip information: bypassed or not
The proposed model is used for both intra luma and inter luma slices
Reduce the total number of models from 4 (JVET-Z0112) to 3
Reduce the total number of parameters from 6.24M (JVET-Z0112) to 4.70M
Test 1: Inter luma model from JVET-Z0112 retrained with only RA data and used only for inter luma slices
Test 2: Inter luma model from JVET-Z0112 retrained with AI and RA data and used for intra and inter luma slices
Test 3: IPB+skip model trained with AI and RA data and used for intra and inter luma slices
Test 4: IPB+skip model tested on top of JVET-AA0111 (EE1-1.6.2, float32, combination with deblocking and SADL)

## Slide 3: NN structure with IPB and skip
Head of the network
Eight residual blocks
Last part of the network

## Slide 4: Summary of complexity and performance
Luma model | Number of luma models | kMAC/sample (Y) | kMAC/pix (YUV) for AI | kMAC/pix (YUV) for RA | kMAC/pix (YUV) worst case (block basis) | Num. of param. of the inter luma model (106) | Num. of parameters in total (106) | Total memory (106 bytes) | RA BDR-Y
JVET-Z0112 | 2 | 429 for intra 418 for inter | 649 | 632 | 649 | 1.551 | 6.24 (luma inter + luma intra + chroma inter + chroma intra) | 24.94 | -9.78%
Test1: JVET-Z0112 Inter luma model retrained with only RA data | 2 | 429 for intra 418 for inter | 649 | 632 | 649 | 1.551 | 6.24 (luma inter + luma intra + chroma inter + chroma intra) | 24.94 | -10.09%
Test2: JVET-Z0112 Inter luma model retrained with AI and RA data | 1 | 418 | 638 | 632 | 638 | 1.551 | 4.67 (luma + chroma inter + chroma intra) | 18.69 | -9.64%
Test3: Model with IPB+skip | 1 | 440 | 660 | 654 | 660 | 1.576 | 4.70 (luma + chroma inter + chroma intra) | 18.79 | -9.99%
The intra chroma model in JVET-Z0112 has a complexity of 110 kMAC/sample and 1.566M parameters. The inter chroma model in JVET-Z0112 has a complexity of 107 kMAC/sample and 1.555M parameters
JVET-AA0111 EE1-1.6.2 | 2 | 429 for intra 418 for inter | 539 | 525 | 539 | 1.551 | 6.24 (luma inter + luma intra + chroma inter + chroma intra) | 24.94 | -10.19%
Test 4: IPB+skip on top of EE1-1.6.2 | 1 | 440 | 550 | 547 | 550 | 1.576 | 4.70 (luma + chroma inter + chroma intra) | 18.79 | -10.27%
Combined with deblocking and SADL (float32)

## Slide 5: Training
Table 3. Network Information for NN-based video coding tool testing in training stage for the luma model. The intra chroma and inter chroma models are the same as in JVET-Z0112. |  | 
Network Information in Training Stage |  | 
Mandatory | GPU Type | GPU: NVIDIA A100-PCIE-40GB
 | Framework: | PyTorch v1.9
 | Number of GPUs per Task | 1
 | Epoch: | 330 (Test 2 and Test 3) 705 (Test 1)
 | Batch size: | 32 (L1) and 16 (L2) for the IPB+skip model (Test3) 64 (L1) and 32 (L2) for the retrained JVET-Z0112 model (Test2) 64 (L1) and 16 (L2) for the retrained JVET-Z0112 model only RA (Test1)
 | Loss function: | Weighted L1 and L2
 | Training time: | 15 days (Test3) 12 days (Test2) 12 days (Test1)
 | Training data information: | DIV2K, BVI-DVC
 | Training configurations for generating compressed training data (if different to VTM CTC): | VTM-11.0 + new MCTF, qp {17, 22, 27, 32, 37, 42}
Optional |  | 
 | Number of iterations | 
 | Patch size | 256x256
 | Learning rate: | 1e-4 and 1e-5
 | Optimizer: | ADAM
 | Preprocessing: | 
 | Mini-batch selection process: | 
 | Other information: | Since the IPB+skip model is larger, it does not fit in the GPU memory using a batch size of 64, so a batch size of 32 is used for L1 training. However, the same number of patches (and samples) are trained in both cases.

## Slide 6: Inference
Table 4. Network Information for NN-based video coding tool testing in inference stage for the luma model. The intra chroma and inter chroma models are the same as in JVET-Z0112. |  | 
Network Information in Inference Stage |  | 
Mandatory | HW environment: | 
 | GPU Type | N/A
 | Framework: | Libtorch v1.9.1
 | Number of GPUs per Task | 0
 | Total Parameter Number | See Slide 4
 | Parameter Precision (Bits) | Fp32
 | Memory Parameter (MB) | See Slide 4
 | Multiplay Accumulate (MAC) | See Slide 4
Optional |  | 
 | Total Conv. Layers | 
 | Total FC Layers | 
 | Total Memory (MB) | 
 | Batch size: | 1
 | Patch size | 128x128, 256x256
 | Changes to network configuration or weights required to generate rate points | 
 | Peak Memory Usage (Total) | 
 | Peak Memory Usage (per Model) | 
 | Border handling | 
 | Other information: | 

## Slide 7: Results
Test 2: JVET-Z0112 Inter luma model retrained with AI and RA data and used for both intra and inter luma slices
Test 1: JVET-Z0112 Inter luma model retrained with only RA data and used only for inter luma slices

## Slide 8: Results
Test 3: IPB+skip model trained with AI and RA data and used for both intra and inter luma slices
Test 4: IPB+skip on top of JVET-Z-EE1-1.6.2 (float32, with combination of deblocking and SADL)

## Slide 9: Conclusions
This contribution proposes to use one luma model with additional IPB and skip inputs for NN-filtering of intra luma and inter luma slices.
With additional IPB and skip inputs, the model gives 0.35% (= 9.99% − 9.64%) higher luma gain for RA than the model without IPB or skip inputs in the tests carried out in the contribution.
It is also shown that the proposed IPB+skip model has a minor loss of 0.1% comparing to using separate intra luma and inter luma models.
The IPB+skip model tested on top of JVET-AA0111 EE1-1.6.2 (a combination of deblocking and SADL) gives a luma gain of 10.27% for RA
The contribution proposes to further study the IPB+skip model for NN loop filters in an exploration experiment and study if we can get the same gain using just IPB or just skip as an input
Thanks to Tencent for cross-checking!