## Slide 1: JVET-AA0098 Ahg 12: encoder configuration proposal to reduce worst case encoding time
F.Le Léannec, P.Andrivon, M. Radosavljević

## Slide 2: Observation & Proposal
ECM-5.0 encoding time becoming problematic to investigate new tools
Worst-case encoder time very long to have complete results
  parallel coding: 8 days of computation needed to get full results for worst-case sequences (DaylightRoad, ParkRunning)
  = 40 days of computation in total
Proposal: reduce the encoding worst case runtime
  change the encoder configuration for lowest QP in class A, random access:
    Test 1: MaxMTTHierarchyDepthByTid=333222
    Test 2: MaxMTTHierarchyDepthByTid=332222
For other QPs and other classes: EE2 CTC unchanged

## Slide 3: Impact on average performance
Test 1
 | Random Access Main 10 |  |  |  | 
 | Over ECM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.03% | 0.03% | 0.05% | 97% | 98%
Class A2 | 0.03% | 0.04% | 0.04% | 96% | 97%
Class B | 0.00% | 0.00% | 0.00% | 100% | 100%
Class C | 0.00% | 0.00% | 0.00% | 100% | 100%
Class E |  |  |  |  | 
Overall | 0.01% | 0.01% | 0.02% | 99% | 99%
Class D | 0.00% | 0.00% | 0.00% | 100% | 100%
Class F | 0.00% | 0.00% | 0.00% | 100% | 100%
Class TGM | 0.00% | 0.00% | 0.00% | 100% | 100%
Test 2
 | Random Access Main 10 |  |  |  | 
 | Over ECM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.04% | 0.06% | 0.09% | 94% | 102%
Class A2 | 0.06% | 0.07% | 0.08% | 93% | 100%
Class B | 0.00% | 0.00% | 0.00% | 100% | 100%
Class C | 0.00% | 0.00% | 0.00% | 100% | 100%
Class E |  |  |  |  | 
Overall | 0.02% | 0.03% | 0.03% | 97% | 100%
Class D | 0.00% | 0.00% | 0.00% | 100% | 100%
Class F | 0.00% | 0.00% | 0.00% | 100% | 100%
Class TGM | 0.00% | 0.00% | 0.00% | 100% | 100%

## Slide 4: Impact on RA worst case
Test 1:
Test 2:
ECM-5.0 Random Access, QP=22 |  |  |  |  |  |  |  |  | 
 | ECM Enc Time |  | Chunks | ECM Enc time/chunk |  | Enc time reduction |  | Enc time reduction/chunk | 
Sequence | [h] | [days] |  | [h] | [days] | [h] | [days] | [h] | [days]
Tango2 | 764.12 | 31.84 | 5 | 152.82 | 6.37 | -101.54 | -4.23 | -20.31 | -0.85
FoodMarket4 | 545.44 | 22.73 | 5 | 109.09 | 4.55 | -38.24 | -1.59 | -7.65 | -0.32
Campfire | 1112.95 | 46.37 | 10 | 111.29 | 4.64 | -138.21 | -5.76 | -13.82 | -0.58
CatRobot1 | 619.82 | 25.83 | 5 | 123.96 | 5.17 | -67.12 | -2.80 | -13.42 | -0.56
DaylightRoad2 | 891.20 | 37.13 | 5 | 178.24 | 7.43 | -169.63 | -7.07 | -33.93 | -1.41
ParkRunning3 | 984.13 | 41.01 | 5 | 196.83 | 8.20 | -175.50 | -7.31 | -35.10 | -1.46
ECM-5.0 Random Access, QP=22 |  |  |  |  |  |  |  |  | 
 | ECM Enc Time |  | Chunks | ECM Enc time/chunk |  | Enc time reduction |  | Enc time reduction/chunk | 
Sequence | [h] | [days] |  | [h] | [days] | [h] | [days] | [h] | [days]
Tango2 | 764.12 | 31.84 | 5 | 152.82 | 6.37 | -177.71 | -7.40 | -35.54 | -1.48
FoodMarket4 | 545.44 | 22.73 | 5 | 109.09 | 4.55 | -76.70 | -3.20 | -15.34 | -0.64
Campfire | 1112.95 | 46.37 | 10 | 111.29 | 4.64 | -270.95 | -11.29 | -27.09 | -1.13
CatRobot1 | 619.82 | 25.83 | 5 | 123.96 | 5.17 | -126.46 | -5.27 | -25.29 | -1.05
DaylightRoad2 | 891.20 | 37.13 | 5 | 178.24 | 7.43 | -271.72 | -11.32 | -54.34 | -2.26
ParkRunning3 | 984.13 | 41.01 | 5 | 196.83 | 8.20 | -251.37 | -10.47 | -50.27 | -2.09

## Slide 5: Conclusion
A modification of EE2 CTCs is proposed to significantly reduce the worst-case encoding time of ECM in random access
Change of ECM performances in EE2 CTCs is minor
ECM test set is made more convenient to use in practice
Propose to adopt one of the two proposed CTC modifications for next JVET cycles
Thanks to ETRI for cross-checking