## Slide 1: JVET-AA0117
AHG7: refining low delay configuration for cloud gaming
S. Puri, T. Poirier, P. Le Guyadec, A. Robert, K. Naser, G. Martin-Cocher, E. Francois

## Slide 2: Introduction
  Low latency and low complexity is a desirable feature in Cloud Gaming use case
  In ECM, template matching tools are added which creates dependency between the different stages of decoding pipeline
  Additionally, tools that use templates require an expensive search on decoder, hence adding complexity and latency in the decoder pipeline and hence, not ideal for low delay applications

## Slide 3: Typical Decoder pipeline
Figure taken from: JVET-T0061
Stage 1
Stage 2
Stage 3
Stage 4
Stage 5
Stage 6
Stage 7

## Slide 4: Typical Decoder pipeline
Figure taken from: JVET-T0061
Stage 1
Stage 2
Stage 3
Stage 4
Stage 5
Stage 6
Stage 7

## Slide 5: Proposed Configurations
  Two configurations proposed
    SET 1: Disable Template Matching tools using following macros:
      TM_AMVP
      TM_MRG
      JVET_W0090_ARMC_TM
      JVET_Z0056_GPM_SPLIT_MODE_REORDERING
      JVET_Z0061_TM_OBMC
      JVET_Z0054_BLK_REF_PIC_REORDER
      JVET_V130_INTRA_TMP
      Implicit disabling of partial tools is then induced by above deactivations:
      JVET_W0097_GPM_MMVD_TM (GPM_TM part)
      JVET_X0141_CIIP_TIMD_TM (CIIP_TM part)
      JVET_Y0134_TMVP_NAMVP_CAND_REORDERING (reordering part)
      JVET_Z0084_IBC_TM (IBC_TM part)
    SET 2: Disable template-based tools (including SET1) using following macros
      JVET_W0123_TIMD_FUSION
      ENABLE_DIMD
      INTER_LIC
      SIGN_PREDICTION
      Implicit disabling of partial tools is then induced by those tools’ deactivations:
      JVET_Z0050_DIMD_CHROMA_FUSION (DIMD_CHROMA part)
      JVET_X0141_CIIP_TIMD_TM (as CIIP_TM part is already disable from set 1)

## Slide 6: Experimental Results
SET 1:
SET 2:
 | Low delay B Main 10 |  |  |  | 
 | Over ECM-5.0 LLCC |  |  |  | 
Class F | 3.09% | 3.48% | 3.35% | 74% | 76%
Class TGM | 5.37% | 5.93% | 5.97% | 77% | 78%
F + TGM | 4.23% | 4.71% | 4.66% | 76% | 77%
 | Low delay B Main 10 |  |  |  | 
 | Over ECM-5.0 LLCC |  |  |  | 
Class F | 4.96% | 5.13% | 5.29% | 64% | 64%
Class TGM | 7.15% | 7.62% | 7.56% | 66% | 68%
F + TGM | 6.06% | 6.37% | 6.43% | 65% | 66%

## Slide 7: Results (vs VTM-17.0 LLCC)
Global BD-rate gain vs complexity of different configurations compared against VTM-17.0 for Class F and TGM

## Slide 8: Proposal
Two set of configurations are proposed:
  Set 1 vs ECM-5.0: 4.23%, 4.71%, 4.66% with EncT=76% DecT=77%
  Set 2 vs ECM-5.0: 6.06%, 6.37%, 6.43% with EncT=65% DecT =66%
Propose to adopt Set 2 as the default LLCC configuration for the low delay for Class F, TGM and Gaming.
*Thanks to Tencent for crosscheck

## Slide 10: Additional Results
SET 1:
SET 2:

## Slide 11: Additional Results
Global BD-rate gain vs complexity of different configurations compared against VTM-17.0 for Class CTC