## Slide 1
JVET-AB0098
EE1-2.3 related: GOP Level Adaptive Resampling with CNN-based Super Resolution
Renjie Chang, Liqiang Wang, Xiaozhong Xu, Shan Liu (Tencent)

## Slide 2
This contribution presents a GOP level adaptive resampling method with CNN-based super resolution.
At the GOP level, the proposed method can adaptively select a scale factor from ×1.0 (original size) and ×2.0 (half size) to determine the encoding resolution, and the designed CNN-based super-resolution will be used for the half size.
Experimental results show {-4.42%, -4.83%, -4.11%} and {-7.53%, -8.14%, -7.24%} BD-rate savings for {Y, Cb, Cr} under RA and AI configurations, respectively.
Introdouction
1

## Slide 3
GOP level encoding resolution decision
Scale factors at GOP level: ×2.0 (half size) and ×1.0 (original size)
Fig. 1 Scale factor decision for RA
Proposed method
1
Fig. 2 Scale factor decision for AI

## Slide 4
Fig. 3: The super resolution network architecture for luma
Fig. 4: The super resolution network architecture for chroma
CNN-based super-resolution
The super resolution network architectures for luma and chroma are shown in Fig. 3 and Fig. 4 respectively.
Proposed method
1

## Slide 5
Results on NNVC-2.0
1
Table 1. Performance of the proposed method (RA)
Table 2. Performance of the proposed method (AI)
 |  | All Intra Main10 |  |  |  | 
 |  | Over VTM-11.0_nnvc-2.0 (QP 22, 27, 32, 37, 42) |  |  |  | 
 |  | Y | U | V | EncT | DecT
Cass A1 | Tango2 | -13.70% | -18.16% | -14.68% | 157% | 5577%
 | FoodMarket4 | -8.77% | -5.62% | -6.75% |  | 
 | Campfire | 0.01% | 0.12% | 0.07% |  | 
Class A2 | CatRobot1 | -11.85% | -6.70% | -3.75% | 101% | 10595%
 | DaylightRoad2 | -7.20% | -23.47% | -18.89% |  | 
 | ParkRunning3 | -3.69% | 5.02% | 0.59% |  | 
Average on A1 |  | -7.49% | -7.89% | -7.12% | 157% | 5577%
Average on A2 |  | -7.58% | -8.38% | -7.35% | 101% | 10595%
overall |  | -7.53% | -8.14% | -7.24% | 129% | 8086%
 |  | Random Access Main10 |  |  |  | 
 |  | Over VTM-11.0_nnvc-2.0 (QP 22, 27, 32, 37, 42) |  |  |  | 
 |  | Y | U | V | EncT | DecT
Cass A1 | Tango2 | -12.28% | -24.26% | -16.65% | 101% | 11895%
 | FoodMarket4 | -10.28% | -11.50% | -12.86% |  | 
 | Campfire | 0.45% | 0.46% | 0.69% |  | 
Class A2 | CatRobot1 | -0.38% | -0.98% | 2.08% | 119% | 1777%
 | DaylightRoad2 | -1.49% | 0.00% | 0.64% |  | 
 | ParkRunning3 | -2.51% | 7.29% | 1.45% |  | 
Average on A1 |  | -7.37% | -11.77% | -9.61% | 101% | 11895%
Average on A2 |  | -1.46% | 2.10% | 1.39% | 119% | 1777%
overall |  | -4.42% | -4.83% | -4.11% | 110% | 6836%

## Slide 6
In this contribution, a GOP level adaptive resampling method with CNN-based super resolution is tested.
By considering the difference between luma and chroma component, the proposed resampling method can better adaptively select the encoding resolution between the original size and the half size.
The experimental results verify that the proposed method can bring considerable coding performance.
Conclusions
1

## Slide 7
Notes: That is all. Thanks.