## Slide 1: JVET-AC0199 AHG13: On Film Grain Synthesis Subjective Evaluation
Xuewei Meng, Wenhao Zhang, Scott Labrozzi (Disney Streaming)

## Slide 2: Outline
Background
Observations
Test Conditions
Evaluation Results

## Slide 3: Background

## Slide 4: Background
This report comes from a in-house study on film grain technologies
  Film grain generating, modeling, delivering, rendering
We have investigated the state-of-the-art film grain synthesis (FGS) in video codec area
This proposal focuses on the subjective evaluation of VVC FGS in our study

## Slide 5: Observations

## Slide 6: Observations
In the VTM-19.0, the film grain synthesis(FGS) denoiser is independent from the encoding path.
  The effect of bitrate saving can’t be evaluated. → Is this a proper design?
The level of synthesized film grain changes regularly in the temporal domain.
  The film grain intensity ramps up every fourth frame. The main reason may be the MCTF and QP adjustment.
For videos with relatively heavy film grain,
  The synthesized grain is coarse-grained, and there are obvious repetitive patterns. → Parameters are recommended to control the synthesized grain size.
  The FGS is turned off in some frames with heavy grain. This may be due to the denoiser or noise modeling method. → More test videos are recommended to cover different content and film grain level.
For videos with low film grain, the synthesized grain looks fine.
The frequency-based FGS method and auto-regressive(AR) based method show different results under different circumstances.
  How to select the proper method for a film grain test video is important.

## Slide 7: A typical film grain synthesis (FGS) framework
De-graining
Encoder
Decoder
Film grain modeling
Film grain synthesis
-
+
Video bitstream
Source video
Degrained video
Encoded video
Film grain parameters
Diff/Residual video
Decoded video
Synthesized grain
Output video
Encoder side
Decoder side
Main modules in the film grain framework
Conventional codec

## Slide 8: FGS in VTM-19.0
De-graining
Encoder
Decoder
Film grain modeling
Film grain synthesis
-
+
Video bitstream
Source video
Encoded video
Film grain parameters
Diff/Residual video
Decoded video
Synthesized grain
Output video
Encoder side
Decoder side
Main modules in the film grain framework
Conventional codec

## Slide 9: Test Conditions

## Slide 10: Test videos
Test Videos
 | Sequences | Resolution | Bitdepth | Frame rate | Chroma Format | Frame Number
JVET | oldTownCross | 1920x1080 | 8 | 50 | YUV420 | 500
 | DinnerScene | 4096x2160 | 10 | 60 | YUV420 | 600
Disney | PrinceOfPersia | 1920x1080 | 10 | 24 | YUV420 | 240
 | StarwarESB | 3840x2160 | 10 | 24 | YUV420 | 240
 | TheMandalorian | 3840x2160 | 10 | 24 | YUV420 | 240
 | TheHandmaid | 3840x2160 | 10 | 24 | YUV420 | 240

## Slide 11: Test video — 1
oldTownCross
    1920x1080
    8bit
    50fps
    YUV420
    500 frames

## Slide 12: Test video — 2
DinnerScene
    4096x2160
    10bit
    60fps
    YUV420
    600 frames

## Slide 13: Test video — 3
PrinceOfPersia
    1920x1080
    10bit
    24fps
    YUV420
    240 frames
Picture and thumbnails will be available when Disney Legal and Copyright approves.

## Slide 14: Test video — 4
StarwarESB
    3840x2160
    10bit
    24fps
    YUV420
    240 frames
Picture and thumbnails will be available when Disney Legal and Copyright approves.

## Slide 15: Test video — 5
TheMandalorian
    3840x2160
    10bit
    24fps
    YUV420
    240 frames
Picture and thumbnails will be available when Disney Legal and Copyright approves.

## Slide 16: Test video — 6
TheHandmaid
    3840x2160
    10bit
    24fps
    YUV420
    240 frames
Picture and thumbnails will be available when Disney Legal and Copyright approves.

## Slide 17: Configurations and Parameter Settings
Configuration: RA (Random Access) with GOP32
QP: 22, 27, 32, 37
Parameters | Settings
SEIFGCEnabled | 1
SEIFGCAnalysisEnabled | 1
SEIFGCCancelFlag | 0
SEIFGCPersistenceFlag | 1
SEIFGCPerPictureSEI | 0
SEIFGCModelID | 0
SEIFGCSepColourDescPresentFlag | 0
SEIFGCBlendingModeID | 0
SEIFGCCompModelPresentComp0 | 1
SEIFGCCompModelPresentComp1 | 0
SEIFGCCompModelPresentComp2 | 0
Parameters | Settings
Block_size in flat block detection | 32x32
Pattern size | 64x64
Table 1. Frequency-domain film grain synthesis configuration
Table 2. Auto-regressive film grain synthesis configuration

## Slide 18: Subjective Results

## Slide 19: oldTownCross (QP=22, frameIdx = 160)
Spatial results (The synthesized grain of frequency-based FGS is coarse-grained, and there are obvious repetitive patterns. The synthesized grain of AR-based FGS is fine-grained and the grain level is lower than the original video.)
Original video
Frequency-based FGS
AR-based FGS
VTM-19.0 without FGS

## Slide 20: oldTownCross (QP=22, frameIdx = 20)
Temporal results (The film grain level of the original video is stable. But the synthesized grain level is not stable, frameIdx=20, 24, 28 is higher, other frames is lower. VTM-19.0 without FGS shows the similar results (frameIdx=20, 24, 28 have more grain noise).)
Original video
Frequency-based FGS
AR-based FGS
VTM-19.0 without FGS

## Slide 21: oldTownCross (QP=22, frameIdx = 21)
Temporal results (The film grain level of the original video is stable. But the synthesized grain level is not stable, frameIdx=20, 24, 28 is higher, other frames is lower. VTM-19.0 without FGS shows the similar results (frameIdx=20, 24, 28 have more grain noise).)
Original video
Frequency-based FGS
AR-based FGS
VTM-19.0 without FGS

## Slide 22: oldTownCross (QP=22, frameIdx = 22)
Temporal results (The film grain level of the original video is stable. But the synthesized grain level is not stable, frameIdx=20, 24, 28 is higher, other frames is lower. VTM-19.0 without FGS shows the similar results (frameIdx=20, 24, 28 have more grain noise).)
Original video
Frequency-based FGS
AR-based FGS
VTM-19.0 without FGS

## Slide 23: oldTownCross (QP=22, frameIdx = 23)
Temporal results (The film grain level of the original video is stable. But the synthesized grain level is not stable, frameIdx=20, 24, 28 is higher, other frames is lower. VTM-19.0 without FGS shows the similar results (frameIdx=20, 24, 28 have more grain noise).)
Original video
Frequency-based FGS
AR-based FGS
VTM-19.0 without FGS

## Slide 24: oldTownCross (QP=22, frameIdx = 24)
Temporal results (The film grain level of the original video is stable. But the synthesized grain level is not stable, frameIdx=20, 24, 28 is higher, other frames is lower. VTM-19.0 without FGS shows the similar results (frameIdx=20, 24, 28 have more grain noise).)
Original video
Frequency-based FGS
AR-based FGS
VTM-19.0 without FGS

## Slide 25: oldTownCross (QP=22, frameIdx = 25)
Temporal results (The film grain level of the original video is stable. But the synthesized grain level is not stable, frameIdx=20, 24, 28 is higher, other frames is lower. VTM-19.0 without FGS shows the similar results (frameIdx=20, 24, 28 have more grain noise).)
Original video
Frequency-based FGS
AR-based FGS
VTM-19.0 without FGS

## Slide 26: oldTownCross (QP=22, frameIdx = 26)
Temporal results (The film grain level of the original video is stable. But the synthesized grain level is not stable, frameIdx=20, 24, 28 is higher, other frames is lower. VTM-19.0 without FGS shows the similar results (frameIdx=20, 24, 28 have more grain noise).)
Original video
Frequency-based FGS
AR-based FGS
VTM-19.0 without FGS

## Slide 27: oldTownCross (QP=22, frameIdx = 27)
Temporal results (The film grain level of the original video is stable. But the synthesized grain level is not stable, frameIdx=20, 24, 28 is higher, other frames is lower. VTM-19.0 without FGS shows the similar results (frameIdx=20, 24, 28 have more grain noise).)
Original video
Frequency-based FGS
AR-based FGS
VTM-19.0 without FGS

## Slide 28: oldTownCross (QP=22, frameIdx = 28)
Temporal results (The film grain level of the original video is stable. But the synthesized grain level is not stable, frameIdx=20, 24, 28 is higher, other frames is lower. VTM-19.0 without FGS shows the similar results (frameIdx=20, 24, 28 have more grain noise).)
Original video
Frequency-based FGS
AR-based FGS
VTM-19.0 without FGS

## Slide 29: DinnerScene (QP=22, frameIdx = 239)
Spatial results (The generated grain in light area is coarse. In the dark area, there is almost no grain generated. And the grain in the source video is more colorful.)
Original video
Frequency-based FGS
VTM-19.0 without FGS

## Slide 30: PrinceOfPersia (QP=22, frameIdx = 15)
Spatial results (The film grain level is very high in the source video. But film grain synthesis is turned off. )
Original video
Frequency-based FGS
AR-based FGS
VTM-19.0 without FGS
Picture and thumbnails will be available when Disney Legal and Copyright approves.

## Slide 31: PrinceOfPersia (QP=22, frameIdx = 44)
Temporal results (The film grain level of the original video is stable. But the synthesized grain level is not stable, frameIdx=44, 48 is higher, other frames is lower. VTM-19.0 without FGS shows the similar results (frameIdx=44,48 have more grain noise).)
Original video
Frequency-based FGS
AR-based FGS
VTM-19.0 without FGS
Picture and thumbnails will be available when Disney Legal and Copyright approves.

## Slide 32: PrinceOfPersia (QP=22, frameIdx = 45)
Temporal results (The film grain level of the original video is stable. But the synthesized grain level is not stable, frameIdx=20, 24, 28 is higher, other frames is lower. VTM-19.0 without FGS shows the similar results (frameIdx=20, 24, 28 have more grain noise).)
Original video
Frequency-based FGS
AR-based FGS
VTM-19.0 without FGS
Picture and thumbnails will be available when Disney Legal and Copyright approves.

## Slide 33: PrinceOfPersia (QP=22, frameIdx = 46)
Temporal results (The film grain level of the original video is stable. But the synthesized grain level is not stable, frameIdx=20, 24, 28 is higher, other frames is lower. VTM-19.0 without FGS shows the similar results (frameIdx=20, 24, 28 have more grain noise).)
Original video
Frequency-based FGS
AR-based FGS
VTM-19.0 without FGS
Picture and thumbnails will be available when Disney Legal and Copyright approves.

## Slide 34: PrinceOfPersia (QP=22, frameIdx = 47)
Temporal results (The film grain level of the original video is stable. But the synthesized grain level is not stable, frameIdx=20, 24, 28 is higher, other frames is lower. VTM-19.0 without FGS shows the similar results (frameIdx=20, 24, 28 have more grain noise).)
Original video
Frequency-based FGS
AR-based FGS
VTM-19.0 without FGS
Picture and thumbnails will be available when Disney Legal and Copyright approves.

## Slide 35: PrinceOfPersia (QP=22, frameIdx = 48)
Temporal results (The film grain level of the original video is stable. But the synthesized grain level is not stable, frameIdx=20, 24, 28 is higher, other frames is lower. VTM-19.0 without FGS shows the similar results (frameIdx=20, 24, 28 have more grain noise).)
Original video
Frequency-based FGS
AR-based FGS
VTM-19.0 without FGS
Picture and thumbnails will be available when Disney Legal and Copyright approves.

## Slide 36: TheMandalorian (QP=22, frameIdx = 95)
Spatial results (The grain of frequency-based FGS is heavy and coarse-grained. And the grain of AR FGS is low and fine-grained. The synthesized film grain can hide encoding artifact. )
Original video
Frequency-based FGS
AR-based FGS
VTM-19.0 without FGS
Picture and thumbnails will be available when Disney Legal and Copyright approves.

## Slide 37: TheHandmaids (QP=22, frameIdx = 0)
Spatial results (The level of film grain in the source video is low. The synthesized film grain is lower than the original video, but looks fine.)
Original video
Frequency-based FGS
AR-based FGS
VTM-19.0 without FGS
Picture and thumbnails will be available when Disney Legal and Copyright approves.

## Slide 38: Thanks