## Slide 1
JVET-AD0124
AHG 12: Fix related to template type selection in Intra TMP
D. Kim, K. Kim, J. Son, J. Kwak
April. 22, 2023
WILUS Inc.

## Slide 2: Introduction
In ECM-8.0, for a IntraTMP, there are three different template types.
The left template is used when only the left template is available at the top boundary of the picture.
  Currently, in ECM-8.0, the isLeftAboveAvailable() function is used to determine the left template type. Therefore, this condition may categorize the left template as NO_TEMPLATE even when the left template is available.
The above template is used when only the above template is available at the left boundary of the picture.
Above
Left
Above
Left
L-shape type
Above type
Left type
LeftAbove

## Slide 3: Proposed method
The proposed fix is to replace the existing condition of isLeftAboveAvailable() with the condition of isLeftAvailable() to select LEFT_TEMPLATE in Intra TMP.
#if JVET_W0069_TMP_BOUNDARY if (isAboveLeftAvailable(cu, chType, posLT) && isAboveAvailable(cu, chType, posLT, numAboveUnits, unitWidth, (neighborFlags + totalLeftUnits + 1)) && isLeftAvailable(cu, chType, posLT, numLeftUnits, unitHeight, (neighborFlags + totalLeftUnits - 1))) { return L_SHAPE_TEMPLATE; } else if (isAboveLeftAvailable(cu, chType, posLT) isLeftAvailable(cu, chType, posLT, numLeftUnits, unitHeight, (neighborFlags + totalLeftUnits - 1))) { return LEFT_TEMPLATE; } else if (isAboveAvailable(cu, chType, posLT, numAboveUnits, unitWidth, (neighborFlags + totalLeftUnits + 1))) { return ABOVE_TEMPLATE; } else { return NO_TEMPLATE; }

## Slide 4: Test Results
 | All Intra Main 10 |  |  |  | 
 | Over ECM-8.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | -0.09% | 0.09% | 102% | 99%
Class A2 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class B | 0.00% | 0.04% | 0.02% | 101% | 99%
Class C | -0.01% | -0.04% | 0.06% | 101% | 99%
Class E | 0.00% | 0.02% | 0.15% | 101% | 99%
Overall | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class D | 0.01% | 0.06% | -0.09% | 100% | 100%
Class F | -0.01% | 0.03% | -0.01% | 101% | 100%
Class TGM | -0.01% | 0.00% | 0.00% | 101% | 100%
 | Random Access Main 10 |  |  |  | 
 | Over ECM-8.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class A2 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class B | -0.01% | 0.12% | 0.10% | 101% | 99%
Class C | -0.03% | 0.04% | 0.16% | 101% | 100%
Class E |  |  |  |  | 
Overall | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class D | -0.02% | 0.06% | -0.33% | 101% | 100%
Class F | 0.02% | 0.04% | 0.06% | 103% | 101%
Class TGM | 0.00% | -0.01% | -0.01% | 103% | 101%
Two more contributions submitted with the same bug
  JVET-AD0142(Non-EE2: bugfix for intraTMP, Dahua)
  JVET-AD0239(Non-EE2: Fixes for IntraTMP template availability, Qualcomm)

## Slide 5: THANK YOU
5th Fl., 216 Hwangsaeul-ro, Bundang-gu, Seongnam-si, Gyeonggi-do 13595, Korea, +82-31-712-0523, info@wilusgroup.com, www.wilusgroup.com