## Slide 1
JVET-AD0217
Non-EE2: Filtered Intra Block Copy (FIBC)
Hong-Jheng Jhu, Xiaoyu Xiu, Che-Wei Kuo, Wei Chen, Ning Yan, Changyue Ma, Xianglin Wang (Kwai)

## Slide 2: Introduction
In ECM-8.0, intra block copy (IBC) is applied for screen content sequences which predict the samples of one current block from the reconstructed sample of its neighboring regions
In the existing IBC design, the reconstructed samples are directly used as the prediction samples of the current block
In EE2 Test-15a and Test-15b, a linear filter is applied to the prediction samples of intra template matching (intraTMP)
The filter coefficients are derived from the neighboring reconstructed samples and their corresponding reference samples

## Slide 3: Filtered IBC (FIBC)
Applies one linear filter to the prediction samples of the IBC
For signaling, one extra indication flag is introduced for the FIBC which is signaled after the IBC-LIC
predVal = C + N + S + W + E +
-th coefficient
offset

## Slide 4: Simulation Results
 | All Intra Main10 |  |  |  | 
 | Over ECM-8.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | -0.92% | -1.10% | -1.04% | 101% | 100%
Class TGM | -0.17% | -0.19% | -0.15% | 102% | 101%
 | Random Access Main 10 |  |  |  | 
 | Over ECM-8.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class F | -0.29% | -0.67% | -0.72% | 101% | 100%
Class TGM | -0.15% | -0.13% | -0.18% | 101% | 100%

## Slide 5: Conclusion
It proposes to improve the prediction efficiency of the IBC by filtering the IBC prediction samples based on an adaptive linear filter
Significant gains on screen content sequences with negligible encoding/decoding impacts
Recommended to study the proposed method into EE