## Slide 1: JVET-AD0251 AHG12 Shifting Quantizer Center
Muhammet Balcilar, Karam Naser, Franck Galpin, Fabrice Le Leannec

## Slide 2: Overview
Recent paper [1] exploits correlation between gradient
w.r.t distortion and gradient w.r.t. entropy for end-to-end
compression models.
This correlation can be exploited at decoder to reduce distortion, even on top of RDOQ optimized latent. Typically, a gain of 1% ~ 2% is achieved for most of compressive auto-encoders.
The same could apply to traditional codecs:
  dequantized coefficients of the residual are replacing the latent
  the gradient w.r.t. entropy is replaced by a simple proxy
  a step to decrease the distortion is computed
[1] Balcilar, M., Damodaran, B. B., Naser, K., Galpin, F., & Hellier, P. Vector Quantization and Shifting: Exploiting Latent Properties to Optimize Neural Codecs. https://openreview.net/forum?id=QVSoh6VM4nG

## Slide 3: Proposal
Assume coefficient rate is linear with dequantized coefficient level and independent from other coefficients.
Assume a fixed step of the coefficient . End up with a simple change: makes coefficient far away from zero point
(5)
Pseudo code
// for non zero coefficient
qIdx2=(qIdx>0? qIdx+1: qIdx-1);
coeff2 = dequantize(qIdx2);
coeff=((1024-rho)*coeff+rho*coeff2)>>10;

## Slide 4
Simulation results
 | All Intra Main 10 |  |  |  | 
 | Over ECM-8.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.11% | -0.11% | -0.07% | 99% | 100%
Class A2 | -0.07% | -0.10% | -0.04% | 100% | 100%
Class B | -0.10% | -0.10% | -0.14% | 98% | 100%
Class C | -0.07% | -0.16% | -0.29% | 99% | 100%
Class E | -0.09% | -0.14% | -0.08% | 99% | 100%
Overall | -0.09% | -0.12% | -0.13% | 99% | 100%
Class D | -0.08% | -0.17% | -0.16% | 99% | 99%
Class F | 0.04% | -0.13% | -0.22% | 98% | 99%
 | Random Access Main 10 |  |  |  | 
 | Over ECM-8.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class B | -0.07% | -0.20% | -0.15% | 100% | 100%
Class C | -0.07% | -0.29% | -0.22% | 100% | 100%
Class E |  |  |  |  | 
Overall |  |  |  |  | 
Class D | 0.01% | 0.01% | -0.47% | 100% | 100%
Class F | -0.02% | -0.32% | -0.20% | 100% | 100%

## Slide 5: Conclusion
Very simple change in the code
Brings consistent gain on CTC sequences
Propose to study in next EE round
Thank you to Qualcomm for crosschecking