## Slide 1
JVET-AF0114
AHG12: Local-Boosting on Cross-Component Merge Mode
H. Qin, K. Ding, Z. Xu, J. Konieczny
TCL

## Slide 2
Introduction
Merge candidate list for cross-component prediction was proposed in JVET-AD0188
Local Boosting, a low-pass filter applied on CCP predicted results when MM-CCLM/MM-CCCM is used was proposed in JVET-AD0120 aspect #1 to boost CCP prediction results
Both proposals were independently adopted into ECM
Still, a way to use LB with CCP merge candidate list is missing

## Slide 3
Proposal
Enable LBCCP aspect #1 upon CCP merge mode
For MM-CCLM/MM-CCCM candidates of CCP merge mode, decide on their LBCCP flag based on template cost using 3-tap and coefficients are:
[3, 10, 3] / 16

## Slide 4
Proposal
Observation: in CCP merge mode at candidate reordering stage, if MM-CCLM is used, CCLM model is tested instead of MM-CCLM
Before
cost += xUpdateOffsetsAndGetCostCCLM<false>(pu, COMPONENT_Cb, pu.Cb(), cclmModels, 1, ccpCand.glmIdc); cost += xUpdateOffsetsAndGetCostCCLM<false>(pu, COMPONENT_Cr, pu.Cr(), cclmModels, 1, ccpCand.glmIdc);
After
cost += xUpdateOffsetsAndGetCostCCLM<false>(pu, COMPONENT_Cb, pu.Cb(), cclmModels, (ccpCand.type & CCP_TYPE_MMLM) ? 2 : 1, ccpCand.glmIdc, (ccpCand.type & CCP_TYPE_MMLM), filteredSAD); cost += xUpdateOffsetsAndGetCostCCLM<false>(pu, COMPONENT_Cr, pu.Cr(), cclmModels, (ccpCand.type & CCP_TYPE_MMLM) ? 2 : 1, ccpCand.glmIdc, (ccpCand.type & CCP_TYPE_MMLM), filteredSAD);

## Slide 5
Results
 | All Intra Main 10 |  |  |  |  | 
 | Over ECM-10.0 |  |  |  |  | 
 | Y | U | V | EncT | DecT | VmPeak
Class A1 | 0.00% | -0.07% | 0.12% | 100.2% | 100.6% | 100.0%
Class A2 | -0.01% | -0.02% | 0.07% | 100.1% | 100.8% | 100.0%
Class B | -0.02% | 0.03% | -0.06% | 100.3% | 100.0% | 100.0%
Class C | -0.02% | -0.03% | 0.04% | 100.3% | 101.3% | 100.0%
Class E | -0.02% | 0.00% | -0.38% | 100.0% | 100.9% | 100.0%
Overall | -0.02% | -0.01% | -0.04% | 100.2% | 100.7% | 100.0%
Class D | -0.02% | -0.03% | 0.08% | 100.2% | 100.1% | 100.0%
Class F |  |  |  |  |  | 
Class TGM |  |  |  |  |  | 

## Slide 6
Results
 | Random Access Main 10 |  |  |  |  | 
 | Over ECM-10.0 |  |  |  |  | 
 | Y | U | V | EncT | DecT | VmPeak
Class A1 |  |  |  |  |  | 
Class A2 |  |  |  |  |  | 
Class B |  |  |  |  |  | 
Class C | 0.01% | -0.02% | -0.23% | 100.1% | 99.8% | 100.1%
Class E |  |  |  |  |  | 
Overall |  |  |  |  |  | 
Class D |  |  |  |  |  | 
Class F |  |  |  |  |  | 
Class TGM |  |  |  |  |  | 

## Slide 7
Conclusions
Recommendation: to further investigate the method of signaling LB flag in CCP merge list and compare performance of the proposed method to other proposals, e.g. JVET-AF0083
Reccomendation: to further investigate the impact of code change (MM variant of CCLM was not included in cost computation of merge list ordering for MM-CCLM candidate)