## Slide 1: JVET-aF0117 Non-EE2:ExtensionS of IBC GPM
Changyue Ma, Xiaoyu Xiu, Wei Chen, Hong-Jheng Jhu, Che-Wei Kuo, Ning Yan, Xianglin Wang

## Slide 2: Introduction
IBC GPM in ECM10.0:
Split a CU into two geometry partitions.
Each of two partitions are generated using IBC prediction or intra prediction.
The IBC part is generated based on IBC regular merge mode and IBC TM merge mode.
The intra part uses the same IPM candidate list of GPM with inter and intra prediction.
There are totally 48 geometry partition modes, which are grouped into 2 sets.
Table 1. Geometry partitioning modes in the first geometry partitioning mode set.
Table 2. Geometry partitioning modes in the second geometry partitioning mode set.

## Slide 3: Proposal
IBC GPM with block vector difference (BVD):
One additional BVD is allowed to be added on top of the BV of one IBC partition.
Only applied to IBC part generated based on regular IBC merge mode.
One flag is signaled for each IBC partition to indicate whether additional BVD is applied.
When the flag is true, the corresponding BVD is further signaled.
Split mode reordering for IBC GPM:
The split mode of IBC GPM is reordered with template matching methods.
The reordering is only applied to the first set of IBC-GPM split modes.

## Slide 4: Performance evaluation
Summary results of IBC GPM with BVD
 | All Intra Main 10 |  |  |  |  | 
 | Y | U | Y | Enc. T | Dec. T | VmPeak
Class F | -0.20% | -0.12% | 0.01% | 103.4% | 99.1% | 100.0%
Class TGM | -0.26% | -0.24% | -0.23% | 103.3% | 99.8% | 100.0%
 | Random Access Main 10 |  |  |  |  | 
 | Y | U | Y | Enc. T | Dec. T | VmPeak
Class F | -0.10% | 0.04% | 0.02% | 102.3% | 99.8% | 99.9%
Class TGM | -0.21% | -0.14% | -0.17% | 101.4% | 99.4% | 100.0%

## Slide 5: Performance evaluation
Summary results of IBC GPM with BVD plus split mode reordering
 | All Intra Main 10 |  |  |  |  | 
 | Y | U | Y | Enc. T | Dec. T | VmPeak
Class F | -0.21% | -0.22% | -0.05% | 105.6% | 99.9% | 101.4%
Class TGM | -0.39% | -0.34% | -0.36% | 106.4% | 99.5% | 101.1%
 | Random Access Main 10 |  |  |  |  | 
 | Y | U | Y | Enc. T | Dec. T | VmPeak
Class F | -0.16% | 0.22% | -0.04% | 103.4% | 99.8% | 101.2%
Class TGM | -0.26% | -0.16% | -0.26% | 102.3% | 99.1% | 100.7%

## Slide 6: Performance evaluation
Summary:
It is proposed to add block vector difference to the block vector of the IBC prediction results.
It is proposed to reorder the split modes with template matching methods
Achieve noticeable coding benefits with reasonable enc/dec run-time impact.
It is recommended to study the proposed methods in the next round of EE.