## Slide 1: AHG9: Copyright SEI message JVET-AGxxxx
Stephan Wenger Arianne Hinds Gilles Teniou
Tencent

## Slide 2: Need for a Copyright SEI Message
Situation in standards
  A copyright SEI message was present in H.263 Annex W, “Picture Message”, MTYPE == 2
  No Copyright SEI message in H.264/H.265/H.266/VSEI
  No Copyright SEI message in MPEG elementary streams (ES) that we are aware of
  Copyright metadata available in ISOMBFF, certain system layer specs including DASH
Situation in the field
  Industry at large seems to rely mostly on system-layer marking
  Some “squatting” on SEI in at least H.264 (and likely also in H.265, though no bitstream analysis was performed beyond a hex-dump)—payloadType 0x88, followed by ASCII data
Why is Elementary Stream ( including video stream) copyright marking desirable
  Increasingly we see manipulation of individual ESs even in composed multimedia streams (translations, AI-based manipulations, …)
  Copyright is associated with creation and modification. If the creation/modification involves just one ES of a multimedia stream, then there should be a way to associate a copyright marker only with the actually created/manipulation part of a multimedia a stream
Notes: 座位号：25F-062

## Slide 3: Proposal 1: Copyright Information in st(v)
ci_cancel_flag, ci_persistence-flag with the usual semantics
ci_information specifies copyright information that pertains to the picture(s) in the persistence scope defined by ci_cancel_flag and ci_persistence_flag.
  Informative note: A typical content of ci_information includes the string “Copyright” or the “©” symbol, information identifying the copyright owner such as a personal or company name, the year of creation of the content according to the Gregorian calendar, and a use/licensing statement such as “all rights reserved”.

## Slide 4: Proposal 2: Structured Copyright SEI 1/2
ci_cancel-flag, ci_persistence_flag with the usual semantics
ci_owner specifies the owner of the copyright that pertains to the picture(s) in the persistence scope defined by ci_cancel_flag and ci_persistence_flag.

## Slide 5: Proposal 2: Structured Copyright SEI 2/2
ci_year_plus1886 specifies the year of creation of the the picture(s) in the persistence scope defined by ci_cancel_flag and ci_persistence_flag minus 1886 years.
ci_information specifies copyright information.
  Informative note: A typical content of ci_information is a use/licensing statement such as “all rights reserved”.
Why the u(8) and “plus1886”?
ci_year_plus1886 specifies the year of creation of the work, hence we can mark content with a year of creation between 1886 and 2141 when using the proposed u(8) syntax.
The year 1886 is the year where the Berne Convention on Copyright was first signed, that established the notion of an internationally recognized copyright regime.
Today, copyright is granted for 70 years after the death of the author. Historically, the past death period was shorter (50 years). Any work created before that year is in the public domain, free to use, and hence has greatly diminished need for a copyright marking.
  Work created before 1886 is, for all practical purposes, in the public domain: 2024 – (1886+50) == 88, which means that the work would have to be created in 1886 by an author that was, in 1886, at least 88 years old (and lived in a Berne convention signatory state, and, and, and). Further, for cinematographic work, copyright is extended only 50/70 years after the first release.