## Slide 1: Application-Required NAL Unit JVET-AG0046
Gilles Teniou Stephan Wenger
Tencent

## Slide 2: Use Case
Marking NAL units as “required” that are not required for the decoding process: SEI, AUD, VCM-data
Marking functionality not needed by decoder, but may be needed in heterogenous system environments
Key Motivation: VCM “Hybrid” encoder/decoder
  End-to-end image compression (EEIC) replaces VVC intra, VVC-inter stays
  EEIC data to be conveyed in SEI messages
Encoder inserting EEIC/AUD per system layer requirement
Decoder/Receiving system relying on presence of EEIC/AUD
MANE may
removing EEIC in SEI and AUD unless marked
Notes: 座位号：25F-062

## Slide 3: Required NAL unit marking
Preferably at the NAL unit layer, not per SEI message
  Allows to mark decoder-optional NAL units: DCI, AUD, EOS, EOB, SEI, Filler
  Easy to parse by MANE
    Based on NAL unit boundaries, NAL unit type—both typically exposed outside encryption context in some form
    Parsing does not require bit-oriented processing
Decoder reaction to req_nu: ignore. Decoder reaction to EEIC/AUD as per profile
MANE reaction: when present, read count. Forward the <count> next NAL units even if their type would suggest they could be dropped
Req_nu count == 2
EEIC
AUD
Unmarked NAL unit
Unmarked NAL unit

## Slide 4: Error resilience
Basic principle in error resilience: system behavior is statistically better with proposal compared to without. Perfection is unachievable.
If req_nu (green) is lost: situation no worse than without the proposal
If req_nu (green) is present, but one blue NAL units were lost on path to MANE
  The ”Unmarked NAL unit #1” would erroneously be marked, and hence forwarded by the MANE even if no such forwarding is required
Req_nu count == 2
SEI
AUD
Unmarked NAL unit #1
Unmarked NAL unit #2