## Slide 1: JVET-AG0049 AHG9: SEI message extension of VVC for object-wave compression and computer-generated hologram use
Jan. 2024
H. Kojima, R. Koiso, K. Nonaka, K. Kawamura, H. Kato (KDDI)

## Slide 2: Overview
At the July meeting, we proposed an SEI for VVC for object wave compression in JVET-AE0182. This proposal is an updated version of JVET-AE0182 with additional preliminary study experiments and modifications to the SEI message, such as persistence scope variables.
Preliminary study:
  Object wave compression by using VTM-20.0 is shown.
  The RD curves of RA and AI were compared to confirm that the inter predictions work.
SEI message:
  The SEI supports the functions for the mapping of object wave to video format and the adjustment of the object wave to the playback device.
Recommend including the extension in the next version of VSEI TuC for use with VVC.

## Slide 3: Background
Computer holography is a technology that reproduces light waves emitted by objects (called object wave), providing a highly realistic 3D video experiences that solves eye fatigue, VR motion sickness, etc.
Due to the high computational complexity for object wave calculations, it is optimal to perform them on the server and then transmit the results to the client.
Work style
Remote collaboration on
design / discussion
Telemedicine
Education
Immersive e-learning
Healthcare

## Slide 4: Object Wave Transmission
The object wave is converted to video and transmitted to the decoder side together with the information necessary for the inverse conversion as SEI message.
(e) Playback (reconstruction)
(i) Object wave calculation
(ii) Mapping from float to integer
(iii) Video enc/dec
(a) 3D model
(iv) Inverse mapping from integer to float
(vi) Conversion from object wave to hologram
(v) Adjustment of object wave
SEI message
(b) Object wave on the object plane
Amplitude
Phase
(d) Object wave on the display
Amplitude
Phase
(c) Integerized
object wave
Parameters for adjustment of object wave
Parameters for Inverse mapping from integer to float

## Slide 5: Preliminary Study: Settings
Codec
  VTM-20.0
Configuration
  RA: encoder_randomaccess_vtm.cfg, formatGBR.cfg
  AI: encoder_intra_vtm.cfg, formatGBR.cfg
Input video
  4:4:4 format, 8-bit depth, 4K x 8K resolutions (amplitude + phase), 30 frames
Evaluation
  Ex. 1: PSNR calculation in the object wave domain
  Ex. 2: PSNR calculation in the reconstructed image domain

## Slide 6: Preliminary Study: Ex. 1 Result
Object wave domain
  QP=22, 27, 32, 37
  The BD-rate of RA compared to AI shows a 53.0% improvement for amplitude and a 42.7% improvement for phase.
Amplitude
Phase

## Slide 7: Preliminary Study: Ex. 2 Result
Reconstructed image domain
  QP=22, 27, 32, 37
  The BD-rate of RA compared to AI shows a 47.4% improvement.
Reconstructed image

## Slide 8: Preliminary Study: Ex. 2 Result
A similar trend to conventional video coding is observed.
  With QP=37, the bitrate is reduced by about 1/20 and distortion is noticeable on the butterfly's wings.
QP=22
QP=37
Original
kbps
kbps
PSNR 37.6
kbps
PSNR 24.0

## Slide 9: Proposal of SEI extension
Persistence scope is specified by the syntax of the SEI message.
object_wave_parameters( payloadSize ) { | Descriptor
owp_cancel_flag | u(1)
if( !owp_cancel_flag ) { | 
owp_persistence_flag | u(1)
owp_value_max | se(v)
owp_value_min | se(v)
owp_pixel_pitch_x | ue(v)
owp_pixel_pitch_y | ue(v)
owp_wavelength_r | ue(v)
owp_wavelength_g | ue(v)
owp_wavelength_b | ue(v)
owp_object_distance | ue(v)
owp_object_plane_distance | ue(v)
} | 
} | 
For linear mapping from integer to float
For adjustment of object wave
For adjustment of object wave
For compensation for wavelength mismatch

## Slide 10: Conclusion
This proposal is an updated version of JVET-AE0182 with additional preliminary study experiments and modifications to the SEI message, such as persistence scope variables.
Preliminary study:
  Object wave compression by using VTM-20.0 is shown.
  The RD curves of RA and AI were compared to confirm that the inter predictions work.
SEI message:
  The SEI supports the functions for the mapping of object wave to video format and the adjustment of the object wave to the playback device.
Recommend including the extension in the next version of VSEI TuC for use with VVC.