## Slide 1: JVET-AG0055 AhG10: CTU-Level Lagrange Multiplier and QP Adaptation for VVC Low-Delay Configuration
Hongwei Guo, Ce Zhu, Lei Luo, Junjie Chen (UESTC)
Yongkai Huo, Yutian Liu (Transsion)

## Slide 2: Method as presented in JVET-AF0089
We first estimate a distortion propagation factor (DPF) for each 32×32 block in the frame to be encoded.
  The frame to be encoded is first pre-encoded with a 32×32 block integer pixel inter-prediction.
  The purpose of pre-encoding is to roughly obtain the coding distortion of a block and its motion compensation predicted (MCP) error, both of which are quantified using Mean Squared Error (MSE) and will be used to calculate the DPF of a block.
Then, a weight coefficient of each CTU is calculated according to DPFs.
Finally, the adaptive Lagrange multiplier and QP are determined.
Suggestions from the last meeting:
  To reduce the variation in sequence-by-sequence performance
  To compare with BIM
  To examine the impact on subjective quality

## Slide 3: Updates to the method
To mitigate potential inaccuracies in calculating DPFs resulting from scene changes, we implement a threshold mechanism designed to detect such cases.
The weight coefficient for each CTU:
: the introduced threshold
: input QP of the encoder
: MAE of predicted residuals derived from the pre-encoded frame
: the occurrence of the scene change

## Slide 4: Comparison with BIM
Block importance mapping (BIM): JVET-V0057 and JVET-Y0077.
Aspect | Block Importance Mapping (BIM) | Our Method
Function | CTU-level QP adaptation | 
Weights Determination | Based on motion compensation to calculate the weights of different CTUs | 
Estimation Avenue | MCP error → delta QP → Lagrange multiplier | MCP error & Coding distortion → Lagrange multiplier → QP
Motion Compensation Algorithm | Motion Compensation Temporal Filter (MCTF) | Pre-encoding
Modified Frames | POC divisible by 8 | Every frame

## Slide 5: Result
Our method BIM

## Slide 6: Subjective Result
BasketballDrill.Q22.jvet10.lb 220

## Slide 7: Conclusion
Over VTM-23.0:
  LDB: -3.59%, -4.72%, -3.78% {103%, 100%}
  LDP: -3.44%, -4.47%, -3.05% {102%, 101%}
This contribution proposes an updated version of the method in contribution JVET-AF0089.
Our method can provide coding performance benefits compared to the original scheme and BIM.
The encoding time of the proposed method is slightly increased.
A subjective video quality test was conducted and no compression artifact was observed.
A bug of compatibility with the original VTM code is fixed.
It is recommended to adopt this proposed scheme into VTM under LD configuration.
Thanks to Xidian Univ. for the cross-check.

## Slide 8: Thanks
www.transsion.com