## Slide 1: AHG12: Intra-prediction using Merged Histogram of Gradients JVET-AG0078
Saverio Blasi, Ivan Zupancic, Pekka Astola, Jani Lainema

## Slide 2
Introduction
When using DIMD, a Histogram of Gradients is computed to predict directionality of template samples.
Up to 5 predictors are blended with Planar mode using weights depending on the HoG amplitudes.
DIMD HoG

## Slide 3
Proposed method
A new mode is proposed, Merged Intra Mode Derivation (MIMD), based on computation of a Merged Histogram of Gradients (MHoG).
MHoG is computed based on HoGs extracted from neighbouring blocks:
For DIMD and MIMD neighbours, the HoG of that block is scaled depending on block size
For non-DIMD neighbours, a synthetic HoG is derived where for , and , where depends on size of the neighbouring block
HoGs extracted from neighbouring blocks are averaged to determine the MHoG.
MHoG
Current CU
Non-DIMD
neighbour
DIMD
neighbour

## Slide 4
Proposed method
The MHoG is used to determine up to 5 intra-prediction modes and weights, identically to DIMD.
MIMD is signalled as a new mode.
To limit complexity:
MIMD is not used on 4x4 blocks
MIMD is only used when there is at least one adjacent MIMD or DIMD block

## Slide 5
Results
 | All Intra Main 10 |  |  |  |  |  | 
 | Over ECM-11.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 | -0.13% | -0.10% | -0.07% | 101.2% | 100.3% | 100.0% | 100.0%
Class A2 | -0.16% | -0.04% | -0.03% | 100.4% | 100.9% | 100.0% | 100.1%
Class B | -0.09% | 0.06% | 0.02% | 100.4% | 99.6% | 101.2% | 100.0%
Class C | -0.07% | 0.03% | 0.00% | 100.7% | 98.4% | 100.1% | 100.0%
Class E | -0.05% | -0.02% | 0.07% | 100.6% | 99.3% | 100.1% | 100.0%
Overall | -0.10% | 0.00% | 0.00% | 100.6% | 99.6% | 100.4% | 100.0%
Class D | -0.06% | -0.08% | 0.05% | 100.6% | 102.3% | 100.1% | 100.0%
Class F | -0.04% | -0.24% | 0.01% | 99.7% | 99.2% | 100.1% | 100.0%
Class TGM | 0.00% | 0.04% | -0.03% | 99.3% | 98.6% | 100.0% | 99.9%
 | Random Access Main 10 |  |  |  |  |  | 
 | Over ECM-11.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 | -0.06% | -0.07% | -0.02% | 100.4% | 101.5% | 100.0% | 100.3%
Class A2 | -0.06% | 0.05% | -0.01% | 99.8% | 101.3% | 99.8% | 100.0%
Class B | -0.03% | 0.11% | -0.01% | 99.1% | 100.3% | 99.5% | 100.5%
Class C | -0.02% | -0.06% | -0.08% | 99.5% | 100.2% | 100.2% | 100.6%
Class E |  |  |  |  |  |  | 
Overall | -0.04% | 0.02% | -0.03% | 99.6% | 100.7% | 99.8% | 100.4%
Class D | 0.00% | -0.15% | -0.30% | 100.4% | 98.7% | 100.3% | 100.6%
Class F | -0.01% | -0.27% | -0.02% | 99.2% | 99.4% | 99.5% | 100.4%
Class TGM |  |  |  |  |  |  | 

## Slide 6
Summary
New MIMD mode is proposed based on computation of Merged Histogram of Gradients
Consistent coding efficiency gains (average -0.10% luma AI gains) for very limited impact on ET.
Higher gains in high-res classes A1 (-0.13%) and A2 (-0.16%).
Proposed to study the technique in the next round of EEs.