## Slide 1: [JVET-AG0083] AHG9: On feature-based optimization type
Chul Keun Kim, Hendry, Jaehyun Lim, Seung hwan Kim

## Slide 2: Motivation
The encoder optimization information(EOI) SEI message is used to indicate if the video has been optimized for human viewing or machine analysis and which types of optimization have been applied in pre-processing or encoding
eoi_type indicates the types of optimization method as specified in table below
The types of optimization method represent the properties of the task and the required information for the task.
bitMask | Interpretation
0x01 | Object-based optimization; the pictures for which this SEI message persists have been pre-processed or encoded so that detected objects in the pictures are optimized with respect to other parts of the pictures for the indicated optimization purposes
0x02 | Temporal resampling optimization
0x04 | Spatial resampling optimization
0x08 | Temporal quality optimization in a manner that quality fluctuates temporally
0x10 | Spatial quality optimization; the pictures for which this SEI message persists have been pre-processed or encoded to reduce unnecessary information or improve the quality of necessary information.(e.g to reduce the amount of noise and remove speckles at the picture-level)
*included in the Technologies under Consideration (JVET-AF2032)

## Slide 3: Proposal
Feature is one of the video properties that need to be retained for tasks, feature-based optimization has been applied and introduced as follow
  1)Feature-based RDO.
      This method optimizes ratio-distortion by calculating distortion using extracted features.
  2)Feature-based pre-processing.
      This method minimizes loss of important features and reduces unnecessary information for machine analysis. This makes the input picture more suitable for compression and reduce the bitrate without negative impact on machine analysis.
Furthermore, When feature-based optimization is performed based on specific models or tasks, it may impact other models, tasks and human perception
It is necessary to provide users with information about feature-based optimization

## Slide 4: Proposal
We propose to add a new value to eoi_type to indicate feature-based optimization in EOI SEI messages that is included in JVET-AF2032
eoi_type indicates the types of optimization method as specified in Table x1 where ( eoi_type & bitMask ) not equal to 0 indicates that the optimization type with the bitMask value in Table x1 has been applied. When eoi_type is greater than 0 and ( eoi_type & bitMask ) is equal to 0, the optimization type with the bitMask value has not been applied. When eoi_type is equal to 0, optimization as determined by the application has been used.
bitMask | Interpretation
0x01 | Object-based optimization; the pictures for which this SEI message persists have been pre-processed or encoded so that detected objects in the pictures are optimized with respect to other parts of the pictures for the indicated optimization purposes
0x02 | Temporal resampling optimization
0x04 | Spatial resampling optimization
0x08 | Temporal quality optimization in a manner that quality fluctuates temporally
0x10 | Spatial quality optimization; the pictures for which this SEI message persists have been pre-processed or encoded to reduce unnecessary information or improve the quality of necessary information.(e.g to reduce the amount of noise and remove speckles at the picture-level)
0x20 | Feature based optimization; the pictures for which this SEI message persists have been pre-processed or encoded based on the quality of features. (e.g to minimize loss of important features or optimize by calculating distortion using extracted features)
The variables EoiObjectBasedFlag, EoiTemporalResamplingFlag, EoiSpatialResamplingFlag, EoiTemporalQualityFlag, and EoiSpatialQualityFlag, EoiFeatureBasedFlag specifying whether eoi_type indicates the type of the optimization to include object-based optimization, temporal resampling optimization, spatial resampling optimization, temporal quality optimization ,spatial quality optimization and feature-based optimization, respectively, are derived as follows:
EoiObjectBasedFlag = ( ( eoi_type & 0x01 ) > 0 ) ? 1 : 0 EoiTemporalResamplingFlag = ( ( eoi_type & 0x02 ) > 0 ) ? 1 : 0 EoiSpatialResamplingFlag = ( ( eoi_type & 0x04 ) > 0 ) ? 1 : 0 (xx) EoiTemporalQualityFlag = ( ( eoi_type & 0x08 ) > 0 ) ? 1 : 0 EoiSpatialQualityFlag = ( ( eoi_type & 0x10 ) > 0 ) ? 1 : 0 EoiFeatureBasedFlag = ( ( eoi_type & 0x20 ) > 0 ) ? 1 : 0