## Slide 1: JVET-AG0111 EE1-2.2: Content-adaptive LOP filter
R. Yang, M. Santamaria, F. Cricri, M. M. Hannuksela, H. Zhang, J. Lainema, A. Hallapuro, D. Bugdayci Sansli

## Slide 2
Highlights
RA segment-wise content adaptation of LOP1 filter, via overfitting to input test content.
New Neural Network Filter Update (NNFU) Adaptive Parameter Set (APS)
  Carries the weight-update, which is coded with MPEG-NNR
  There is one NNFU APS per RA segment
Results over NNVC-7.1 (LOP1 and NN-Intra ON)
  -1.41% (Y); -3.55 (Cb), -2.99% (Cr)
Results over NNVC-7.1 (NN tools OFF)
  -7.93% (Y); -11.03 (Cb), -10.13% (Cr)

## Slide 3
Overfitting of LOP filter
Content-adaptation is achieved by means of neural-network over-fitting on each RA segment.
The model to be over-fitted is selected as the base model (one out of four) with the highest PSNR gain
Only a subset of parameters (multipliers) are over-fitted
Technique is applied to the LOP1 filter (JVET-AD0156)

## Slide 4
Weight-update signalling
NNFU APS
nnfu_payload_byte contains the byte sequence representing the size of the model QPs, the model QPs and the bitstream conforming to ISO/IEC 15938-17.

## Slide 5
Results of RA segment-wise overfitting
1 NNFU APS for every RA segment

## Slide 6
Results of RA segment-wise overfitting
Speed-up
Significant speed-up of segment-wise overfitting process, due to better implementation.
A1 & A2: 1 hour (previous: 1 day)
B: 15 mins (previous: 4 hours)
C: 10 mins (previous: 20 mins)
D: 5 mins
F: 15 mins (previous 4 hours)

## Slide 7
Summary
Content-adaptive LOP is proposed
RA results over NNVC-7.1 with LOP1 and NN-intra ON: -1.41% (Y), -3.55% (Cb), -2.99% (Cr)
RA results over NNVC with NN tools off: -7.93% (Y), -11.03% (Cb), -10.13% (Cr)
No significant complexity added at decoder side
Segment-wise overfitting process was significantly sped up
Thanks Ittiam and OPPO for cross-checking the training and inference
Recommendation: adopt into the next version of NNVC software

## Slide 9
Previous results of sequence-wise overfitting (JVET-AF0056)
1 NNFU APS for the whole sequence

## Slide 10
Simulated results of 5 seconds segment-wise overfitting
1 NNFU APS for each 5 seconds segment (simulating streaming segments)

## Slide 11
Proposal
Trade-offs between use cases and achievable gains
For on-demand streaming use case:
Adaptation for each streaming segment (approximately 5 seconds).
Average gains by considering 1 NNFU APS per streaming segment (simulated, non-optimized):
Number of NNFU APSs = roundup ( num_frames / fps ) / 5
  1.10%, 6.31%, 5.39% (RA, over NNVC 6.0)
For video archives (files) use case:
Same as on-demand streaming use case
For broadcasting use case:
RA segment-wise adaptation.
Average gains with 1 NNFU APS per RA segment:
  1.41% (Y); 3.55% (Cb), 2.99% (Cr) (RA, over NNVC 7.1 with LOP1)

## Slide 12
Simulated results (1 NNFU per 5 sec streaming segment) – Streaming and files use cases
1 NNFU APS for every RA segment – Broadcasting use case
Results of RA segment-wise overfitting
Over NNVC-7.1 (LOP2 & NN-Intra ON)