## Slide 1: JVET-AG0129 AHG11: Unified CNN-based super resolution C. Zhou, Z. lv

## Slide 2: Aspect #1
Motivation: to verify if using high-resolution reconstruction after RPR as input is possible at the scaling ratios of 2x and 1.5x.
Key points:
Using the training scripts from NNLF, with the following differences:
  Input: use high-resolution reconstruction after RPR as input
  Dataset: exclude low-resolution videos and does not include scaled images in DIV2K.
The training method is same as that used in the NNLF LOP training stage Ⅲ.
Two separate models for 2x and 1.5x.
Complexity: 13kMAC/pxl, 0.05M

## Slide 3: Aspect #2
Motivation: to design a single network to handle different scaling ratios.
Key points:
Using the training scripts from NNLF, with the following differences:
  Input: use high-resolution reconstruction after RPR as input, and adds scaling ratio as an input.
  Dataset: exclude low-resolution videos and does not include scaled images in DIV2K.
The training method is same as that used in the NNLF LOP training stage Ⅲ.
Single model for 2x and 1.5x.
Complexity: 13kMAC/pxl, 0.05M

## Slide 4: Results
Aspect #1 (two models)
Results of aspect #1 (2x)
Results of aspect #1 (1.5x)
 | AI Main10 |  |  | RA Main10 |  | 
 | Y-PSNR | U-PSNR | V-PSNR | Y-PSNR | U-PSNR | V-PSNR
Class A1 | -2.71% | -1.52% | -0.92% | -5.34% | -0.28% | -2.09%
Class A2 | -4.55% | 3.35% | 4.75% | -2.45% | 5.76% | 8.19%
Avg. A1 & A2 | -3.63% | 0.91% | 1.92% | -3.89% | 2.74% | 3.05%
Aspect #2 (single model)
Results of aspect #2 (2x)
Results of aspect #2 (1.5x)
 | AI Main10 |  |  | RA Main10 |  | 
 | Y-PSNR | U-PSNR | V-PSNR | Y-PSNR | U-PSNR | V-PSNR
Class A1 | -2.91% | 1.69% | 2.46% | -5.10% | -1.24% | -1.06%
Class A2 | -4.03% | 1.59% | 4.17% | -2.32% | 4.39% | 4.66%
Avg. A1 & A2 | -3.47% | 1.64% | 3.31% | -3.71% | 1.58% | 1.80%
 | AI Main10 |  |  | RA Main10 |  | 
 | Y-PSNR | U-PSNR | V-PSNR | Y-PSNR | U-PSNR | V-PSNR
Class A1 | -2.54% | -1.09% | -0.35% | -5.42% | 0.32% | 0.20%
Class A2 | -4.58% | 4.86% | 5.85% | -2.56% | 7.36% | 9.35%
Avg. A1 & A2 | -3.56% | 1.89% | 2.75% | -3.99% | 3.84% | 4.77%
 | AI Main10 |  |  | RA Main10 |  | 
 | Y-PSNR | U-PSNR | V-PSNR | Y-PSNR | U-PSNR | V-PSNR
Class A1 | -2.94% | 2.41% | 3.46% | -5.16% | -0.86% | 0.59%
Class A2 | -4.00% | 2.58% | 5.29% | -2.30% | 5.05% | 5.08%
Avg. A1 & A2 | -3.47% | 2.49% | 4.38% | -3.73% | 2.09% | 2.84%

## Slide 5: Conclusion
Proposed to introduce an unified NNSR method to handle different scaling ratios.
It is suggested to investigate in the next round of EE1.

## Slide 6
THANK
YOU