## Slide 1: Carriage of depth and alpha maps as HEVC single-layer bitstreams JVET-AG0144-v3
E. Thomas, E. Potetsianakis, E. Alexiou, R. Ghaznavi-Youvalari, M. Abdoli, M-L. ChampeL 01/25/2024

## Slide 2: 1. Background: XR rendering
XR application
Display
XR runtime
Texture
Eye buffer
Alpha channel
Depth map
View
Depth map are essential in AR to stabilise the virtual objects in the real world but also for lighting, other techniques etc.
Alpha channel is required in AR for video see-through device to alpha blend the view with the captured real-world scene.
More information can be found in the OpenXR specification (link)
Renderer
Sensor data reading

## Slide 3: 1. Background: Split rendering concept
XR remote renderer
XR application
Display
XR runtime
Renderer
Views
Eye buffer
Sensor data reading
XR application
Display
XR runtime
Renderer
Views
Eye buffer
Sensor data reading
Local XR rendering
XR split rendering
Network
The views are transmitted over the network

## Slide 4: 1. Background: 3GPP HEVC split rendering
Split rendering server
XR application
Display
XR runtime
Texture
Eye buffer
Alpha channel
Depth map
View
Overview of 3GPP SA4 split rendering service*
HEVC RTP stream
HEVC RTP stream
HEVC RTP stream
View reception and decoding
* See 3GPP SA4 TS 26.565 Split Rendering Media Service Enabler (link) for more details

## Slide 5: 2. Design goals
Enabling depth and alpha maps in HEVC single-layer bitstream by signalling:
Indication that the bitstream carries a depth map sequence or an alpha map sequence.
Indication on the mapping used between the depth/alpha map (mono-channel) and the luma and chroma components.
Information specifying how to interpret the sample values from the decoded pictures to reconstruct the depth/alpha maps.

## Slide 6: 3. Possible solutions for design goal #1
  Adding colour_primaries code points in CICP. (based on JVET-AG0308)
1. Information indicating that the bitstream carries a depth map sequence or an alpha map sequence.
Note: See Word contribution in JVET-AG0144 for entire spec text

## Slide 7: 3. Possible solutions for design goal #2
  Adding matrix_coeffs code points for mono-channel (luma only) in CICP. (based on JVET-AG0308)
2. Indication on the mapping used between the depth/alpha map (mono-channel) and the luma and chroma components.
Note: See Word contribution in JVET-AG0144 for entire spec text
…

## Slide 8: 3. Possible solutions for design goal #3
  Modifications of existing SEI messages to be used in the single layer context.
3. Information specifying how to interpret the sample values from the decoded pictures to reconstruct the depth/alpha maps.
Example changes in the depth representation SEI message:
When present, the depth representation information SEI message shall be associated with either:
one or more layers with AuxId value equal to AUX_DEPTH
a layer with primary pictures carrying depth maps
The syntax elements in the depth representation information SEI message specify various parameters for auxiliary pictures of type AUX_DEPTH or non-auxiliary pictures carrying depth maps. Those parameters are signalled for the purpose […]
See Word contribution for full text changes.

## Slide 9: Conclusion
Split rendering is critical for XR applications.
3GPP SA4 is developing a split rendering service specification.
This service requires multiple RTP HEVC streams for texture sequence and depth and alpha map sequences.
Solutions are proposed to enable HEVC single layer carriage of depth and alpha maps based on CICP code points and modifications of existing HEVC depth and alpha SEI messages.
We recommend documenting the solution in the relevant draft specification documents.