## Slide 1: EE2-related: Chroma LIC derivation with template costs
Tae Meon Bae
Sachin Deshpande
JVET-AG0172

## Slide 2: Introduction
In ECM 11, one LIC flag of CU applies to all color components of CU.
  The separate control of LIC for each color component could achieve additional coding gain.
  Controlling LIC for each color component increases encoding time and requires additional signaling of LIC flags for each color components.
Proposal
  Use separate chroma LIC flags for chroma components
  Derive chroma LIC flags based on template costs

## Slide 3: Proposed Method
LIC process for chroma components are controlled by chroma LIC flags when the LIC flag of CU is on.
  The LIC flag of CU controls Luma LIC activation. When the LIC flag of CU is disabled, chroma LIC flags are also disabled.
  When the LIC flag of CU is enabled, each chroma LIC flag determines whether to apply LIC to the color component.
Derivation of Chroma LIC flags:
  Apply the approach based on JVET-AF0128 in deriving chroma LIC flags
  Determine LIC flag based on the ratio of SAD/MRSAD of template.
  The chroma LIC flag is set to be false, if SAD/MRSAD < threshold.

## Slide 4: Simulation results
 | Low delay B Main10 |  |  |  | 
 | Over ECM-11.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.03% | 0.46% | 0.32% | -% | -%
Class C | 0.00% | 0.25% | 0.06% | 100.9% | 99.3%
Class E | -0.24% | -0.04% | -0.18% | 100.0% | 98.1%
Overall | -0.07% | 0.26% | 0.11% | -% | -%
Class D | -0.05% | -0.38% | -0.34% | 99.2% | 97.5%
Class F | -0.09% | -0.40% | -0.23% | -% | -%
Table 1: Coding performance of the proposed method.

## Slide 5: Conclusion
This contribution proposes deriving chroma LIC flags based on the template costs. The proposed method brings -0.24% coding gain for class E in LB.
Implementation of SAD and MRSAD is not optimized.
It is suggested to further study the proposed method in EE2.

## Slide 6
Thank you.