## Slide 1: AHG9/AHG16: On chroma key fusion for the generative face video SEI message
JVET-AI0194
Shiv Gehlot, Guan-Ming Su, Peng Yin, Sean McCarthy, Gary J. Sullivan

## Slide 2: Outline
Discussion of previous contribution (JVET-AH0118) and meeting notes
Illustration and examples of use of chroma key for fusion in the GFV SEI message
Proposed syntax and semantics

## Slide 3: Introduction
JVET-AH0118
  proposed a method of fusing generated face pictures with background pictures to mitigate artifacts.
  Required both encoder and receiver to contain a background segmentation process
During the discussion at the 34th JVET meeting
  It was noted that mismatch between segmentation at encoder and receiver could cause artifacts
  It was asked if chroma key could be used to avoid mismatch artifacts
This contribution proposes syntax and semantics to support chroma key in the GFV SEI message

## Slide 4: Use of chroma key for fusion in the GFV SEI message
VVC Encoder
Base Picture
Background Base Picture
Segmented Driving Pictures
foreground + chroma key background
Compact Features Representation
Segmentation
Inpainting
VVC Decoder
Decoded Base Picture
foreground + chroma key background
Motion Estimation and Frame Generation
Chroma-key fusion
Generated Segmented Driving Pictures
foreground + chroma key background
Background Stabilized Driving Pictures
Encoder
Receiver
Decoded Background
Base Picture
Base Picture
foreground + chroma key background
In this example, the green chroma key background colour corresponds to RGB values of 0, 177, and 64, respectively
Segmentation not needed in receiver

## Slide 5: C012
Original CFTE without picture fusion (QP=22):10.4kbps CFTE with chroma key picture fusion (QP=22):10.5kbps

## Slide 6: C018
Original CFTE without picture fusion (QP=22):9.6kbps CFTE with chroma key picture fusion (QP=22):10.4kbps

## Slide 7: V010
Original CFTE without picture fusion (QP=22): 6.2kbps CFTE with chroma key picture fusion (QP=22): 6.1kbps

## Slide 8: C007
Original CFTE without picture fusion (QP=22): 10.2kbps CFTE with chroma key picture fusion (QP=22): 9.7kbps

## Slide 9: V001
Original CFTE without picture fusion (QP=22):5.5kbps CFTE with chroma key picture fusion (QP=22):5.7kbps

## Slide 10: Proposed generative face video SEI message syntax
generative_face_video ( payloadSize ) { | Descriptor
gfv_id | ue(v)
gfv_cnt | ue(v)
gfv_base_pic_flag /*indicate if current decoded output picture is a base picture*/ | u(1)
if( gfv_base_pic_flag ) { /*specify TranslatorNN( )*/ | 
gfv_nn_present_flag | u(1)
if( gfv_nn_present_flag ) { | 
… | 
} | 
gfv_chroma_key_info_present_flag | u(1)
if( gfv_chroma_key_info_present_flag ) { | 
for( c = 0; c < 3; c++ ) { | 
gfv_chroma_key_value_present_flag[ c ] | u(1)
if( gfv_chroma_key_value_present_flag[ c ] ) | 
gfv_chroma_key_value[ c ] | u(8)
} | 
for( i = 0; i < 2; i++ ) { | 
gfv_chroma_key_thr_present_flag[ i ] | u(1)
if( gfv_chroma_key_thr_present_flag[ i ] ) | 
gfv_chroma_key_thr_value[ i ] | ue(v)
} | 
} | 
} else /* current decoded output picture is a driving picture*/ | 
… | 
} | 
modelled on the chroma key information function specified in ITU-T H.263

## Slide 11: Proposed generative face video SEI message semantics (1 of 2)
gfv_chroma_key_info_present_flag equal to 1 indicates that the syntax elements gfv_chroma_key_value_present_flag[ c ] and gfv_chroma_key_thr_present_flag[ i ] are present and the syntax elements and gfv_chroma_key_value[ c ] and gfv_chroma_key_thr_value[ i ] might be present. gfv_chroma_key_info_present_flag equal to 0 specifies that the syntax elements gfv_chroma_key_value_present_flag[ c ], gfv_chroma_key_thr_present_flag[ i ], gfv_chroma_key_value[ c ], and gfv_chroma_key_thr_value[ i ] are not present.
gfv_chroma_key_value_present_flag[ c ] equal to 1 indicates that the syntax element gfv_chroma_key_value[ c ] is present. gfv_chroma_key_present_flag[ c ] equal to 0 indicates that the syntax element gfv_chroma_key_value[ c ] is not present.
The variable ChromaKeyDefaultValueFlag is set equal to !( gfv_chroma_key_value_present_flag[ 0 ] | | gfv_chroma_key_value_present_flag[ 1 ] | | gfv_chroma_key_value_present_flag[ 2 ] ).
gfv_chroma_key_value[ c ] specifies the chroma key value corresponding to the c-th colour component as follows:
– If ChromaKeyDefaultValueFlag is equal to 1, the variables GfvChromaKeyValue[ c ] are specified as follows:
– GfvChromaKeyValue[ 0 ] is set equal to 50
– GfvChromaKeyValue[ 1 ] is set equal to 220
– GfvChromaKeyValue[ 2 ] is set equal to 100
– Otherwise, ChromaKeyDefaultValueFlag is equal to 0, the following applies:
– if gfv_chroma_key_value_present_flag[ c ] is equal to 1, GfvChromaKeyValue[ c ] is set equal to the value of gfv_chroma_key_value[ c ]
– otherwise, gfv_chroma_key_value_present_flag[ c ] is equal to 0, GfvChromaKeyValue[ c ] is not specified by this Specification.

## Slide 12: Proposed generative face video SEI message semantics (2 of 2)
gfv_chroma_key_thr_present_flag[ i ] equal to 1 indicates that the syntax element gfv_chroma_thr_value[ i ] is present. gfv_chroma_key_thr_present_flag[ i ] equal to 0 indicates gfv_chroma_key_thr_value[ i ] is not present.
gfv_chroma_key_thr_value[ i ], when present, specifies the i-th chroma key threshold value. When not present, the value of gfv_chroma_key_thr_value[ i ] is inferred as follows:
If i is equal to 0, gfv_chroma_key_thr_value[ 0 ] is set equal to 48
Otherwise, i is equal to 1, gfv_chroma_key_thr_value[ 1 ] is set equal to 75
NOTE – The syntax elements gfv_chroma_key_value_present[ c ], gfv_chroma_key_value[ c ], and gfv_chroma_key_thr_value[ i ] could be used to determine a transparency indicator for fusion of the generated face picture and background picture. For example, a transparency indicator, denoted as alpha[ x ][ y ] , for picture sample value, denoted as I[ c ][ x ][ y ] with bitDepth[ c ], where bitDepth[ 0 ] is equal to BitDepthY, bitDepth[ 1 ] and bitDepth[ 2 ] are equal to BitDepthC, and GfvChromaKey[ c ] values for sample coordinates x, y, and colour components c could be determined as follows:
d[ x ][ y ]= 0 for( c = 0; c < 3; c++ ) if( gfv_chroma_key_value_present[ c ] | | ChromaKeyDefaultValueFlag ) d[ x ][ y ] += ( I[ c ][ x ][ y ] / ( 1 << (bitDepth[ c ] – 8) ) − GfvChromaKeyValue[ c ] )2 (XX) if ( ( d[ x ][ y ] < gfv_chroma_key_thr_value[ 0 ] ) alpha[ x ][ y ] = 0 else if ( ( d[ x ][ y ] > gfv_chroma_key_thr_value[ 1 ] ) alpha[ x ][ y ] = 1 else alpha[ x ][ y ] = ( d[ x ][ y ] - gfv_chroma_key_thr_value[ 0 ] ) ÷ ( gfv_chroma_key_thr_value[ 1 ] - gfv_chroma_key_thr_value[ 0 ] )
A value of alpha[ x ][ y ] equal to 0 could indicate transparency. A value of alpha[ x ][ y ] equal to 1 could indicate opacity. Intermediate values of alpha[ x ][ y ] could indicate semitransparency.

## Slide 13: Conclusion
It is recommended to adopt the proposed syntax and semantics to support chroma key for the generative face video SEI message into the next version of VSEI.