## Slide 1: JVET-AI0324 AHG12: temporal ALF
Luhang Xu, Yue Yu, Haoping Yu, Dong Wang

## Slide 2: Proposed method (1/2)
The temporal ALF (TALF) is placed between SAO and ALF to improve performance of the current loop filters.
TALF has four filtering types:
    Uni-filtering mode 1, it uses the integerized uni-Mv and reference picture information to obtain the offset positions in the reference picture and uses those positions for the temporal uni-filtering.
    Uni-filtering mode 2, it uses the reference picture information to obtain the collocated positions in the reference picture for the temporal uni-filtering.
    Bi-filtering mode 1, it uses the integerized bi-Mvs and reference picture information to obtain the offset positions in the two reference pictures and uses those positions for temporal bi-filtering.
    Bi-filtering mode 2, it uses the reference picture information to obtain the collocated positions in the two reference pictures for the temporal bi-filtering.

## Slide 3: Proposed method (2/2)
The uni-directional filter is a 13-coefficient symmetric and diamond-shaped filter. The bi-directional filters are two 7-coefficient, symmetric and diamond-shaped filters.
TALF can reuse the history filters. Two history tables with max size equal to 8 are used to maintain the history uni-directional or bi-directional filters.
The adaptive precision and the non-linear clipping for ALF are also implemented in TALF.

## Slide 4: Simulation results
proposed method over ECM-13.0 (Without SIMD implementation):
 | Random Access Main 10 |  |  |  |  |  | 
 | Over ECM-13.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class B | -0.19% | 0.14% | -0.02% | #DIV/0! | #DIV/0! | #DIV/0! | #DIV/0!
Class C | -0.03% | 0.07% | 0.06% | 101.4% | 106.7% | 101.1% | 100.6%
Class D | -0.05% | 0.12% | 0.29% | 101.8% | 108.5% | 100.0% | 100.2%
Class F | -0.23% | 0.15% | 0.11% | #DIV/0! | #DIV/0! | #DIV/0! | #DIV/0!
 | Low delay B Main 10 |  |  |  |  |  | 
 | Over ECM-13.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class B | -0.15% | 0.16% | 0.13% | #DIV/0! | #DIV/0! | #DIV/0! | #DIV/0!
Class C | -0.09% | 0.17% | -0.30% | #DIV/0! | #DIV/0! | #DIV/0! | #DIV/0!
Class E | -0.09% | 0.47% | 0.72% | #DIV/0! | #DIV/0! | #DIV/0! | #DIV/0!
Overall | -0.11% | 0.24% | 0.14% | #DIV/0! | #DIV/0! | #DIV/0! | #DIV/0!
Class D | -0.21% | -0.04% | 0.40% | #DIV/0! | #DIV/0! | #DIV/0! | #DIV/0!

## Slide 5: Conclusions
This contribution proposes TALF in the loop filtering:
  Uni-directional and bi-directional filtering are proposed,
  The reusing of history filters, the non-linear clipping and the adaptive precision are included in TALF.
The partial results show coding performance improvement beyond the ECM-13.0.
It is suggested to further study the proposed method in EE2.