## Slide 1: Block-based filter adaptation with intra prediction mode and CU depth information
JCTVC-G463
Shiqi Wang
Siwei ma
Jie Jia

## Slide 2: Summary
Simplification of filter adaptation in BA-ALF for intra slices
Intra prediction modes, CU depth information and PU sizes are used instead of calculating diretional and Laplacian features
Reduction on the # of operations for each 4x4 block
  48  3
Performance (All-Intra High Efficiency)
  Decoding time reduction : 2% (3% is reported from cross check)
  0.1% BD loss

## Slide 3: BA Filter adaptation in HM 4.0
H(i,j) = abs ( X(i,j)<<1 - X(i,j-1) - X(i,j+1) )
V(i,j) = abs ( X(i,j)<<1 - X(i-1,j) - X(i+1,j) )
H’B = ∑i=0,2 ∑j=0,2 H(i,j)
V’B = ∑i=0,2 ∑j=0,2 V(i,j)
L’B = H’B + V’B
avgVar = max{ 15, (LB * 1024) >> (3 + BitDepthY) }
 | avgVar |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
dir 0 | 0 | 1 | 2 | 2 | 2 | 3 | 3 | 3 | 3 | 3 | 4 | 4 | 4 | 4 | 4 | 4
dir 1 | 5 | 6 | 7 | 7 | 7 | 8 | 8 | 8 | 8 | 8 | 9 | 9 | 9 | 9 | 9 | 9
dir 2 | 10 | 11 | 12 | 12 | 12 | 13 | 13 | 13 | 13 | 13 | 14 | 14 | 14 | 14 | 14 | 14
Filter Index
Filter indexes are obtained from
  Directional and Laplacian features of sub-sampled pixel positions

## Slide 4: Proposed BA Filter Adaptation
Logical prediction modes | Filter Group
DC, Planar | 0
10~17 | 1
1~9 | 2
18~24 | 3
25~33 | 4
 |  | Class(L) |  | 
 |  | 0 | 1 | 2
Filter Group | 0 | 0 | 1 | 2
 | 1 | 5 | 4 | 3
 | 2 | 6 | 7 | 8
 | 3 | 11 | 10 | 9
 | 4 | 12 | 13 | 14
Filter Index
Filter indexes are obtained from
  CU depth and PU size
  intra prediction modes

## Slide 5: Complexity analysis
 |  | H(i,j) and V(I,j) | H'B and V'B | L'B | Filt_Num calc | Total
Operation | Addition | 16 | 6 | 1 | 3 | 26
 | Shift | 4 |  | 1 | 5 | 10
 | Comparison |  |  |  | 4 | 4
 | Absolute | 8 |  |  |  | 8
LUT access |  |  |  |  | 1 (size 16) | 1
 |  | Prediction mode Grouping | L | class(L) | Filt_Num calc | Total
Operation | Addition |  | 1 |  | 3 1 | 7 1
 | Shift |  |  |  | 1 | 
 | Comparison |  | 1 |  | 1 | 2
 | Absolute |  |  |  |  | 
LUT access |  | 1 (size 35) | 1(size 5) | 1 (size 5) | 1(size 5) | 2 4
48 operations and 1 LUT access
7 3 operations and 2 4 LUT access
<HM 4.0>
<Proposed>
For derivation of filter indexes,

## Slide 6: Experimental Results
 | Intra |  | 
 | Y BD-rate | U BD-rate | V BD-rate
Class A | 0.26% | 0.03% | 0.03%
Class B | 0.10% | 0.00% | 0.00%
Class C | 0.07% | 0.03% | 0.04%
Class D | 0.05% | -0.02% | -0.02%
Class E | 0.13% | -0.01% | -0.02%
All | 0.12% | 0.01% | 0.01%
Enc (%) | 100% |  | 
Dec (%) |  | 98% | 
Anchor : HM 4.0 with RD-cost advantage on RA
Tested : Proposed w/o RD-cost advantage on RA

## Slide 7: Conclusion
This contribution proposes a simplified block-based filter adaption method which avoids the variance calculation in BA ALF for intra slice.
The proposed method reports 2% decoding time reduction with 0.1% BD-rate loss for All intra HE case compared with HM 4.0. Meanwhile, no syntax change is required.