## Slide 1: 2D/3D compatibility for Stereo 3D using Frame packing arrangement SEI
JCTVC-I0058
O. Nakagami and T. Suzuki
Sony Corporation
Joint Collaborative Team on Video Coding (JCT-VC) of ITU-T SG 16 WP 3 and ISO/IEC JTC 1/SC 29/WG 11
9th Meeting: Geneva, CH, 27 April – 7 May 2012

## Slide 2: Introduction
Stereo 3D using Frame packing arrangement SEI (FPA_SEI)
Left
Right
Right
Left
side-by-side
frame sequential
Left
Right
top-bottom
when decoders do not support
the FPA_SEI
when decoders support
the FPA_SEI
Works fine.
Always output the packed stereo.
+
Other packing type
To support SEI is not mandatory.
In this contribution, methods to output only the base-view are proposed. Thus, 2D/3D compatibility for some packing types are achieved.
Notes: Stereo 3D coding is supported in the current draft by using frame packing arrangement SEI (FPA_SEI).
Such frame packing stereo 3D is beneficial because all HEVC ver. 1 decoders can decode the stereo 3D bitstream.
However, one issue is compatibility among decoders.
Since decoding SEI message is not mandatory process in the draft, some decoders, which do not decode FPA_SEI, output the decoded pictures directly as the packed frame.
When the output display is a 2D display, such result is not desirable.
On the other hand, decoders, which support FPA_SEI, output correctly for both 2D and 3D display.
Thus, the focus of the proposal is on decoders which do not decode FPA_SEI.
It’s conceivable that the most part of decoders belong to this category because the most output devices still support 2D only.
In order to resolve these situations, the contribution proposes three alternative methods to realize the 2D compatibility among decoders for frame packing stereo 3D.

## Slide 3: 3 method to realize 2D/3D compatibility
 |  | 2D/3D compatibility |  |  | Burden for decoders which are not interested in FPA_SEI
 |  | Frame sequential | side-by-side, top-bottom | Other packing method | 
HM6.0/CD |  | No | No | No | -
1 | Change decoder process to support FPA_SEI | Yes | Yes | Yes | Yes
2 | Modify decoding process for FPA_SEI | Yes by using max_temporal_id_minus1 | Yes by using cropping or syntax | No | No
3 | Assign a new nal_unit_type for Frame packing Stereo 3D | Yes | No | No | No

## Slide 4: Method1: Change decoder process to support FPA_SEI
Add a 1-bit flag in VUI to indicate the existence of Frame packing arrangement SEI in the AU.
And give a strict definition for the flag.
frame_packing_arrangement_indication_presence_flag equal to 1 specifies that a Frame packing arrangement SEI message shall be present in the bitstream (or in the same AU). When the flag equal to 1, decoders should support the SEI message.
SPS
FPA_
SEI
VUI
frame_packing_arrangement_indication_presence_flag
vui_parameters_present_flag
Notes: Define FPA_SEI as a mandatory process
A 1-bit flag, named as frame_packing_arrangement_indication_presence_flag, is added in VUI.
The flag represents that FPA_SEI message exists in the bistream or in the same AU. The flag enables decoders to parse the SEI easier.
Furthermore, when the flag is true, all decoders shall decode FPA_SEI as a mandatory process.
Method1 enables all decoders to know the base view part in the bitstream, and can output the base view only if necessary.
However, note that method1 isHowever, it is noted that method1 is a burden for decoders which are not interested in frame packing 3D.

## Slide 5: Method2-1 Cropping & Side-by-side (Top-bottom)
Add a 1-bit flag in VUI to indicate the existence of Frame packing arrangement SEI in the AU.(Same as method1)
Set pic_cropping_flag equal to 1 and the offset to crop the base-view area in SPS
  → Decoders, which don’t support FPA_SEI, output only base-view.
When frame_packing_arrangement_indication_presence_flag is true and the FPA_SEI is pursed, the decoders shall infer pic_cropping_flag is equal to be 0 and ignore picture cropping information.
  → Decoders, which support FPA_SEI, can decode with keeping regulations.
SPS
FPA_
SEI
VUI
change pic_cropping_flag info.
frame_packing_arrangement_indication_presence_flag
vui_parameters_present_flag
Left
Right
side-by-side
cropping
Notes: Method2 uses SPS/NAL syntax for the 2D compatibility
Add a 1-bit flag in VUI to indicate the existence of FPA_SEI in the AU. (Same as method1)
In Side-by-side (Top-bottom) case,
Cropping syntax is used to realize the compatibility.
Set pic_cropping_flag equal to 1 and offset to crop the base view area in SPS.
→ Decoders, which do not support FPA_SEI, outputs only the base-view as a result ofthe cropping
When frame_packing_arrangement_indication_presence_flag is true and frame_packing_arrangement_type is equal to 3 or 4, the decoders shall infer pic_cropping_flag is equal to be 0 to ignore picture cropping information.
→ Decoders, which support FPA_SEI, decode both views.
Note- This process is necessary for the conformance because the cropping operation is a mandatory process.

## Slide 6: Method2-2 temporal_id & Frame sequential
Add a 1-bit flag in VUI to indicate the existence of Frame packing arrangement SEI in the AU.(Same as method1)
Set max_temporal_id_minus1 equal to the maximum temporal_id minus 1 of Left view in SPS
  → Decoders, which don’t support FPA_SEI, decode only base-view.
When frame_packing_arrangement_indication_presence_flag is true and the FPA_SEI is read, max_temporal_id_minus1 in SPS is overwritten by a value in SEI as the maximum temporal_id minus 1 of Right view.
SPS
FPA_
SEI
VUI
overwrite max_temporal_id_minus1
frame_packing_arrangement_indication_presence_flag
vui_parameters_present_flag
L
R
L
R
temporal_id
POC
Max_t_L
L
Max_t_R
drop
Notes: Frame sequential case
Temporal scalability (temporal_id) is used to realize the compatibility.
Assign lower temporal_id to the base view picture, and higher temporal_id to the additional view picture. For example, the base view pictures are encoded with temporal_id lower than or equal to 3, and the additional view pictures are encoded with temporal_id larger than 3.
Set max_temporal_id_minus1 equal to the maximum temporal_id minus 1 of the base view in SPS. In the above example, set max_temporal_id_minus1 equal to 2.
→ Decoders, which do not support FPA_SEI, decode only base-view due to the max_temporal_id_minux1 syntax.
When frame_packing_arrangement_indication_presence_flag is true and frame_packing_arrangement_type is equal to 5, max_temporal_id_minus1 in SPS is updated by a value in the SEI(*) as the maximum temporal_id minus 1 of the additional view.
→ Decoders, which support FPA_SEI, decode both views with keeping regulations.
(*) See JCTVC-I0057 for the proposed syntax and semantics.

## Slide 7: Method3 Assign new nal_unit_type for Frame packing Stereo 3D
Assign nal_unit_type=X for the base-view, where X belongs to any nal_unit_type defined in the current draft.
Assign nal_unit_type=Y for the additional-view, where Y is a new nal_unit_type for 3D.
→ Decoders, which don’t support nal_unit_type=Y, drop Right-view.
→ Decoders, which support nal_unit_type=Y, can decode both view.
In Method3, Frame sequential is only supported.
Right
nal_unit_type=Y
Left
nal_unit_type=X
Right
nal_unit_type=Y
Left
nal_unit_type=X
POC
Decoders, which don’t support nal_unit_type=Y, drop Right-view.
Notes: Method3 Define a new nal_unit_type for 3D
Assign nal_unit_type=X for the base view picture, where X is any nal_unit_type for coded slice defined in the current draft.
Assign nal_unit_type=Y for the additional view picture, where Y is a new nal_unit_type for 3D.
→ Decoders, which do not support nal_unit_type=Y, decode only base view by dropping additional view.
→ Decoders, which support nal_unit_type=Y, decode both views.
Note that frame sequential is only supported in method3. For spatial packing 3D (side-by-side and top-bottom), decoders, which do not support the proposed nal_unit_type, do not decode at all. Thus, the 2D compatibility is not realized for spatial packing 3D.

## Slide 8: 3 method to realize 2D/3D compatibility
 |  | 2D/3D compatibility |  |  | Burden for decoders which are not interested in FPA_SEI
 |  | Frame sequential | side-by-side, top-bottom | Other packing method | 
HM6.0/CD |  | No | No | No | -
1 | Change decoder process to support FPA_SEI | Yes | Yes | Yes | Yes
2 | Modify decoding process for FPA_SEI | Yes by using max_temporal_id_minus1 | Yes by using cropping or syntax | No | No
3 | Assign a new nal_unit_type for Frame packing Stereo 3D | Yes | No | No | No
Notes: Method2 requires encoder trick to generate bitstream. And decoders, which support FPA_SEI, need to modify decode process.
However, the most decoders, which do not support FPA_SAI, can output 2D view without changing decoding process. Also, by the proposed definition of frame_packing_arrangement_indication_presence_flag, the decoder conformance is satisfied.
Furthermore, method2 supports both spatial and temporal packing.

## Slide 9: Conclusion
Method2 realizes 2D/3D compatibility with the minimum change of decode procedure of the three.
Proposed modification for method2
  Add a 1-bit flag in VUI which represents the existence of the Frame packing arrangement SEI in the same AU.
  To realize compatibility,
    For side-by-side (top-bottom)coding, cropping info. in SPS are discarded by the SEI.
    For frame sequential coding, max_temporal_id in SPS are overwritten by a parameter in the SEI.