## Slide 1: Refinement for SAO and ALF syntax in the APS
Semih Esenlik
Matthias Narroschke
Thomas Wedi
Panasonic Corporation
9th JCT-VC meeting, Geneva 27.April-07.May 2012

## Slide 2: Summary
Proposal
Change the name and semantics of the following syntax elements in APS:
  sao_num_lcu_in_width_minus1
  sao_num_lcu_in_height_minus1
  alf_num_lcu_in_width_minus1
  alf_num_lcu_in_height_minus1
Benefits
Coding gain for SAO in APS signalling mode
  0.1% average gain for 64x64 LCU
  0.4% average gain for 16x16 LCU

## Slide 3: Explanation for SAO
Modification for ALF syntax is the same

## Slide 4
Background: SAO parameter set in APS
aps_sao_param( ) { | Descriptor
sao_cb_enable_flag | u(1)
sao_cr_enable_flag | u(1)
sao_num_lcu_in_width_minus1 | ue(v)
sao_num_lcu_in_height_minus1 | ue(v)
sao_one_luma_unit_flag | u(1)
if(sao_one_luma_unit_flag) | 
sao_offset_vlc( 0, 0, 0 ) | 
if( sao_cb_enable_flag ){ | 
sao_one_cb_unit_flag | u(1)
if( sao_one_cb_unit_flag ) | 
sao_offset_vlc( 0, 0, 1 ) | 
} | 
if( sao_cr_enable_flag ){ | 
sao_one_cr_unit_flag | u(1)
if( sao_one_cr_unit_flag ) | 
sao_offset_vlc( 0, 0, 2 ) | 
} | 
for( ry = 0; ry <= sao_num_lcu_in_height_minus1; ry++ ) { | 
for( rx = 0; rx <= sao_num_lcu_in_width_minus1; rx++ ) { | 
if( aps_sample_adaptive_offset_flag && ! sao_one_luma_unit_flag ) { | 
if( ry > 0 && rx = = 0 ) | 
sao_repeat_row_flag[ 0 ] | u(1)
sao_unit_vlc(rx, ry, 0 ) | 
} | 
if( sao_cb_enable_flag && ! sao_one_cb_unit_flag ) { | 
if( ry > 0 & & rx = = 0 ) | 
sao_repeat_row_flag[ 1 ] | u(1)
sao_unit_vlc(rx, ry, 1 ) | 
} | 
if( sao_cr_enable_flag & & !sao_one_cr_unit_flag ) { | 
if( ry > 0 & & rx = = 0 ) | 
sao_repeat_row_flag[ 2 ] | u(1)
sao_unit_vlc( rx, ry, 2 ) | 
} | 
} | 
} | 
} | 
Required for parsing
For each LCU, one SAO parameter unit is sent

## Slide 5
Problem
Semantics
  sao_num_lcu_in_width_minus1 plus 1 specifies the number of coding treeblocks in picture width.
  sao_num_lcu_in_height_minus1 plus 1 specifies the number of coding treeblocks in picture height.
Problems
  Duplicate information just for parsing of an APS (APS does not have a link to SPS).
  Increase in bitrate due to semantics (one SAO parameter unit per each LCU).

## Slide 6
Due to the semantics;
One SAO parameter unit has to be signalled for each LCU.
Picture partitioning is inefficient due to repeated “merge left” and “merge up” flags (same problem with run coding and repeat row flags).
Picture frame
Problem

## Slide 7
Proposal
aps_sao_param( ) { | Descriptor
sao_cb_enable_flag | u(1)
sao_cr_enable_flag | u(1)
sao_num_units_in_width_minus1 | ue(v)
sao_num_units_in_height_minus1 | ue(v)
if (sao_num_units_in_width_minus1 ¦¦ sao_num_units_in_ height_minus1){ | 
sao_one_luma_unit_flag | u(1)
if(sao_one_luma_unit_flag) | 
sao_offset_vlc( 0, 0, 0 ) | 
if( sao_cb_enable_flag ){ | 
sao_one_cb_unit_flag | u(1)
if( sao_one_cb_unit_flag ) | 
sao_offset_vlc( 0, 0, 1 ) | 
} | 
if( sao_cr_enable_flag ){ | 
sao_one_cr_unit_flag | u(1)
if( sao_one_cr_unit_flag ) | 
sao_offset_vlc( 0, 0, 2 ) | 
} | 
} | 
for( ry = 0; ry <= sao_num_units_in_ height_minus1; ry++ ) { | 
for( rx = 0; rx <= sao_num_units_in_width_minus1; rx++ ) { | 
if( aps_sample_adaptive_offset_flag && ! sao_one_luma_unit_flag ) { | 
if( ry > 0 && rx = = 0 ) | 
sao_repeat_row_flag[ 0 ] | u(1)
sao_unit_vlc(rx, ry, 0 ) | 
} | 
if( sao_cb_enable_flag && ! sao_one_cb_unit_flag ) { | 
if( ry > 0 & & rx = = 0 ) | 
sao_repeat_row_flag[ 1 ] | u(1)
sao_unit_vlc(rx, ry, 1 ) | 
} | 
if( sao_cr_enable_flag & & !sao_one_cr_unit_flag ) { | 
if( ry > 0 & & rx = = 0 ) | 
sao_repeat_row_flag[ 2 ] | u(1)
sao_unit_vlc( rx, ry, 2 ) | 
} | 
} | 
} | 
} | 

## Slide 8: Proposed semantic changes
      7.4.2.6 Sample adaptive offset parameter semantics
sao_num_unitslcu_in_width_minus1 plus 1 specifies the number of coding treeblocksSAO parameter units in picture width.
sao_num_unitslcu_in_height_minus1 plus 1 specifies the number of coding treeblocksSAO parameter units in picture height.
7.4.2.8 Sample adaptive offset VLC semantics
sao_type_idx[ cIdx ][ rx ][ ry ] indicates the offset type as specified in Table 7‑6 of current coding treeblock at position rx Ctbx and ry Ctby for the colour component cIdx where;.
rx = floor (((Ctbx + 1) * (sao_num_units_in_width_minus1 + 1)) / num_LCU_in_width) – 0.0001)
ry = floor (((Ctby + 1) * (sao_num_units_in_height_minus1 + 1)) / num_LCU_in_height) – 0.0001)
Coding treeblock coordinates are used to calculate SAO parameter unit coordinates

## Slide 9
Proposal
sao_num_units_in_width_minus1 = 3
sao_num_units_in_height_minus1 = 1
sao_num_units_in_width_minus1 = 1
sao_num_units_in_height_minus1 = 0
Encoder can choose to group LCUs

## Slide 10
Simulation results for SAO: LCU size 64x64
*Picture based encoding is used in all test cases.

## Slide 11
Simulation results for SAO: LCU size 16x16
*Picture based encoding is used in all test cases.

## Slide 12: Simulation Results for ALF
Staightforward extension to ALF

## Slide 13
Simulation results for ALF: LCU size 16x16
*Picture based encoding is used in all test cases.
*Runtime measuments not accurate.

## Slide 14
Simulation results for SAO & ALF: LCU size 16x16
*Picture based encoding is used in all test cases.
*Runtime measuments not accurate.

## Slide 15: Conclusion
Proposal
Change the name and semantics of the following syntax elements in APS:
  sao_num_lcu_in_width_minus1
  sao_num_lcu_in_height_minus1
  alf_num_lcu_in_width_minus1
  alf_num_lcu_in_height_minus1
Benefits
Coding gain for SAO in APS signalling mode
  0.1% average gain for 64x64 LCU
  0.4% average gain for 16x16 LCU