## Slide 1: JCT-VC M0215: Non-SCE4: Adaptive up-sampling of base layer picture using Simplified Separable bilateral filters
Jie Zhao, Kiran Misra, Andrew Segall
Presenter: Andrew Segall

## Slide 2: Outline
Introduction
Algorithms
  Use of separable Bilateral filtering in inter layer prediction
  Combined into upsampler and can be done in the same pass as upsampling
  Low complexity
Performance
Summary

## Slide 3: Introduction
Background:
  In SCE4.2.6, (JCTVC-M0213), we proposed an adaptive upsampling approach using 2D bilateral filter
  It shows good gain but with high complexity. (average 1.4% BD rate reduction for 2x cases, 0.3-0.5% rate reduction for other cases).
Goal:
  Improve upsampled based layer using “bilateral” filter aiming at preserving edge and reducing noise. – same as M0213.
  In addition, reduce complexity, and maintain the gain.

## Slide 4: Algorithm
When INTRA_BL mode is on, there are two versions of upsampled base layer pictures available for inter layer prediction
  The first base layer picture is from fixed upsampler of SHM 1.0,
  A second base layer picture generated by combined upsampling and a separable bilateral filter
  Does not apply to SNR case
Upsampler index is signaled at CU level when INTRA_BL mode is selected.
Encoder side: decided in checkRDCostIntraBL by RD decision.

## Slide 5: Algorithm
Main novelty/difference from our 2D bilateral filter proposal (M0213):
  Separable filter. Lower complexity and can be combined into upsampling process.
  In order to remove dependencies on neighboring pixels that are upsampled, only integer pel pixels and the current upsampled pixel are used in the bilateral filtering.
  No additional memory access. Can be done in the same pass as upsampling.

## Slide 6: Algorithm
In separable filters, the bilateral filter process can still be expressed using the 2D bilateral filter equations (shown on the right), except that filter supporting region is one dimensional in horizontal /vertical filtering step.
Ix,y , Ia,b denote the input pixel value at location (x,y) and (a,b) .
Ox,y denotes the output value at location (x,y). It is weighted average within a window.
Weight f() consists of spatial kernel S(a,b) and a gradient kernel and is related to both the gradient of a pixel at (a,b) to the input pixel at (x,y) and related to the distance to the input pixel.
G(Ia,b, Ix,y) denotes the gradient of the input at (a,b) relative to input at (x,y).
ϬR is a control parameter to adjust the weight based on the Gradient.
S(a,b) denotes a spatial kernel, which is typically a Gaussian kernel, to adjust the weight based on the distance of location (a,b) to the input location (x,y)

## Slide 7: Algorithm
Specifically, in this proposal we used 3x1 spatial kernel.
  Filtering integer pel Ai,j, it only uses Ai,j and 2 other neighbor integer pels.
  Filtering the upsampled pel bi,j it only uses the upsampled pel and 2 neighbor integer pels.
As shown in the equation, proposed filtering does not depend on other upsampled pixel.
Therefore, it can be done in the same pass as upsampling.
Fig. Illustration of 2X upsampled pixels.
Note: Ai,j denote integer pel, bi,j denote the upsampled pel

## Slide 8: Example Syntax
CU level on/off when INTRA_BL mode is selected.
Can be predicatively coded from a most probable upsampler index ( 0 or 1).
At high level, signal if bilateral filter is present or not.

## Slide 9: Experimental Result
SHM1.0 IntraBL framework.
SCE4 test configuration.
Used 1 fixed upsampler and 1 bilateral filter.
Decoder timing is from picture based implementation.
Note: timing information shown in the table are from our cross checker Samsung
which has homogenous cluster, so their timing information is more reliable.

## Slide 10: Experimental Result
Average 0.9/0.8/1.0% rate reduction for AI/RA/LD_P 2X cases.
0.2/0.0/0.3% rate reduction for AI/RA/LD_P 1.5X cases.

## Slide 11: Experimental Result
We also implemented CU based upsampler/filter at decoder side into SHM1.0 and into our test software.
1st tables shows the speedup of CU based upsampler vs. picture based upsampler in SHM1.0.
2nd table shows the decoder timing ratio of our proposed tool vs. SHM1.0 anchor, both using CU based upsampler.
Decoder Timing of SHM1.0 with CU based upsampler
vs. SHM1.0 with picture based upsampler
Decoder Timing of SHM1.0 with CU based upsampler
vs. SHM1.0 with picture based upsampler

## Slide 12: Complexity
In our test, we used 3x1 spatial kernel and a 9 level gradient kernel
Spatial kernel and gradient kernel in f(a,b,Ia,b, Ix,y) are combined into one look-up-table to reduce the number of multiplications. Division is also implemented as reciprocal look up.
The 3x1 bilateral filter equations shown before can be simplified as below. It takes 3 multiplication, and 5 additions (including 2 to calculate the gradient) to compute an output value.
Note: Ai,j denote integer pel, bi,j denote the upsampled pel

## Slide 13: Complexity (Worst Case)
To account for horizontal and vertical separable filters, it needs 9 multiplication and 15 addition for each sample (including both luma and chroma) in addition to the 37 multiplication and 32 adds from the fixed upsampler.
The worst case of Inter-Layer Prediction shown in the table on the right include both the fixed upsampler and the proposed tool.
No increase to memory bandwidth
The computation increase is small, It does not change the worse case of HEVC.

## Slide 14: Complexity
Complexity result shown in the table include both the proposed tool and the existing fixed upsampler.
No additional memory access.

## Slide 15: Cross-Check
Result are cross checked by Samsung, (cross check report JCTVC-M0250).

## Slide 16: Summary
Proposed a non-linear and content adaptive bilateral filtering process
Separable filter combined with upsampler
Lower complexity.
0.9/0.8/1.0% rate reductions are observed for AI/RA/LD_P 2X spatial scalability respectively, 0.2/0.0/0.3% rate reduction for AI/RA/LD_P 1.5x scalability.
Propose to adopt into SHM.