## Slide 1: Non-SCE1: Complexity reduction in intra prediction of enhancement layer in SHVC
Jun Xu and Cheung Auyeung
Sony Electronics Inc.

## Slide 2: Introduction
In SHM-1.0 software, intra prediction of enhancement layer reuses the filtering process of reference pixels and boundary samples from HEVC. In particular, when some conditions are met, filtering is applied to the followings:
  Reference pixels for some intra prediction modes and transform block sizes.
  Top row and left column of DC prediction.
  Top row of horizontal prediction.
  Left column of vertical prediction.
This contribution proposes to remove these filtering processes in the enhancement layer for intra prediction with the following results:
  Complexity reduction.
  -0.03% BDR for both AI 2x and AI 1.5x.

## Slide 3: Filtering in SHM-1.0 Intra Prediction
Some Intra
Prediction Modes
and
Transform Block Sizes
Mode Dependent Smoothing of Reference Samples
Luma DC
Prediction Block
Transform Size < 32
Filtering
Filtering
Luma Vertical
Prediction Block
Transform Size < 32
Filtering
Luma Horizontal
Prediction Block
Transform Size < 32
Filtering

## Slide 4: Propose to Remove Filtering
Some Intra
Prediction Modes
and some
Transform Block Sizes
Luma DC
Prediction Block
Transform Size < 32
Luma Vertical
Prediction Block
Transform Size < 32
Luma Horizontal
Prediction Block
Transform Size < 32

## Slide 5: Results with SHM1.0
SHM1.0 with proposed contributions
  Encoding was performed in a Microsoft HPC 64 bits computer cluster.
  Decoding was performed with a dedicated Windows 7 64 bits machine with two Intel Xeon X5365 CPUs (8 cores) in a single thread and no other application processes.
  Would like to thank TI for cross-checking in JCTVC-M0376.
 | AI HEVC 2x |  |  | AI HEVC 1.5x |  | 
 | Y | U | V | Y | U | V
Class A | 0.00% | -0.01% | -0.04% |  |  | 
Class B | -0.05% | -0.11% | -0.12% | -0.03% | -0.04% | -0.04%
Overall (Test vs Ref) | -0.03% | -0.08% | -0.09% | -0.03% | -0.04% | -0.04%
Overall (Test vs single layer) | 12.48% | 13.74% | 13.19% | 10.27% | 10.13% | 9.26%
EL only (Test vs Ref) | -0.09% | -0.14% | -0.15% | -0.07% | -0.08% | -0.08%
Enc Time[%] | 95.0% |  |  | 99.5% |  | 
Dec Time[%] | 94.4% |  |  | 100.3% |  | 
Enc Mem[%] | #DIV/0! |  |  | #NUM! |  | 
BL Match | Matched |  |  | Matched |  | 

## Slide 6: Results with SCE1 2.4+2.5
SCE 1 Category 2.4+2.5 with proposed contribution
  Removed filtering of reference pixels of intra prediction, filtering of horizontal and vertical intra prediction.
  Encoding was performed in a Microsoft HPC 64 bits computer cluster.
  Decoding was performed with a dedicated Windows 7 64 bits machine with two Intel Xeon X5365 CPUs (8 cores) in a single thread and no other application processes.
  Would like to thank LG for cross-checking in JCTVC-M0385.
 | AI HEVC 2x |  |  | AI HEVC 1.5x |  | 
 | Y | U | V | Y | U | V
Class A | -0.56% | -1.58% | -1.87% |  |  | 
Class B | -0.50% | -0.89% | -0.84% | -0.09% | -0.53% | -0.48%
Overall (Test vs Ref) | -0.52% | -1.09% | -1.14% | -0.09% | -0.53% | -0.48%
Overall (Test vs single layer) | 11.90% | 12.60% | 11.97% | 10.18% | 9.59% | 8.77%
EL only (Test vs Ref) | -0.29% | -0.90% | -0.96% | 0.45% | -0.08% | -0.02%
Enc Time[%] | 94.3% |  |  | 96.1% |  | 
Dec Time[%] | 101.6% |  |  | 104.6% |  | 
Enc Mem[%] | #NUM! |  |  | #NUM! |  | 
BL Match | Matched |  |  | Matched |  | 

## Slide 7: Conclusions
This contribution reduced the complexity in SHVC with negligible coding gain by removing the filtering process in the intra prediction processes of
  Reference samples
  DC, horizontal, and vertical prediction
Propose to be adopted to SHVC.