## Slide 1
Seung-Hwan Kim, Misra Kiran, Zhao Jie, Andrew Segall
JCTVC-R0232 “Non-SCCE3: High throughput palette coding ”

## Slide 2: Context coded bins for palette coding mode
Palette_run_type flag (context coded)
    0.98 context bin/pixel
Palette_run coding (1 context bin/pixel)
    Significance map (context coded)
    GR_1 flag map (context coded)
    GR_2 flag map (context coded)
    Remaining level (bypass coded)
Input level | # context bins | The number of pixels coded | Average context bins/pixel
0 | 1 | 1 | 1
1 | 2 | 2 | 1
2 | 3 | 3 | 1
3 | 3 | 4 | ¾ = 0.75
>3 | 3 | N | 3/N
palette_run_type_flag ==0 ?
Yes
Code “palette_index”
Palette_index==Palette_Size ?
Code
”palette_escape_value”
Yes
code
“palette_run”
Escape mode
Index mode
Code
“palette_run”
Copy_above_mode
No
No
Notes: 2

## Slide 3: JCTVC-R0232
Propose to limit the number of context coded bins for palette mode.
  Remove unnecessary context coded bins.
  Reduces the worst case number of context coded bins from 1.984375bins/pixel to 1.5625 bins/pixel
  No significant coding loss.
palette_run_type_flag ==0 ?
Yes
Code “palette_index”
Palette_index==Palette_Size ?
Code
”palette_escape_value”
Yes
code
“palette_run”
Escape mode
Index mode
Code
“palette_run”
Copy_above_mode
No
No
Notes: 3

## Slide 4: Proposed High Throughput palette coding
palette_run_type_flag ==0 ?
Yes
Code “palette_index”
Palette_index==Palette_Size ?
Code
”palette_escape_value”
Yes
Escape mode
Index mode
Copy_above_mode
No
No
“palette_run_b”
N > TH
Yes
“palette_run”
No
“palette_run_b”
N > TH
Yes
“palette_run”
No

## Slide 5: Throughput Comparison
1.98 bins/pixel
1.56 bins/pixel
1.56 bins/pixel
1.56 bins/pixel
Regular coding (non-palette mode)
Palette coding mode
Notes: 5

## Slide 6: Result (Lossy Full IBC)
 | All Intra |  |  | Random Access |  |  | Low delay B |  | 
 | G/Y | B/U | R/V | G/Y | B/U | R/V | G/Y | B/U | R/V
RGB, text & grap. with mot.,1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0%
RGB, text & grap. with mot.,720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | -0.1% | 0.0% | 0.0%
RGB, mixed content, 1440p | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | -0.1% | 0.0% | 0.1%
RGB, mixed content, 1080p | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | -0.2% | -0.2% | -0.3%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, text & grap. with mot., 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, text & grap. with mot.,720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 0.1% | 0.0% | 0.1%
YUV, mixed content, 1440p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | -0.2% | 0.1% | 0.1%
YUV, mixed content, 1080p | 0.0% | 0.0% | 0.0% | 0.2% | 0.3% | 0.3% | -0.1% | -0.8% | -0.7%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 100% |  |  | 100% |  |  | 101% |  | 
Dec Time[%] | 100% |  |  | 100% |  |  | 103% |  | 

## Slide 7: Result (Lossy 2CTB IBC)
Results in lossless are almost 0.0%.
 | All Intra |  |  | Random Access |  |  | Low delay B |  | 
 | G/Y | B/U | R/V | G/Y | B/U | R/V | G/Y | B/U | R/V
RGB, text & grap. with mot.,1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0%
RGB, text & grap. with mot.,720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.1% | 0.1%
RGB, mixed content, 1440p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 0.1% | 0.0%
RGB, mixed content, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.2% | -0.1% | 0.1%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, text & grap. with mot., 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, text & grap. with mot.,720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.2% | 0.1%
YUV, mixed content, 1440p | 0.0% | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 0.1% | -0.1%
YUV, mixed content, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.4% | -0.1%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 101% |  |  | 101% |  |  | 101% |  | 
Dec Time[%] | 102% |  |  | 101% |  |  | 103% |  |