## Slide 1: Parameter derivation for intra LM chroma prediction
J. Kim
JCTVC-J0160

## Slide 2: Introduction
Intra chroma prediction : IntraFormLuma
Chroma TU
: to be predicted
Luma TU
: reconstructed

## Slide 3: Introduction
The parameters are calculated every TU when chroma samples of the TU are predicted.
chroma reconstruction
for T0
Parameter
Calculation for T0
TU0
TU1
TU2
TU3
chroma reconstruction
for T1
Parameter
Calculation for T1
chroma reconstruction
for T2
Parameter
Calculation for T2
chroma reconstruction
for T3
Parameter
Calculation for T3

## Slide 4: Proposed Method
We propose that the parameters are calculated every CU and used for every TU in the entire CU
chroma reconstruction
for T0
Parameter
Calculation for CU
TU0
TU1
TU2
TU3
chroma reconstruction
for T1
chroma reconstruction
for T2
chroma reconstruction
for T3

## Slide 5
 | All Intra HE10 |  |  | Random Access HE10 |  |  | Low delay B HE10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | 0.0% | -2.3% | -2.4% | 0.0% | -2.2% | -1.7% |  |  | 
Class B | 0.0% | -0.6% | -0.4% | 0.0% | -0.5% | -0.3% | 0.0% | 0.1% | -0.3%
Class C | 0.0% | -0.3% | -0.4% | 0.0% | -0.2% | -0.2% | 0.0% | 0.0% | 0.0%
Class D | 0.0% | -0.1% | -0.2% | 0.0% | -0.1% | -0.1% | 0.0% | 0.6% | 0.1%
Class E | 0.0% | -0.3% | -0.2% |  |  |  | 0.0% | -0.6% | -1.3%
Overall | 0.0% | -0.7% | -0.7% | 0.0% | -0.7% | -0.6% | 0.0% | 0.1% | -0.3%
 | 0.0% | -0.7% | -0.7% | 0.0% | -0.7% | -0.6% | 0.0% | 0.1% | -0.3%
Class F | 0.0% | -0.4% | -0.2% | 0.0% | -0.2% | -0.2% | 0.1% | 0.7% | 0.7%
Enc Time[%] | #NUM! |  |  | #NUM! |  |  | #NUM! |  | 
Dec Time[%] | #NUM! |  |  | #NUM! |  |  | #NUM! |  | 
BD rate of CU based parameter calculation
Experimental Results

## Slide 6: Conclusion
We proposed CU based parameter calculation to reduce number of calculation.
It reduced number of calculation from 64 to 1 when CU size is 64x64 and TU size is 4x4
It also showed small gains since it used bigger test set when calculating parameters.

## Slide 7: Working Draft