## Slide 1: Non-TE5: Memory reduction for MV data of EL in SHVC
Jun Xu, Ali Tabatabai, Kazushi Sato, Shuo Lu
SONY

## Slide 2: Introduction
Motivation
  EL uses temporal MV for merge and MV prediction.
  Memory size is large even with MV compression because EL has large resolution.
  Inter-layer MV prediction can improve the coding efficiency significantly.
  A new trade-off can be achieved by manipulating available MV information across spatial, temporal and layer dimensions.

## Slide 3: Memory for MV in SHVC
EL
BL
Layer
POC
N
N+1
TMV
Current
MV
TMV
Current
MV
TMV
Current
MV
4:1 MV compression
TMV
Current
MV
ETRI’s postpone
SMuC sample solution
N-1
TMV: Temporal MV

## Slide 4: JCTVC-L0221
Memory reduction in EL
  Disable TMV for merge and MV prediction in EL but enable interlayer MV prediction.
  Inter-layer MV prediction will compensate the loss of disabling TMV in EL.
Pros
  Less memory usage.
Cons
  Slight BD performance drop.
Implemented based on ETRI’s proposal (TE5-5.2.3)

## Slide 5: JCTVC-L0221
EL
BL
Layer
POC
N
N+1
TMV
Current
MV
TMV
Current
MV
TMV
Current
MV
4:1 MV compression
TMV
Current
MV
N-1
TMV: Temporal MV

## Slide 6: Performance
Thanks to InterDigital for cross-checking
  0.3%~0.7% drop in performance
  Anchor is SMuC 0.1.1
Method | Test | Y-RA-2x | Y-RA-1.5x | Y-RA-SNR | Y-LDP-2x | Y-LDP-1.5x | Y-LDP-SNR
JCTVC-L0221 | Merge | -1.67 | -1.99 | -2.12 | -0.58 | -0.67 | -1.60
 | AMVP | -0.84 | -0.97 | -1.09 | -0.51 |  | 
 | Merge+AMVP | -1.92 | -2.20 | -2.32 | -0.86 | -0.91 | -1.78
5.2.3 K0037 (ETRI) | Merge | -2.20 | -2.30 | -2.42 | -1.24 | -1.20 | -1.95
 | AMVP | -1.55 | -1.52 | -1.60 | -0.97 | -0.83 | -1.08
 | Merge+AMVP | -2.36 | -2.46 | -2.57 | -1.31 | -1.26 | -2.03

## Slide 7: Conclusion
To save memory for MV, removing temporal MV from merge list and AMVP list of EL is proposed.
Performance trade-off is acceptable.
Establish CE or AHG on this topic.