## Slide 1: Depth Quadtree Prediction for HTM
JCT3V-B0068, Shanghai, October 2012
Joel Jung, Elie Mora – Orange Labs

## Slide 2: Introduction
  QuadTree limitation and predictive coding (QTL+PC) proposed in JCT-3V #1 meeting (JCT3V-A0044)
  Output:
    non-normative part (QTL) adopted (included in HTM4.1 software but disabled in CTC),
    normative part (QTL+PC) to be studied in CE3 (3 experiments).
  Basic principle of QTL+PC:
    Initial observation: it can be observed that “often” a given texture CU is more partitioned than its collocated depth CU: interesting assumption for efficient prediction
    Modification of the depth quadtree decoding process. For a given CTU, the quadtree of the depth is linked to the collocated CTU quadtree in the texture
    A given CU of the depth cannot be split more than its collocated CU in the texture.
    The quadtree of the depth is predictively encoded relatively to the quadtree of the texture.

## Slide 3: Predictive depth QT coding (1/2)
Experiment H1
Applies the proposed method on both Intra and Inter slices
Experiment H2
Applies the proposed method on Inter slices only.
Sending split flag for depth is useless when texture is not split.
Sending partition size for depth is useless when the texture is not split and its partition size is equal to 2Nx2N.

## Slide 4: Predictive Depth QT Coding (2/2)
Experiment H3
Is a simplification of experiment H2, with the following 2NxN and Nx2N partitions difference
2NxN and Nx2N partitions handling is the following:
Experiment H1 and H2: when the texture is split in 2NxN (resp Nx2N), depth allows 2NxN (resp Nx2N) partitioning and disallows Nx2N (resp 2NxN) partitioning and NxN partitioning.
Experiment H3: when the texture is split in 2NxN (or Nx2N), depth disallows 2NxN, Nx2N, and NxN partitioning.
Sending split flag for depth is useless when texture is not split.
Sending partition size for depth is useless when the texture is not split and its partition size is equal to 2Nx2N, Nx2N or 2NxN.

## Slide 5: Predictive Depth QT Encoding
Send nothing if the CU of the texture is not further split, and send one bit to indicate if depth is split or not when the current partition of the texture is further split.
H3 : The depth partition size is also not be sent if the texture is not split and its partition size is different than NxN.
Texture
Depth
Saves bits for QT signaling
DepthLevel | 0 | 1 | 2 | 2 | 2 | 3 | 3 | 3 | 3 | 2 | 1 | 1 | 1 | 2 | 2 | 2 | 2
TextureSplitFlag | 1 | 1 | 0 | 0 | 1 | - | - | - | - | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
TexturePartSize | - | - | 0 | 0 | - | 0 | 0 | 0 | 0 | 1 | 2 | 0 | - | 0 | 0 | 0 | 0
DepthSplitFlag | 1 | 1 | 0 | 0 | 0 |  |  |  |  | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
DepthPartSize | - | - | 0 | 0 | 0 |  |  |  |  | 0 | 0 | 0 | - | 0 | 0 | 0 | 0
ResidualDepthSplitFlag | 1 | 1 | - | - | 0 |  |  |  |  | - | - | - | 1 | - | - | - | -
ResidualDepthPartSize | - | - | - | - | 0 |  |  |  |  | - | - | - | - | - | - | - | -

## Slide 6: Parsing Dependency
For H3:
  Depth split flag is not parsed if corresponding texture split flag = 0
  Depth partition size is not parsed if corresponding texture partition size is different than SIZE_NxN
Consequently:
  The quadtree syntax elements of the texture need to be stored by the decoder until the corresponding depth is parsed
  Parallel parsing is not possible
Remark:
  Not a concern for robustness, because if texture is lost, we do not need corresponding depth anyways.

## Slide 7: Experimental Results
 | video 0 | video 1 | video 2 | video only | synthesized only | coded & synthesized | enc time | dec time | ren time
Poznan_Hall2 | 0,0% | 0,0% | 0,0% | 0,0% | 1,0% | 0,1% | 69,1% | 99,7% | 94,5%
Poznan_Street | 0,0% | 0,0% | 0,0% | 0,0% | 0,6% | -0,1% | 68,4% | 99,3% | 97,3%
Dancer | 0,0% | 0,0% | 0,0% | 0,0% | 1,6% | 0,3% | 65,6% | 101,0% | 104,6%
GhostTownFly | 0,0% | 0,0% | 0,0% | 0,0% | -0,1% | -0,6% | 68,8% | 102,3% | 112,2%
Kendo | 0,0% | 0,0% | 0,0% | 0,0% | 0,0% | -0,8% | 68,8% | 99,9% | 96,1%
Balloons | 0,0% | 0,0% | 0,0% | 0,0% | -0,1% | -0,4% | 67,3% | 97,5% | 90,9%
Newspaper | 0,0% | 0,0% | 0,0% | 0,0% | -0,1% | -0,4% | 66,5% | 104,3% | 102,4%
1024x768 | 0,0% | 0,0% | 0,0% | 0,0% | 1,0% | 0,1% | 67,7% | 100,0% | 98,7%
1920x1088 | 0,0% | 0,0% | 0,0% | 0,0% | -0,1% | -0,6% | 67,9% | 101,0% | 100,1%
Average | 0,0% | 0,0% | 0,0% | 0,0% | 0,4% | -0,3% | 67,8% | 100,5% | 99,5%
Proposed method: QTL + PC vs HTM4.1, CTC
3 views test case
(negative values are gains)
QTL + PC brings gain and encoder runtime saving

## Slide 8: Experimental Results
 | video 0 | video 1 | video 2 | video only | synthesized only | coded & synthesized | enc time | dec time | ren time
Poznan_Hall2 | 0,0% | 0,0% | 0,0% | 0,0% | 1,3% | 0,4% | 73,3% | 102,9% | 105,9%
Poznan_Street | 0,0% | 0,0% | 0,0% | 0,0% | 0,9% | 0,2% | 66,8% | 101,2% | 104,1%
Dancer | 0,0% | 0,0% | 0,0% | 0,0% | 2,0% | 0,7% | 69,2% | 102,7% | 120,0%
GhostTownFly | 0,0% | 0,0% | 0,0% | 0,0% | 0,0% | -0,4% | 75,2% | 99,6% | 96,4%
Kendo | 0,0% | 0,0% | 0,0% | 0,0% | 0,6% | -0,3% | 67,8% | 100,7% | 99,4%
Balloons | 0,0% | 0,0% | 0,0% | 0,0% | 0,2% | -0,2% | 73,0% | 100,3% | 100,2%
Newspaper | 0,0% | 0,0% | 0,0% | 0,0% | 0,2% | -0,2% | 74,1% | 107,8% | 101,1%
1024x768 | 0,0% | 0,0% | 0,0% | 0,0% | 1,4% | 0,4% | 69,7% | 102,3% | 109,8%
1920x1088 | 0,0% | 0,0% | 0,0% | 0,0% | 0,3% | -0,3% | 72,5% | 102,0% | 99,3%
Average | 0,0% | 0,0% | 0,0% | 0,0% | 0,7% | 0,0% | 71,3% | 102,1% | 103,6%
QTL only vs HTM4.1, CTC
3 views test case
(negative values are gains)
QTL brings runtime savings

## Slide 9: Results Summary
 | video 0 | video 1 | video 2 | video only | synthesized only | coded & synthesized | enc time | dec time | ren time
Poznan_Hall2 | 0,0% | 0,0% | 0,0% | 0,0% | -0,3% | -0,3% | 94,3% | 96,9% | 89,3%
Poznan_Street | 0,0% | 0,0% | 0,0% | 0,0% | -0,3% | -0,3% | 102,4% | 98,1% | 93,5%
Dancer | 0,0% | 0,0% | 0,0% | 0,0% | -0,4% | -0,4% | 94,8% | 98,3% | 87,1%
GhostTownFly | 0,0% | 0,0% | 0,0% | 0,0% | -0,2% | -0,2% | 91,5% | 102,7% | 116,3%
Kendo | 0,0% | 0,0% | 0,0% | 0,0% | -0,6% | -0,6% | 101,5% | 99,1% | 96,7%
Balloons | 0,0% | 0,0% | 0,0% | 0,0% | -0,3% | -0,3% | 92,3% | 97,2% | 90,7%
Newspaper | 0,0% | 0,0% | 0,0% | 0,0% | -0,2% | -0,2% | 89,6% | 96,8% | 101,3%
1024x768 | 0,0% | 0,0% | 0,0% | 0,0% | -0,4% | -0,4% | 97,1% | 97,8% | 89,9%
1920x1088 | 0,0% | 0,0% | 0,0% | 0,0% | -0,3% | -0,3% | 93,6% | 98,9% | 100,8%
Average | 0,0% | 0,0% | 0,0% | 0,0% | -0,3% | -0,3% | 95,1% | 98,4% | 96,0%
QTL + PC vs QTL only
3 views test case
(negative values are gains)
Consistent results
PC part brings BD rate gains, without runtime increase

## Slide 10: Conclusion
A modification of the depth quadtree decoding process is proposed.
For a given CTU, the quadtree of the depth is linked to the collocated CTU quadtree in the texture, so that a given CU of the depth cannot be split more than its collocated CU in the texture.
The quadtree of the depth is predictively encoded.
68% encoder runtime is achieved compared to the reference with BDR gains of 0.3% for coded + synthesized.
36.5% encoder runtime is achieved for just the depth component
Propose this method for adoption in the HTM and in the WD.
Thanks to Intel, Panasonic and Samsung
for the cross-check

## Slide 12: Analysis: Where do the gains come from?
CTB |  | Texture | 
 |  | Homogeneous 64x64 | Textured/Edge 8x8
Depth | Homogeneous 64x64 | Runtime savings (frequent) | No impact (frequent)
 | Textured/Edge 8x8 | Quality Loss + Bits savings (not a frequent case) | Bits savings for Depth QT
  - Savings relatively to the respective partitioning of Texture and Depth:
  - Method can smooth wrong depths edges (ex: Kendo)